## Slide 1: AMP link access
Date: 2024-03-10
Authors:

## Slide 2: Abstract
Three modes of the AMP link access is presented and discussed.

## Slide 3: Three modes of access
# | Access Mode
1 | - Random access of multiple AMP STA - no RX (no Trigger frame) - AMP STA transmits broadcast addressed frame
2 | - Random access of multiple AMP STA - AMP STA receives groupcast addressed Trigger frame - AMP STA responds with unicast addressed frame
3 | - Access of single AMP STA. AMP STA receives unicast addressed Trigger frame - AMP STA responds with unicast addressed frame

## Slide 4: Exemplary frame exchange (access mode 1)
Mode | Trigger frame | Duration and Number of slots | Response frame |  | Comment
 |  |  | RA | TA | 
1 | Does not present | Preset out or the frame | N/A (broadcast) | N/A (broadcast) | There might not be RA and TA in the frame format
AMP-STA
Protection
CTS to self
AMP AP STA
…
Response frame
Frame control
RA
TA
…
Slots (Si)
…
…
…
AMP AP STA
Energizing
The energizing ends at this point if it is supplied in the same channel as the CTS-to-self.

## Slide 5: Exemplary frame exchange (access mode 2)
Mode | Trigger frame |  |  |  | Response frame |  | Comment
 | Y/N | RA | TA | Duration and Number of slots | RA | TA | 
2 | Y | Broadcast/groupcast | unicast | >=1 | unicast | N/A | There might not be RA in the Trigger frame format
Response frame
AMP-STA
Trigger frame
Frame control
…
RA
TA
Duration and Number of slots
…
CTS to self
Frame control
RA
TA
…
AMP AP STA
Protection
Slot (Si)
…
…
…

## Slide 6: Exemplary frame exchange (access mode 3)
Mode | Trigger frame |  |  |  | Response frame |  | Comment
 | Y/N | RA | TA | Number of slots | RA | TA | 
3 | Y | unicast | unicast | 1 | unicast | unicast | 
Response frame
AMP-STA
Trigger frame
Frame control
…
RA
TA
Duration and Number of slots
…
CTS to self
Frame control
RA
TA
…
AMP AP STA
Protection
Slot
…

## Slide 7: Three modes of access - comparison
[begin placing presentation body text here]
# | Mode | AMP STA | AMP AP STA | Basic functionality | Comments
1 | Access of multiple AMP STA. Broadcast TX, no RX. Keeps AMP STA incognito | TX Broadcast frame during one of the preset access slots upon reaching the Energy threshold. The number and size of the access slots are set by default. | TX energy signals | No association/pairing, no individual addressing AMP STA – no RX | AMP AP STA transmits CTS_to_self frame at 2.4 GHz and a power signal simultaneously/sequentially, respecting 2.4 channel access rules. The protection set by CTS_to_self frame should cover the energy signal and the access slots
2 | Access of multiple AMP STA. Unicast TX, Broadcast RX. Keeps AMP STA incognito | TX Unicast frame during one of the access slots when it is initiated by AMP AP STA. The number and size of the access slots can be set in the Trigger frame | TX energy signals TX broadcast trigger frames at 2.4 GHz The number and size of access slots can be determined by the trigger frame. | No association/pairing, no individual addressing. AMP AP STA broadcasts triggers. AMP STA responds with unicast frames to AMP AP STA | AMP AP STA transmits trigger frame at 2.4 GHz also respecting 2.4 channel access rules. Using multicast addresses instead of broadcasting requires prior configuration in AMP AP STA.
3 | Access of single AMP STA. Unicast TX, Unicast RX AMP STA does not save incognito | TX Unicast frame following the Trigger frame when it is initiated by AMP AP STA. | TX energy signals TX unicast trigger frames at 2.4 GHz | Association/pairing, individual addressing. AMP AP STA TX unicast triggers AMP STA. The AMP STA responds with unicast frames to AMP AP STA | AMP AP STA transmits trigger frame at 2.4 GHz also respecting 2.4 channel access rules. Point to point protection is achievable

## Slide 8: Cons and Pros of different modes of Link Access
# | Separation of energizing and communication in the bridges/AP is allowed | Pros | Cons
1 | No, an energy signal must be issued by an AMP AP STA simultaneously or sequentially with a CTS_ to_self frame, thus an AMP STA transmission initiated by an energy signal is protected by a CTS_ to_self frame | - No RX - AMP AP STA triggers multiple AMP STAs in a single access, thereby reducing the number of channel accesses per AMP AP STA. - Through response broadcasting, multiple AMP AP STAs deliver the response frame of the same AMP STAs to upper layers of the network. This may enable some applications. - Keeps incognito of the AMP STA | - No way to communicate with the AMP STA - Creates excessive link load due to multiple AMP AP STAs forwarding frames sent by AMP STAs - No information of link level delivery success - No link integrity
2 | Yes, if the AMP STA is able waking up at the Trigger frame | - AMP AP STA triggers multiple AMP STAs in a single access, thereby reducing the number of channel of channel accesses per AMP AP STA. - Keeps incognito of the AMP STA | - No link between AMP STA and AMP AP STA - No information of link level delivery success - No link integrity
3 | Yes, if the AMP STA is able waking up at the Trigger frame | - Regular link level reliability is achievable - Regular link level integrity is achievable | - AMP AP STA shall trigger each AMP STAs in a separate access, thereby increasing the number of channel accesses per AMP AP STA - Does not keep incognito of the AMP STA

## Slide 9: Conclusion
For AMP, three link access modes have been proposed and analyzed, which may be suitable depending on:
method of energy supply (RF, solar energy …)
application and associated operating conditions: density, frequency of accesses, movability, lifespan, accessibility for maintenance, etc.
We recommend further investigation into the presented approaches as potential solution for the specification

## Slide 10: References
11-23-0774-00-0amp-wur-applicability-for-amp-downlink
11-24-0047-01-0amp AMP Station operation states