## Slide 1: Low Power and Long-Range Preamble Follow Up
Apr 2024
Authors:
Name | Affiliation | Phone | email
Brian Hart | Cisco Systems |  | brianh@cisco.com
Malcolm Smith | Cisco Systems |  | 
Juan Carlos Zuniga | Cisco Systems |  | 
Stephen Orr | Cisco Systems |  | 
Jerome Henry | Cisco Systems |  | 

## Slide 2: A Low Power Listening Mode was proposed in 22/1414 and 22/1841 …
Client only has its lower-power mode radio awake (low MCS-capable, 1SS)
RTS/Trigger indicates the recipient and lists many PHY parameters (NSS, bandwidth, MCS)
Based on RTS/Trigger, client can wake up and tune the resources needed for its high-power radio
The initial frame provides flexibility for implementation on the listening operation.
Different implementations can choose their preferred alternative to leverage the initial frame and trade off.

## Slide 3: … yet this seems inefficient and motivates the study of alternatives
This is a RTS/Trigger frame sent before transmitting on the downlink
The NSS, MCS and BW fields are already signaled in the preamble of the main PPDU – so this is sending SIG info duplicates – is there a more efficient option that allows for just CTS2self, or no MAC protection at all?
For context:
  Signalable eMLSR transition delays are 0/16/32/64/128/256 usec
  CTS2self at non-HT/MCS0 is 60 usec
  RTS + SIFS + CTS + SIFS at non-HT/MCS0 is 128 usec long; then “UHR-SIG” info adds a further N*4 usec.
Accordingly, [1] proposed a preamble extension field between the UHR SIG and UHR STF field
LSTF
LLTF
LSIG
R-LSIG
USIG
UHR SIG
Preamble Extension
UHR STF
UHR LTF
Data
PE
Padding used to wake up hi-capability RX
Single copy of SIG parameters
Hi-capability receiver finishes processing the PPDU
Lo-capability receiver initially processes the PPDU
Signaling of Preamble Extension field duration
Alternative location for Preamble Extension

## Slide 4: Comment on [1]: What if the client’s low power radio can only receive 20 MHz wide signals, since this is too narrow for the UHRSIG?
What if the client’s low power radio is only 20 MHz wide, since this is too narrow for the UHRSIG?
  EHT SIG (and UHR SIG?) have two content channels. In some 80 MHz static puncturing scenarios, receiving both CCs requires 80 MHz reception
  The CCs of EHT SIG (and UHR SIG?) can differ between 80 MHz frequency subblocks, so actually 160/320 MHz reception could be required
See updated proposed in the next slides

## Slide 5: Updated Proposal for Low Power and, optionally, Long Range Preamble
PreExtA (Preamble Extension A) field is inserted between USIG and UHRSIG
PreExtB (Preamble Extension B) field is inserted between UHRSIG and UHRSTF
The recipient reports the minimum required duration of a) PreExtA and b) PreExtA+PreExtB
An indication of the duration of the PreExt1 and PreExt2 fields is provided in an earlier field (e.g., USIG and UHRSIG field respectively)
LSTF
LLTF
LSIG
R-LSIG
USIG
UHR SIG
PreExtB
UHR STF
UHR LTF
Data
PE
Single copy of SIG params
Hi-capability (multiple SS, wideband) RX processes the UHR modulated field of the PPDU
Lo-capability (1SS, 20 MHz) RX processes the initial preamble
Signaling of PreExtA field duration
PreExtA
Signaling of PreExtB field duration (USIG/UHRSIG)
Single copy of SIG params
Mid-capability (1SS, wideband) RX processes UHR-SIG

## Slide 6: Contents of PreExtA and PreExtB
Three natural options for the PreExtA contents:
  Repeated USIG
    Simplest and most natural
    Also enables longer range if the hi-capability receiver is always active
  Repeated UHR SIG
  Some mix of these options
Three natural options for the PreExtB contents:
  Extended UHR STF
    Simplest
  Repeated UHR SIG
    Also enables longer range if the hi-capability receiver is always active
  Some mix of these options
LSTF
LLTF
LSIG
R-LSIG
USIG
UHR SIG
PreExtB
UHR STF
UHR LTF
Data
PE
PreExtA
Extended UHRSTF
R-USIG
R-UHRSIG
R-UHRSIG

## Slide 7: Summary
We propose a modified preamble with two additional preamble extension fields to support power savings
Especially when a mid-capability and hi-capability receiver can be woken up relatively quickly, the extended preamble provides greater efficiency than RTS/Trigger + CTS frames sent before transmitting data on the downlink
When the preamble is extended via a repeated U-SIG and repeated UHR-SIG, and when the hi-capability receiver is always active, then the preamble can also provide for long range operation.
  Synergistic with DL DRU and SU UL DRU

## Slide 8: Strawpoll
Do you agree to add the following text to the 11bn SFD:
  11bn shall define a preamble that supports low power operation via early reporting of bandwidth, MCS and number of spatial streams.
  Note: TBD if this replaces/complements an RTS/Trigger frame that carries bandwidth, MCS and number of spatial streams information.
Y / N / A

## Slide 9: References
[1] 23/1100, “Low Power and Long Range Preamble”, Brian Hart (Cisco Systems)