## Slide 1: AP Coordination Listening Instances
Date: 2024-03-11
Authors:

## Slide 2: Problem
11bn is considering add different Coordinated AP (C-AP) schemes to improve the tail performance.
  C-AP schemes include: C-TDMA, C-SR, etc.
C-AP schemes assume that one AP can receive frames from another AP
  However, APs can generally be locked in communications with their clients (e.g., if APs are not in ED range), and may miss C-AP related frames from neighboring APs
This calls for instances at which APs can listen to each other, to effectively exchange frames useful for specific coordinated AP schemes
  The proposed scheme does not preclude coordinated AP frame exchanges outside of these instances. However, introduction of AP coordination listen instances will improve efficiency

## Slide 3: Solution
Introduce C-AP listening time instances at which APs can effectively communicate with each other
An AP can announce the time instances at which intends to use coordinated AP schemes
  Announcements can be provided via beacon or other longer-term signaling
  It is assumed that APs can hear each other every once in a while
  The time-granularity of the coordinated time instances (content of the announcement) is smaller than that of its container
An AP can monitor announcements for C-AP listening time instances and be in the listen mode at the said time instances

## Slide 4
Beacon
AP1
AP2
Coordinated AP scheme
Coordinated AP scheme
Coordinated AP scheme
Coordinated AP scheme
Listening instance
Listening instance
Listening instance
Listening instance
An AP receiving the set of time-instances for coordination can enter the listening state at such times for effective exchange of coordination frames with the announcing AP

## Slide 5: Thank You