## Slide 1: Dynamic Channel Switch Operation
Date: 2024-01-10
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: Dynamic Channel Switch
STAs can dynamically switch to secondary channels per associated AP’s request for the frame exchanges per TXOP.
  The AP notifies a STA the secondary channels where the STA will park within the TXOP.

## Slide 3: Soliciting Control Frame and STA’s Parking Channel
We agree to use Trigger frame, e.g. MU-RTS, BSRP/BQRP, as the initiating frame to initiate STAs’ channel switch.
Each STA that supports dynamic channel switch announces the padding time for STA’s switch from primary channel to the secondary channel.
The RU (RU) being allocated to a STA in the initiating frame that triggers the STA’s dynamic channel switch decides the STA’s parking secondary channel(s).
  Example 1: in a 160MHz BSS, if a 20MHz STA acquires a 26-tone RU in 8th secondary channel in a frame exchange that trigger STA’s dynamic channel switch in a TXOP, the STA parks in 8th secondary channel in the TXOP.
  Example 2: in a 160MHz BSS, if a STA with 40MHz operating BW acquires a 52-tone RU in 5th secondary channel in a frame exchange that trigger STA’s dynamic channel switch in a TXOP, the STA parks in 5th + 6th secondary channels in the TXOP.
  Example 3: in a 160MHz BSS, if a STA with 80MHz operating BW acquires a 52-tone RU in 5th secondary channel in a frame exchange that trigger STA’s dynamic channel switch in a TXOP, the STA parks in 5th + 6th + 7th + 8th secondary channels in the TXOP.
  Example 4: in a 80MHz BSS, if a 20MHz STA with acquires a 52-tone RU in 3rd secondary channel in a frame exchange that trigger STA’s dynamic channel switch in a TXOP, the STA parks in 3rd secondary channels in the TXOP.

## Slide 4: Frame Exchanges and Switching Back to Primary Channel
It is not allowed to have a frame exchange that no TXOP responder is solicited in primary channel.
At the end of the TXOP, a STA as the TXOP responder that switched to the secondary channel and is not EMLSR/EMLMR STA switches back to the primary channel.
  Another variant is to follow eMLSR’s conditions to switch back to listening mode.
if an EMLSR/EMLMR STA detects a failed frame exchange or received a frame that is not addressed to the STA (eMLSR’s conditions to switch back to listening mode), the STA switch back to the primary channel.

## Slide 5: NAV Timer with BW Information
Per the baseline rules, if the Basic NAV Timer is not 0, the TXOP responder can’t transmit the responding frame although TXOP responder switch to the secondary channels that are idle.
One improvement could be that a STA can maintain its Basic NAV timer with BW information.
  If the switched secondary channels of a STA are not covered by the BW of the STA’s non-zero basic NAV timer and the PHY CCA within SIFS before transmitting the responding frame indicates the medium idle of the switched secondary channels, the STA can transmit the responding frame.
Basic NAV Timer operation:
  If a received OBSS PPDU BW is wider than the NAV timer, the BW of the basic NAV timer is set to the BW of the received OBSS PPDU.
  If the received OBSS frame or OBSS PPDU indicates a TXOP duration that is longer than the value of the basic NAV timer at the end of the received OBSS PPDU, the NAV timer is set to the Duration in received OBSS frame or the PHY header of the received OBSS PPDU at the end of the received PPDU.

## Slide 6: Dynamic Channel Puncture vs Dynamic Channel Switch
When a STA switches to a group of secondary channels and one of them is dynamically punctured, the STA may miss the PPDU addressed to it since the STA use the punctured channel to start the PPDU decoding.
  a STA with 20MHz operating BW switches to a secondary channel has no such issue.
    Once the secondary channel that a 20MHz STA switch to dynamically is punctured in a frame exchange, the STA will not be scheduled in the frame exchange.
Solution:
  Option 1:
    In a TXOP, it is ok to do dynamic channel puncture for the frame exchange (e.g. BSRP Trigger + QoS Null) that solicits the STAs to do dynamic channel switch.
    In the following frame exchanges of the TXOP, the further channel puncture is not allowed.
      A variant to this is that the secondary channels on which no STAs switch dynamically can be punctured.

## Slide 7: Dynamic Channel Puncture vs Dynamic Channel Switch
Solution:
  Option 2:
    An AP announces the subchannels of its BSS where a subchannel include multiple 20MHz channels (primary channel and/or secondary channels).
    Each subchannel without primary channel has an anchor channel that is never punctured.
    In a TXOP, it is ok to do dynamic channel puncture for the secondary channels other than anchor channel(s) for the frame exchange (e.g. BSRP Trigger + QoS Null) that solicits the STAs to do dynamic channel switch.
    In the following frame exchanges of the TXOP, the further channel puncture is allowed for the secondary channels other than anchor channel(s).
  Option 3:
    The dynamic channel puncture is not allowed in the frame exchanges with STAs switching to secondary channels.

## Slide 8: Initiating Control Frame for Dynamic Channel Switch
BSRP/BQRP Trigger + QoS Null provide less protection since the responding QoS Null is carried in UHR TB PPDU.
In dynamic channel switch operation, some responding STAs may switch to secondary channels to transmit CTS frames while one or multiple STAs transmit CTS frame(s) in non-HT duplicate PPDU(s) that covers the primary channel.
  If no STAs transmits CTS frame(s) in non-HT duplicate PPDU(s) that covers the primary channel while the STAs switched to secondary channels transmit CTS, the AP may assume the failed MU-RTS + CTS frame exchange
    the OBSS STAs/APs that receive CTS in secondary channel assume the medium busy.
    One exception is that if the AP can do the parallel PHY header decoding or channel combination, the AP can detect CTS in secondary channels although the primary channel has no responding CTS.
Primary 20MHz channel
BSS operating channel
MU-RTS
Request STA2,3 to switch to secondary 80MHz channel
while STA0, 1 stay in primary 80MHz channel.
CTS
STA0, 1 detect medium busy
TXOP per Duration field
TXOP per Duration field

## Slide 9: MU-RTS/CTS with Help of STA’s CF-End
When a STA that switches to a secondary channel per the initiating MU-RTS and transmits CTS doesn’t receive the following PPDU from the AP after SIFS + one time slot or another defined IFS, the STA can transmit CF-End to let its neighbor STAs/APs to reset their NAV timers.
If a STA switched to the secondary channels transmits the CF-End, the non-HT duplicate PPDU to carry the CF-End has the same BW as the solicited CTS of the STA.
The multiple STAs may transmit CF-End at the same secondary channel.
  The same data rate (defined by the spec, e.g. 6Mbps), scramble initial value (e.g. the scramble initial value of MU-RTS) need to be used by all the STAs that transmits CF-End.
Primary 20MHz channel
BSS operating channel
MU-RTS
Request STA2,3 to switch to secondary 80MHz channel
while STA0, 1 stay in primary 80MHz channel.
CTS
STA2, 3 can’t detect the PPDU from the AP
TXOP per Duration field
TXOP per Duration field
CF-End

## Slide 10: MU-RTS/CTS with Help of AP’s Additional PPDU Decoding
An AP that transmits MU-RTS to solicit STAs’ dynamic channel switch needs to support either the parallel PHY header decoding or channel combination.
  This one is preferable.

## Slide 11: Summary
The dynamic channel switch is discussed in the presentation:
  Various Trigger frames are used to announce the dynamic channel switch.
  The switching delay at the beginning of the channel switch and the end of the frame exchanges on the switched channel are announced.
  The potential issues of various Trigger frame for dynamic channel switch are discussed.
  The NAV timer and dynamic channel puncture under DSO are discussed.
We prefer to reuse various Trigger frames for the dynamic channel switch.