## Slide 1: In-device Coexistence Follow Up: Control Frame
Date: 2024-03-06
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Yi-Ling Chao Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Dynamic Control Information for Various Purpose
In a TXOP, the TXOP holder can notify the BW, MCS, Nss that will be used by the TXOP responder within the TXOP for the enhanced power save (low-capacity mode listening to high-capacity mode for frame exchange).
  The TXOP responder can switch to the high-capacity mode from the low-capacity listening mode and stay in high-capacity mode until the end of the TXOP.
In a TXOP, the TXOP responder can notify the available BW, available time, unavailable time because of the in-device non-WiFi radio activity (for in-device radio coexistence).
  The available time and unavailable time have different responding time requirements.
A STA/AP may announce its available BW, available time, unavailable time because of the in-device non-WiFi radio activity without soliciting.
A STA and AP may negotiate the Tx/Rx parameters for the TXOP or SP.
The TXOP responder may notify the reason why the frames in A-MPDU are not received correctly so that the TXOP holder will not drop the Tx MCS wrongly.

## Slide 3: Various MAC Features under Dynamic Control Information Exchange
The EMLSR mode needs to be supported under enhanced power save, in-device radio coexistence.
The TXOP protection, dynamic BW negotiation needs to be supported under enhanced power save, in-device radio coexistence.
The MU operation needs to be supported under enhanced power save, in-device radio coexistence.
  One exception to this could be the Tx/Rx parameters negotiation.

## Slide 4: Support of Different Features
A STA/AP can announce whether it supports the enhanced power save feature, in-device coexistence feature, and per TXOP Tx/Rx parameter negotiation separately.

## Slide 5: Updated Control Frame
For the enhanced power save and in-device co-existence, the updated existing control frames are used as ICF (initial control frame) frames.
  One example of the updated control frames includes
    Trigger frame, e.g. MU-RTS, BSRP Trigger and the responding frame
      In one option, only MU-RTS, BSRP Trigger with some updating can be used. In another option, MU-RTS, BSRP Trigger, BQRP Trigger with some updating can be used. In third option, all Trigger frames can be used.
    BA
      multi-STA BA with some updating can be used.
        The updated multi-STA BA can be used to replace Ack if the information of power save and/or co-existence needs to be carried.
A STA can transmit MU-RTS for in-device coexistence and enhanced power save.
For the Tx/Rx parameter negotiation of the TXOP and SP, the new control subtype may be used to define the new control frame as ICF frame.

## Slide 6: Updated Control Frame
In Trigger frame, the various types of information for all the addressed STA(s) of the Trigger frame, e.g. unavailable time (start time and the time period when the transmitter is not available), is carried in one or multiple User Info fields with the specific AID value (e.g. 2006 or 2009) in AID12 field of the User Info field.
  Such User Info has the same length as the Special User Info field where the Trigger Dependent User Info if exists is reserved.
  A combination of control ID + Length + control content is used to carry one of the various types of the information. One or multiple control ID + Length + control content can be carried in the User Info field(s) with the specific AID value in AID12 field.
  Another variant is that the control bitmap and the following optional various information fields can be carried in the User Info field(s) with the specific AID value in AID12 field.
In Trigger frame, the information for a user (e.g. Tx/Rx parameters for the user in the TXOP) is carried in an additional User field following the User Info field for the User.
  The additional User field is another User Info field whose AID12 field has a specific value (AID 2005 as an example) or the User’s AID value.
  A combination of control ID + Length + control content is used to carry one of the various types of the information.
  Another variant for MU-RTS is that the reserved bits of the User Info field for a user is used to carry the information for the user.
One special case can be MU-RTS that has reserved bits in Common Info and User Info field.

## Slide 7: Separate Unavailable Time and Allowed TXOP Duration
The CTS solicited by MU-RTS with single recipient carry the allowed TXOP duration in the Duration field of CTS.
The QoS Null solicited by BSRP Trigger carries the allowed TXOP duration in the Duration field of CTS.
  One variant is that the HE Control in QoS Null is used to carry the unavailable time also.
  Multiple QoS Null frames with the different HE Control content can also be used.
The multi-STA BA is used to carry the unavailable time in the TXOP following MU-RTS+CTS frame exchange or BSRP+QoS Null frame exchange.
  The multi-STA BA is used to replace Ack or compressed BA if the unavailable time needs to be reported by the TXOP responder.

## Slide 8: ICF with New Control Subtype or Not
BSRP Trigger + QoS Null with HE Control to carry the negotiation information.
Updated BAR+BA for Tx/Rx parameter negotiation:
  The updated BAR + Multi-STA BA are used for Tx/Rx parameter negotiation of the TXOP or SP.
  The frame exchange of MU-RTS + CTS and the frame exchange of updated BAR + BA can be used in one TXOP.
    The BAR+BA as the first frame exchange can use 20MHz non-HT PPDU while the following frame exchange can have wider BW.

## Slide 9: ICF with New Control Subtype or Not
New control subtype of soliciting ICF and responding ICF for Tx/Rx parameter negotiation:
  The unicast soliciting ICF and responding ICF with the new control subtypes in the first frame exchange of a TXOP or SP are used for Tx/Rx parameter negotiation of the TXOP or SP.
    These frames are needed for enhanced power save feature + in-device coexistence feature.
  The ICF can do the TXOP protection where when the medium is busy at the TXOP responder, the TXOP responder will not respond with the ICF responding frame.
  The ICF can do the dynamic BW negotiation where the TXOP responder will respond with the ICF responding frame in the idle BW that includes the primary channel.
  Another variant is that the ICF is not used for TXOP protection and/or dynamic BW negotiation.
One potential issue with soliciting ICF and responding ICF for Tx/Rx parameter negotiation is that it is difficult to be used when one side is in EMLSR mode
  The solution could be to disable the Tx/Rx parameter negotiation when one side is in EMLSR mode.
A variant is that the updated MU-RTS + responding ICF with new control subtype.