## Slide 1: Considerations for Coordinated TDMA
Date: 04-08-2024
Authors:

## Slide 2: Abstract
In this contribution, we discuss the overall framework for coordinated TDMA and highlight some of the aspects related to this method of multi-AP coordination.

## Slide 3: Introduction
Coordinated TDMA (C-TDMA) has been discussed as one of the key multi-AP (MAP) coordination mechanisms for TGbn [1-3].
The TXOP sharing framework defined in 802.11be can extended for sharing TXOP between multiple APs.
The MU-RTS TXS trigger frame can be extended for TXOP allocation in this purpose.
In this contribution, we highlight some of the aspects of coordinated TDMA.

## Slide 4: Framework for Coordinated TDMA
Coordinated TDMA and any other multi-AP coordination should accommodate both the enterprise and non-enterprise (e.g. residential use cases) deployment scenarios.
  The framework should be general enough that two APs from different vendors can also participate in multi-AP coordination and benefit from it.
Accordingly, for the coordinated TDMA, procedures for discovery and negotiation need to be integrated into the overall framework.
  This would enable setting up the terms for coordination among the participating APs
Overall C-TDMA flow

## Slide 5: C-TDMA Announcement and Negotiation
C-TDMA announcement: During this phase, the C-TDMA initiating AP can identify the other APs that are willing to participate in coordinated TDMA
  Basic capability and coordination information can be announced during this phase by the initiating AP.
  If a neighboring AP is willing and prepared to participate in the C-TDMA coordination, it can inform the C-TDMA initiating AP by responding to the announcement received from the TWT sharing AP.
  This phase essentially forms a C-TDMA coordination group.
C-TDMA Negotiation: During this phase, C-TDMA parameters for MAP coordination are decided among the participating APs.
  The C-TDMA initiating AP can send a coordination request to the other APs in the C-TDMA coordination group.
    The request will contain the set of parameters that the initiating AP intends to use for coordination.
  Upon receiving the request, the responding AP can either accept/reject the request or suggest an alternative set of C-TDMA parameters.
  Upon successful negotiation, a long-term C-TDMA agreement would be set up among the participating APs.

## Slide 6: SCS for C-TDMA
During the C-TDMA negotiation phase, the participating APs should indicate their resource need as part of the multi-AP coordination with C-TDMA
  This would set the long-term expectation on how often the TXOP sharing AP would need to trigger the participating shared APs and allocate the TXOPs
SCS/QoS Characteristics elements can be exchanged among the coordinating AP to indicate C-TDMA resource needs.

## Slide 7: Dynamic TXOP Request
The TXOP requirements for the APs participating in the C-TDMA may fluctuate around the expected requirements that are set during the C-TDMA negotiation phase.
There should be a mechanism for the APs to indicate to the TXOP sharing AP the updated C-TDMA resource requirements so that the TXOP sharing AP can appropriately allocate the TXOP.
  Alternatively, the TXOP sharing AP, before allocating the TXOP, may solicit such information from the other coordinating APs.
Sharing the BSR serves similar purposes for non-AP STAs receiving the TXOP from the associated AP.
  However, for C-TDMA, the TXOP received by the coordinating APs should also account for the portion of the time needed for triggering the non-AP STAs for uplink or P2P in the respective BSS.

## Slide 8: Multi-STA/Multi-AP TXOP Sharing
In 802.11be, the TXOP sharing process using the MU-RTS TXS trigger frame allows only one STAs to be triggered at a time for TXOP allocation.
This incurs recurrent overhead when the TXOP holder intends to allocate TXOPs to multiple STAs
In 802.11bn, for efficient operation, the group can consider to allocate TXOP to multiple STA or multiple APs using a single trigger frame
  The current MU-RTS TXS trigger frame already has the necessary format to allow such multi-STA/multi-AP allocation.
    TXOP recipient identifiers can be listed in the User Info field
  For 802.11bn, the spec change can be as simple as lifting the current restriction of “single user-only” TXOP allocation using the TXS frame.

## Slide 9: Alteration/Teardown of C-TDMA Agreement
An existing C-TDMA agreement between two coordinating APs may not be perpetual in nature.
There would be a need to modify an existing agreement
  Such modification is desirable when the load condition changes in one of the participating AP’s BSS. For example, when the load increases, more TXOP allocation would be desirable.
Modification of an existing agreement can be characterized by replacing the previous set of C-TDMA parameters with a new set of C-TDMA parameters.
  A time instant can be indicated when the new C-TDMA parameter sets can take effect.
Similarly, there needs to be a mechanism to tear down or opt out of an existing C-TDMA agreement

## Slide 10: Summary
802.11be TXOP sharing procedure can be extended to enable coordinated TDMA functionalities.
C-TDMA framework should accommodate both the enterprise and non-enterprise scenarios.
  Accordingly, C-TDMA agreement negotiation procedure among multiple APs should be supported
For C-TDMA, a procedure is needed to allow the participating APs to indicate resource needs to the other coordinating APs.
  Such indication can be on long-term and short term basis.
For efficient C-TDMA operation, triggering multiple STAs/APs using a single TXS trigger frame can be supported.

## Slide 11: Appendix

## Slide 12: Example: C-TDMA Announcement and Negotiation
  Figure: Example frame exchanges for C-TDMA announcement and negotiation. Assumes wireless MAP coordination. For managed networks, similar frame exchanges can happen through the central controller.

## Slide 13: References
[1] Yanjun Sun, et.al., IEEE 802.11-23/41r0, “Considerations on Coordinated TDMA”.
[2] Geonhwan Kim, et.al., IEEE 802.11-23/1085r0, “Thoughts on Coordinated TDMA”.
[3] Yanjun Sun, et.al., IEEE 802.11-23/739r1, “Follow-up on Coordinated TDMA (C-TDMA)”.

## Slide 14: Straw Poll-1
Do you agree to define a mechanism to allow an AP to share a portion of its obtained TXOP with one or more other APs/STAs?

## Slide 15: Straw Poll-2
For coordinated TDMA (C-TDMA), do you agree to define a mechanism that would allow the participating APs to discover each other and negotiate parameters for the C-TDMA agreement?

## Slide 16: Straw Poll-3
For coordinated TDMA (C-TDMA), do you agree to define a mechanism that would allow the participating APs to exchange information on the resource (TXOP) needs with other coordinating APs?
  Such resource needs can be on a long-term and/or short-term basis.

## Slide 17: Straw Poll-4
For coordinated TDMA (C-TDMA), do you agree to define a mechanism that would allow the coordinating APs to modify and/or teardown an existing C-TDMA agreement?