## Slide 1: SP-based Non-Primary Channel Access
Date: 2024-02-17
Authors:

## Slide 2: Motivation
To meet throughput and latency requirements mentioned in the UHR PAR [1], non-primary channel access (NPCA) was proposed as a potential method
Existing Techs: Many contributions [2] focus on TXOP-based NPCA
  To switch to a non-primary channel when OBSS TXOP is detected on the primary channel
  To switch back to the primary channel when OBSS TXOP on the primary channel ends
Reality: OBSSs often use the same primary channel, if the operating channels overlap
  Heavy traffic is anticipated during TWT SPs => Primary channel becomes very busy during an OBSS TWT SP
  Frequent switching is anticipated during OBSS TWT SPs
    Wherein durations on the primary channel might be too shattered to be used
=> SP-based NPCA is introduced

## Slide 3: Recap: TXOP-based NPCA
With a wider operating channel width and a denser network deployment, channel efficiency is low when only the primary channel access is used
  With only primary channel access, a STA has to do backoff for transmission if the primary channel is busy, even when non-primary channels are idle.
With TXOP-based NPCA, when the primary channel is occupied by an OBSS TXOP, STAs switch to a non-primary channel to contend for the channel, using idle non-primary channels to access the medium, and switch back to the primary channel when the OBSS TXOP ends.
OBSS TXOP
BSS TXOP
Primary
channel
Non-primary
channel
Switch to a non-primary channel
Switch back to the primary channel

## Slide 4: Concept: SP-based NPCA
With SP-based NPCA, a BSS switches to a non-primary channel to access the medium during an OBSS TWT SP and switches back when SP ends, because
  It is anticipated that there would be heavy traffic during the TWT SPs
  OBSSs with staggered parking channels reduce collisions
Non-primary channel | BSS parking |  | BSS parking | 
Primary channel | OBSS TWT SP | BSS parking | OBSS TWT SP | BSS parking
time
frequency
OBSS TWT SP
BSS parking
Primary
channel
Non-primary
channel

## Slide 5: Proposal
Negotiation Phase: AP and non-AP STAs negotiate parameters used in SP-based NPCA phase
  Parked non-primary channel, etc.
SP-based NPCA Phase: AP and non-AP STAs park on the non-primary channel during OBSS TWT SPs, and park on the primary channel outside OBSS TWT SPs
Primary
channel
Non-primary
channel
Negotiation
Negotiation Phase
AP announces OBSS TWT Info
SP-based NPCA Phase
OBSS TWT SP
BSS parks
OBSS TWT SP
BSS parks
…
Note: Not parked on the subchannel

## Slide 6: Detail 1. SP-based NPCA Phase
For each OBSS TWT Info detected by AP
  Step 1. AP announces an OBSS TWT Info
  Step 2. AP and non-AP STAs in a BSS, park on a non-primary channel instead of the primary channel only during OBSS TWT SPs
    AP and non-AP STAs in a BSS automatically switch to the non-primary channel when an SP starts and automatically switch back to the primary channel when an SP ends
AP announces OBSS TWT Info
Primary
channel
Non-primary
channel
BSS switches to a non-primary channel
Switches back to the primary channel
OBSS TWT SP
BSS parking
BSS parking
BSS parking

## Slide 7: Detail 1-1. AP’s Announcement of OBSS TWT
AP collects OBSS TWT Info via, e.g.,
  Listening to OBSS’s beacon, or
  Information exchange among multiple APs (Multi-AP co-operation)
OBSS TWT Info is announced/broadcasted by AP via, e.g.,
  Modified current TWT element, or
  Defined OBSS TWT element

## Slide 8: Discussions
Legacy STAs in BSS
  AP could explicitly notify legacy STAs, before switching to non-primary channel
Scaling: “Multiple BSSs are likely to switch to the same non-primary channel because of the same OBSS TWT”
  They should contend on the non-primary channel
ETSI regulation: “primary channel cannot be changed more than once per second”
  Primary channel is not changed while parking is changed

## Slide 9: Summary
The idea of SP-based NPCA is introduced: A BSS parks on a non-primary channel during OBSS TWT SPs
  AP and non-AP STAs in the BSS
    switch to the non-primary channel when an OBSS TWT SP starts, and
    switch back to the primary channel when the OBSS TWT SP ends

## Slide 10: Straw Poll
Do you support to include SP-based NPCA where a BSS parks on a non-primary channel during OBSS TWT SPs in 11bn SFD?

## Slide 11: References
[1] 11-23/0480r3, “UHR proposed PAR,” Laurent Cariou
[2] 11-23/2005r1, “Non-primary channel access (NPCA),” Minyoung Park