## Slide 1: Thoughts on Coordinated Spatial Reuse
Authors:
Name | Affiliations | Address | Phone | email
Sherief Helwa | Qualcomm |  |  | shelwa@qti.qualcomm.com
George Cherian |  |  |  | 
Abhishek Patil |  |  |  | 
Alfred Asterjadhi |  |  |  | 
Alice Chen |  |  |  | 
Sameer Vermani |  |  |  | 
Bin Tian |  |  |  | 
Date: 2024-03-11

## Slide 2: Objective
Background
  There are many contributions presented on Coordinated Spatial Reuse
  Most of the contributions assume TXOP based reuse, which adds significant overhead and complexity:
    Per-TXOP Interference measurement and signaling between TXOP sharing & Shared APs
    Last moment scheduling decision that the TXOP shared AP has to make, based on which clients TXOP sharing AP has scheduled
    Tx power backoff decision & MCS selection that the TXOP shared AP has to make, based on which clients TXOP sharing AP has scheduled
Objectives of this contribution
  Provide some thoughts on a simpler coordinated spatial reuse mechanism

## Slide 3: Design Goal
Goal of this proposal is to strike a balance between complexity and gains
In enterprise cases, large proportion of clients are mostly (semi)static.
  So, can we have coordinated SR, using a longer-term signaling?
    Say, multiple of Beacons through management frame signaling
  Avoid last moment signaling that requires complex scheduling decisions
Longer-term signaling can be achieved by leveraging the concept of Service Periods (SPs)
  SPs are announced much time ahead, hence not putting the APs under stringent time requirements for scheduling and interference estimation.

## Slide 4: Proposal Summary
Classify the clients as “inner” or “outer clients” (on a semi static basis)
  Inner clients are those clients that experience less interference from neighboring APs
Allow reuse at a Service Period basis level
  ‘Reuse Service periods’ for inner clients Vs ‘Orthogonal Service periods’ for outer clients
A Sharing AP use long term signaling to announce reuse criteria and the service periods
  Use longer term signaling (say, Beacon, or management frame)

## Slide 5: Some more details
Sharing AP pre-determines the “inner zone” clients, on a semi-static basis
  For example, the Sharing AP may determine inner/outer client based on its client’s reporting of Beacon power from neighboring APs that is measured periodically, (Or other means of inner/outer classification that AP may choose)
Sharing AP advertises Spatial Reuse parameters on a long-term basis
  Advertises “Reuse Service Periods” , “Max interference level” etc. that sharing AP can allow
Shared AP determines the candidate clients based on SP Sharing AP criteria
  Provides flexibility for shared AP to schedule its clients without getting last moment values on spatial reuse parameters

## Slide 6: Simulation Scenario
Gains are analyzed for different inter-AP distances in a 5-AP topology
  The AP under test is AP1 for which performance metrics are collected
  Reason: AP1 is a representative AP of a larger topology of a dense network
  BSS radius expands as inter-AP distances increase
Parameter | Assumption
EDCA | Medium access distributed evenly among APs
Scheduler | Round-robin [STA1 STA2 STA3 STA1 STA2 …]
Rate Adaptation | Ideal (Genie-aided PER estimate which maps to the best goodput in the rate table)
NSS | 2 (NSS2 RA table used)
Variable Tx Power | No power change with different MCS values
PL Model | TGn Path loss model (without wall loss)
Rate Calculation | Average across all possible locations within BSS area
S11
S12
S13
S14
S15
S21
S22
S23
S24
S25
S31
S32
S33
S34
S35
S41
S42
S43
S44
S45
S51
S52
S53
S54
S55
AP1
AP2
AP3
AP4
AP5

## Slide 7: Topology Details
Topology resembles a Reuse-1 scenario:
  Square BSS coverage areas assumed
  As inter-AP distances increase, each AP coverage area is extended to include in between STAs and have no gaps in between

## Slide 8: Simulation Results
Schemes compared:
  Baseline: APs share every SP if RSSI is below ED
  TDM: APs share the medium in a round-robin fashion
  CSR:
    Sharing AP decides to share SPs where it serves inner clients
    Shared APs decide to do simultaneous transmissions in shared SP to serve their inner clients if RSSI is below ED
Average throughput over all possible STA locations is calculated for the AP under study
Average throughput is calculated versus midpoint SNR calculated at the edge client between adjacent APs
Terminology:
  Midpoint SNR: Interference-free SNR at midpoint between two closest APs (𝑑/2 away from AP1).
  X-axis of the plot represented in terms of decreasing midpoint SNR (representing increasing AP-AP distance)

## Slide 9: Simulation Results
Rate CDF curves were generated for the AP under study to understand how throughput is spatially distributed within the BSS under study

## Slide 10: Simulation Results
Rate CDF curves were generated for the AP under study to understand how throughput is spatially distributed within the BSS under study

## Slide 11: Conclusion
A simplified, Service-Period based Coordinated Spatial Reuse mechanism is considered in this presentation
Significant complexity/overhead reduction can be achieved with this scheme.
Initial gain analysis show that, with proper optimization of how inner/outer STA classification is done, we can achieve significant throughput gains over baseline scheme
  Gain analysis for other scenarios in progress