## Slide 1: Data Forwarding within TXOP for XR Use Cases
Date: 2024-04-08
Name | Affiliations | Address | Phone | email
Seongho Byeon | Samsung Electronics |  |  | sh.byeon@samsung.com
Jack Jonghyo Lee |  |  |  | 
Jaheon Gu |  |  |  | 
Jinho Choi |  |  |  | 
Jonghoe Koo |  |  |  | 
Mingyu Lee |  |  |  | 
Taeyoung Ha |  |  |  | 
Youngwan So |  |  |  | 

## Slide 2: Introduction
Emerging XR use-cases
  Need to support low End-to-End (E2E) latency
  Encompassing the case where the two devices (i.e., remote device like VR glass and XR headset, and device for computation offloading such as laptop or smartphone) are connected through the same AP
    XR compute offloading over wireless links is a key capability to scale the adoption of XR devices [1]
    In such two-hop topology, sensing data or render data flows between two STAs via AP, requiring minimal control and contention overhead
STA A
STA B
AP

## Slide 3: Introduction
Emerging XR use-cases
  A proxy SCS mechanism is proposed to improve E2E QoS for the above use cases [2-4]
    Due to size, thermal, cost and power constraint, XR devices may leverage a different device for computation, however, the compute device may not have the latest Wi-Fi technology and cannot exercise advanced Wi-Fi features
    Introducing a new concept of procedure to set up the QoS, proxy SCS, between two devices within BSS, to enable the AP to deliver the proper E2E QoS for the traffic between STA A and STA B via the AP
   In this contribution, we would like to discuss the way of effectively supporting data forwarding between the two established STAs through proxy SCS or other QoS providing methods within TXOP

## Slide 4: Introduction
Various cases where data forwarding is actually needed in the local network
AP
Home Cloud Server
MR device
Smart Display
Laptop
Smart IoT Hub
Smartphone

## Slide 5: Problem Statement
Data forwarding within TXOP for low latency proxy traffic
  Method for using legacy protocols to effectively support data forwarding
    Normal EDCA
    After participating in contention, STA A(B) transmits data within its TXOP
    The AP also needs to win the contention, and then, transmits the corresponding data to STA B(A) depending on scheduling policy
      The time overhead required for transmission and reception is large, and the latency is dependent on the AP's scheduling policy
    Reverse Direction Grant (RDG)
    STA A(B) sends one piece of data to the AP, after initiating TXOP
    Then, the AP becomes TXOP holder and is able to continuously send data to STA B(A)
      After a single session of data forwarding, there is no way for STA A(B) to get the TXOP back in order to transmit the next data to STA B(A) via the AP, nor is there any guarantee that the AP will forward the data
      No large-scale industry adoption of RDG

## Slide 6: Problem Statement
Data forwarding within TXOP for low latency proxy traffic
  TXOP Sharing in IEEE 802.11 be
    Only the AP can share its TXOP using MU-RTS TXS Trigger Frame
      The latency is dependent on the AP's scheduling policy
      Large control overhead for frequent assigning and switching DL/UL for data forwarding
  TXOP optimization proposal [1]
    TXOP optimization method is proposed to improve overall QoS by reducing E2E latency, allowing any STA to share TXOP with minimal overhead for forwarding traffic to fit in TXOP
    TXOP sharing for forwarding to reduce contention latency for TXOP responder for co-related flow

## Slide 7: Data Forwarding within TXOP
Data forwarding (DF) supporting E2E QoS
  Assumptions
    C1. STA A and STA B are associated within the same BSS or the same multi-BSS
    C2. Both STA A and STA B may not hear each other
AP
STB A
STA B
QoS data A-MPDU 1
BA
QoS data A-MPDU 1
BA
TXOP
SIFS
SIFS
QoS data A-MPDU 2
SIFS
DF-ICF
SIFS
DF-RSP
SIFS
Example: STA B initiates TXOP and transfers frame(s) to STA A via the AP
Upon completing the forwarding of QoS Data n (including retransmission) within the TXOP, the TXOP is handed over back to STA B, automatically
DF-End
TXOP initiator informs other STAs that it finishes TXOP, if the remaining TXOP is not sufficient for the next QoS data transmission and forwarding
SIFS
…
…
…
BA
DF-End
SIFS
SIFS
DF-Fin
Since the time required for data forwarding cannot be accurately predicted, the TXOP might be set as long as possible within the range allowed by the AP (TBD)
SIFS
[NOTE] The specific type of control frames are TBD

## Slide 8: Conclusion
In this presentation, we propose a straightforward enhancement to the baseline TXOP sharing mechanism in order to facilitate two-hop data forwarding
This allows the AP to provide proper E2E QoS for low latency traffic between two STAs, particularly for emerging XR use-cases in the local network

## Slide 9: References
[1] 11-23/1387r1 TXOP sharing extensions for XR use-cases (Dibakar Das, Intel)
[2] 11-23/0073r0 Thoughts on Proxy SCS (Guagang Huang, Huawei)
[3] 11-23/1958r0 Proxy QoS management for XR use cases (Guoqing Li, Meta)
[4] 01-24/1885r1 End-to-end QoS with SCS (Duncan Ho, Qualcomm)