## Slide 1: Data Forwarding within TXOP for XR Use Cases
Date: 2024-04-08
Name | Affiliations | Address | Phone | email
Seongho Byeon | Samsung Electronics |  |  | sh.byeon@samsung.com
Jack Jonghyo Lee |  |  |  | 
Jaheon Gu |  |  |  | 
Jinho Choi |  |  |  | 
Jonghoe Koo |  |  |  | 
Jungjun Kim |  |  |  | 
Mingyu Lee |  |  |  | 
Taeyoung Ha |  |  |  | 
Youngwan So |  |  |  | 

## Slide 2: Introduction
Emerging XR use-cases
  Need to support low End-to-End (E2E) latency
  Encompassing the case where the two devices (i.e., remote device like VR glass or XR headset, and device for computation offloading such as laptop or smartphone) are connected through the same AP
    XR compute offloading over wireless links is a key capability to scale the adoption of XR devices [1]
    In such two-hop topology, sensing data or render data flows between two STAs via AP, requiring minimal control and contention overhead
      STA A and STB B may not hear each other
STA A
STA B
AP

## Slide 3: Introduction
Low E2E Latency Support for XR use-cases
  Additional QoS setup b/w two devices for lower latency support using stream classification service (SCS) in TGbn [2-4]
    Introducing a new concept of procedure to set up the QoS, proxy SCS, between two devices within BSS, to enable the AP to deliver the proper E2E QoS for the traffic between STA A and STA B via the AP
  As data is exchanged between the remote computer device and XR device through AP, both Wi-Fi links have great impact on the overall XR user experience
   In this contribution, we would like to discuss the way of effectively supporting data forwarding established between the two UHR STAs through proxy SCS or other QoS providing methods within a TXOP

## Slide 4: Introduction
Various cases where data forwarding is actually needed in the local network
  When home cloud server or storage like NAS is running in LAN, various types of data forwarding may be required between multiple computing devices and monitor devices

## Slide 5: Problem Statement
No existing direct data forwarding mechanism
  Legacy EDCA operation for the case:
    STA A(B) wins contention of the medium and sends UL data
    AP receives the data and keeps it in its transmit queue under the same QoS level
    AP wins contention, and sends the data to STA B(A)
    The time overhead required for transmission and reception is large, and the latency depends on the AP’s queue status
  Trigger-based operation:
    AP initiates a TXOP and sends Trigger frame to STA A(B)
    STA A(B) transmits the data to AP, that needs to be forwarded to STA B(A)
    AP then sends the data to STA B(A)
    AP acquires the TXOP for data forwarding on behalf of STAs, and the potential latency depends on the AP's scheduling policy

## Slide 6: Recap
TXOP optimization proposal [1]
  TXOP optimization method is proposed to improve overall QoS by reducing E2E latency, allowing any STA to share TXOP with minimal overhead for forwarding traffic to fit in TXOP
    TXOP sharing for forwarding to reduce contention latency for TXOP responder for co-related flow
  Thoughts for going further
    There is a need for a new protocol to ensure or guarantee that an associated AP transmits the data requiring forwarding within a shared TXOP
    It is necessary to quickly retrieve the shared TXOP after data forwarding so that the TXOP initiator can continue with the next data forwarding

## Slide 7: Data Forwarding within TXOP
Data forwarding (DF) supporting E2E QoS
  Assumptions
    A1. STA A and STA B are associated within the same BSS or the same multi-BSS
    A2. STA A and STA B may not hear each other
AP
STB A
STA B
QoS data A-MPDU 1
BA
QoS data A-MPDU 1
BA
TXOP
SIFS
SIFS
QoS data A-MPDU 2
SIFS
DF-ICF
SIFS
DF-ICR
SIFS
Example: STA B initiates TXOP and transfers frame(s) to STA A via the AP
Upon completing the forwarding of QoS Data (including retransmission) within the TXOP, the TXOP is handed over back to STA B, automatically
DF-End
TXOP initiator informs other STAs that it finishes TXOP, if the remaining TXOP is not sufficient for the next QoS data transmission and forwarding or no more data to be forwarded
SIFS
…
…
…
BA
DF-End
SIFS
SIFS
DF-Fin
Since the time required for data forwarding cannot be accurately predicted, the TXOP might be set as long as possible within the range allowed by the AP (TBD)
SIFS
[NOTE] The specific type of control frames are TBD

## Slide 8: Conclusion
In this presentation, we propose a straightforward enhancement to the baseline TXOP sharing mechanism in order to facilitate two-hop data forwarding
This allows the AP to provide proper E2E QoS for low latency traffic between two STAs for emerging XR use-cases in the local network
The proposed data forwarding mechanism can be adopted to various local network senarios

## Slide 9: References
[1] 11-23/1387r1 TXOP sharing extensions for XR use-cases (Dibakar Das, Intel)
[2] 11-23/0073r0 Thoughts on Proxy SCS (Guagang Huang, Huawei)
[3] 11-23/1958r0 Proxy QoS management for XR use cases (Guoqing Li, Meta)
[4] 01-24/1885r1 End-to-end QoS with SCS (Duncan Ho, Qualcomm)