## Slide 1: Timely Transmission of Low Latency Traffic with Reduced Preemption Occurance
Date: 2024-05-10
Authors:
Name | Affiliations | Address | Phone | email
Shirley Yin | Clourney Semiconductor |  |  | shy166@clourneysemi.com
Jerome Gu | Clourney Semiconductor |  |  | 
Jason Sheng | Clourney Semiconductor |  |  | 

## Slide 2: Introduction
“Enabling at least one mode of operation capable of improving the tail of the latency distribution and jitter compared to EHT MAC/PHY operation, with mobility between BSSs” is one of the objectives of 802.11bn[1].
In [2-6], the details of preemption mechanism are provided, nevertheless, how to guarantee the timely transmission of low latency traffic and user experience related to preemption is always an important problem.
Regarding this, a scheme to release Nss for low latency traffic in EMLMR operation is given in [7], however, it is limited to EMLMR only.
In this submission, we discuss the problem with a general solution, w.r.t the operating mode[8] and emerging capability mode [9].

## Slide 3: Recap
  Operating mode is supported in 11be[8].
  The operating mode may include BW, NSS, and maybe other settings/fields/elements
  The initiating STA may have different reasons for changing the Operating Mode of the responding STA
    For example the initiating STA has or will have certain changes (e.g., operating mode, network conditions or throughput/latency/QoS requirements) and requests the responding STA to change its operating mode (e.g., for better throughput, latency, QoS, etc.)
  The responding STA may have its own reasons to be running in certain operating mode and may accept or deny the Operating Mode Request.
A Motion on Capability mode was approved[9]
  TGbn defines a power save mode for a STA that is a UHR Mobile AP or a UHR non-AP STA wherein the STA may transition from a lower capability mode to a higher capability mode upon reception of an initial control frame
    Lower capability mode (e.g., 20 MHz BW, one SS, limited data rates, PPDU format)
    Higher capability mode (e.g., operating BW, NSS and MCSs, with at least one higher capability than that in the lower power capability mode)

## Slide 4: Problem statement 1
In the existing preemption mechanism, the ongoing transmission in the current TXOP should be terminated, and completing the transmission of low latency traffic in the remaining TXOP.
Deliver the LL traffic by preemption is rude and rough:
  The preempting STA which is going to transmit the LL traffic can only get the transmission opportunity by preemption.
    When LL traffic arrives, it may not well supported by the current capability mode or operating mode of the preempting STA. If the STA is continuously maintain its current mode, the LL traffic can not be timely transmitted even with preemption.
AP
STA1
STA2
AP’s TXOP
DL PPDU1
DL PPDU2
PRI
TF
LL data
Remaining TXOP
BA
LL transmission could not be transmitted before the end of the TXOP

## Slide 5: Problem Statement 2
Therefore, it is desirable that the preempting STA is able to change the capability mode or operating mode, making them adapt to the LL traffic, so as to reduce the preemption occurance.
AP
STA1
STA2
AP’s TXOP
DL PPDU1
DL PPDU2
PRI
TF
LL data
Remaining TXOP
BA
By adjusting the capability mode or operating mode of STA2, the LL transmission could be finished before the end of TXOP.

## Slide 6: Discussions
Without dynamically change the capability mode or operating mode, it is highly likely that the LL traffic can not be transmitted in time and the preempted service is severely impacted, especially when
  the data amount of LL traffic is huge, e.g., for VR/XR.
  the time is tight for the LL traffic.
  the preempting STA can be with certain unfriendly capability mode or operating mode for the LL traffic.
The capability mode or operating mode of the preempting STA should be adjusted.
  It enhances the capability of the preempting STA to well support the LL traffic transmission.

## Slide 7: Summary
For an AP or a non-AP STA, changing the capability mode or operating mode is needed for timely delivery of LL traffic.

## Slide 8: References
[1] 23/0480r3, UHR Proposed PAR
[2] 24/0390r0, A Uniform Procedure for Preemption
[3] 24/0389r0, Preemption for Low Latency
[4] 24/0168r0, TXOP preemption in 11bn
[5] 24/0391r0, Legacy STA and OBSS Issues for Preemption
[6] 24/0103r1, TXOP Level Pre-emption for Low Latency Application
[7] 23/1593r0, Low Latency Transmission in EMLMR
[8] 24/0797r0, Operating Mode Request
[9] 24/0176r6, TGbn Motions List