## Slide 1: NB Update
Date: 2024-05-13
Authors:

## Slide 2: Background: Europe 6 GHz NB vs 802.11 VLP spectrum
NB with 14 dBm EIRP is 15/18/21 dB stronger than 802.11 VLP with 80/160/320 MHz
160 MHz
802.11
10 dBm/MHz
-8 dBm/MHz
320 MHz 802.11
-11 dBm/MHz
80 MHz 802.11
-5 dBm/MHz
NB
Note that skirts associated with NB spectrum are not shown and affect many 802.11 sub-carriers
Carlos Aldana, Meta Platforms

## Slide 3: Background in Coex SC
11-24-148r0 concluded that NB should adopt a mandatory coex mechanism to enable shared use of the spectrum and adequate performance for both 802.11 and NB. This mandatory mechanism should consist of one or more of LBT or other techniques.
11-24-360r4 (coauthored by 8 individuals from Meta, BCA, Qualcomm, Cisco, Intel, HPE, and Mediatek) recommends to make either CSMA-CA (with CCA mode 1) or SSBD with a provided set of parameters mandatory for NB-Data and NBA-MMS transmissions.

## Slide 4: Background in 802.15.4ab
15-24-212r5 proposes 2 possible technical solutions for discussion:
  CSMA-CA with CCA mode 1 (i.e., LBT) shall be used as the channel access mechanism before every TX
  For a NB capable device, if its NB TX duty cycle is more than 2.5%, it shall perform listen-before-talk (LBT) before any NB transmission. Otherwise, LBT is optional.
Carlos Aldana, Meta Platforms
NB
Poll
NB
Resp
Initiator
Responder
NB
Report 1
NB
Report 2
Optional w/ 10 dBm/MHz PSD
UWB
UWB
UWB
UWB
UWB
UWB
UWB
UWB
UWB
UWB
UWB
UWB
UWB
UWB
1ms
-41.3 dBm/MHz PSD
10 dBm/MHz PSD

## Slide 5: Background in ETSI 303687
Bluetooth SIG made a channel access proposal based on LBT to ETSI in BRAN(24)123a003r1
Carlos Aldana, Meta Platforms

## Slide 6: References
Spectrum Sensing Based Deferral (SSBD) : 15-22-0486-05
Carlos Aldana, Meta Platforms