## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Considerations for Non-Coherent UWB Receivers Operating in Long Range Mode]
Date Submitted: [16 March, 2010]
Source: [Adrian Jennings] Company [Time Domain]
Address [330 Wynn Drive, Suite 300, Huntsville, AL. 35805. USA]
Voice:[+1 256 759 4708], FAX: [+1 256 922 0387], E-Mail:[adrian.jennings@timedomain.com]
Re: [Packet structures to aid non-coherent UWB receivers]
Abstract: [This document proposes two remedies to help non-coherent UWB receivers receive and demodulate Long Range Mode packets intended primarily for coherent receivers]
Purpose: [To resolve outstanding issues on the current baseline proposal]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Considerations for Non-Coherent UWB Receivers Operating in Long Range Mode
Adrian Jennings
adrian.jennings@timedomain.com
+1 256 759 4708

## Slide 3: Background
The current draft of the 802.15.4f standard includes a long range mode for the UWB PHY
  Intended primarily for use by a coherent receiver
  Uses many (m) pulses per bit to enable pulse integration
This mode must also be received and demodulated by a non-coherent receiver
Two potential problems arise
  The long SFD is not ideal for synchronization
  Any long periods of zeros will cause loss of synchronization
Item #2 is also problematic for the coherent receiver when using OOK modulation

## Slide 4: Attaining Alignment

## Slide 5: Preamble Proposal
It is proposed that the Long Range Mode preamble include the 1 pulse per symbol SFD as the last 16 pulses
This provides a sync marker for the non-coherent receiver at the expense of slightly reduced preamble energy for the coherent receiver

## Slide 6: Proposed Preamble Diagram
Preamble
SFD
Key:
Long Range Mode
(2 MHz)
Base Mode
(1 MHz)
1111111111111111
0001010010011101
1111
0000
1111
1111
1111
1111
1111
1111
1111
1111
1111
1111
1111
0001
0000
0000
1111
0000
1111
0000
0000
0100
1001
1101
Etc.
1:1 SFD
1:1 SFD
4:1 SFD
Using 4 pulses per symbol for illustrative purposes only:

## Slide 7: Energy Lost in Preamble
Preamble Length | Pulses per symbol |  |  | 
 | 8 | 16 | 32 | 64
16 | -0.63 | -0.31 | -0.15 | -0.08
32 | -0.31 | -0.15 | -0.08 | -0.04
48 | -0.21 | -0.10 | -0.05 | -0.03
64 | -0.15 | -0.08 | -0.04 | -0.02
Energy loss in dB
A minimal effect given the gain in interoperability

## Slide 8: Maintaining Alignment

## Slide 9: The Issue
For an OOK system, no energy is received for a zero data value
Long stretches of zeros therefore provide no reference to correct for clock drift during a packet
We must ensure that the modulation scheme allows this “sync on data” functionality in all modes
This is of particular concern in the Long Range mode which has a much higher likelihood of long sequences of zeros

## Slide 10: Modulation Proposal
It is proposed that the modulation scheme be modified to ensure a maximum length to any run of zero pulse positions
This means inserting a data 1 after a defined run of data 0’s
How many 0’s can be tolerated?

## Slide 11: Example Calculations
Assumptions
  100MHz Rx clock, which can make 10ns pulse windows
  20ppm crystals in Tx and Rx per the UWB 4a PHY
  Goal is to drift no more than one window before receiving a pulse (which is a data 1)
Calculations
  Worst case link drift is 2x20ppm = 40ppm
  Time to drift 10ns @ 40ppm = 250ms
  # pulses @ 2MHz in 250ms = 500
  # pulses @ 1MHz in 250ms = 250

## Slide 12: Modulation Modification
Worst case is Long Range Mode, with multiple pulses per symbol
Exact number of pulses per symbol still TBD
Table below shows how many bits are in a 500 pulse run for various symbol mapping values
Mode | Pulses per Symbol | # 0's before inserting 1
Base (1 MHz) | 1 | 250
Long Range | 8 | 63
Long Range | 16 | 31
Long Range | 32 | 16
Long Range | 48 | 10
Long Range | 64 | 8

## Slide 13: Summary
Interoperability between Long Range tags and Base Mode receivers can be significantly improved with little cost
Proposal Summary
  Insertion of 1:1 mapped SFD as last 16 pulses of Long Range preamble
  Modification of data modulation as follows:
    Insert redundant one after 250 zeros in Base and Enhanced Modes
    Insert redundant one after 8 zeros in Long Range Mode