## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposed frequency arrangements to section 10 of TG3d Technical Requirements Document]
Date Submitted: [12 January 2015]
Source: [Akifumi Kasamatsu, Iwao Hosako, and Hiroyo Ogawa]
Company: NICT
Address [4-2-1, Nukuikita, Koganei, 184-8795, Tokyo, Japan]
Voice:[+ 81 42 327 6876], FAX: [], E-Mail:[kasa@nict.go.jp]
Re: []
Abstract: [The aim of this contribution is to propose the frequency arrangement for section 10 (Operational frequency bands) of TG3d Technical Requirements Document (TRD]
Purpose: [Proposing frequency arrangement in section 6 of TG3d Technical Requirements Document (TRD).]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Andrew Estrada, Sony

## Slide 2: Frequency Allocation below 275 GHz in Radio Regulation
Allocation to services | 
250-252 GHz | EARTH EXPLORATION-SATELLITE (passive) RADIO ASTRONOMY SPACE RESEARCH (passive) 5.340 5.563A
252-265 GHz | FIXED MOBILE MOBILE-SATELLITE (Earth-to-space) RADIO ASTRONOMY RADIONAVIGATION RADIONAVIGATION-SATELLITE 5.149 5.554
265-275 GHz | FIXED FIXED-SATELLITE (Earth-to-space) MOBILE RADIO ASTRONOMY

## Slide 3: Proposed Frequency Arrangement
CH1
CH2
CH3
CH4
2.160GHz
2.160GHz
2.160GHz
2.160GHz
8.640GHz
8.640GHz
8.640GHz
8.640GHz
8.640GHz
Based on IEEE802.15.3c
252GHz
BW=43.2GHz
295.2GHz

## Slide 4
Proposal
To use the same channel bandwidth specified by IEEE 802.15.3c as the first basic channel (BW=2.160 GHz).
Four bonded channel bonding is applied to create the second basic channel (BW=8.640 GHz).
To utilize the already allocated band of 252-275 GHz to mobile services.
To add the additional band of 275-295.2 GHz for mobile services.
To include this channel arrangement in section 10 as the operational frequency bands.