## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Operational frequency bands for TG3d devices]
Date Submitted: [12 January 2015]
Source: [Akifumi Kasamatsu, Iwao Hosako, and Hiroyo Ogawa]
Company: NICT
Address [4-2-1, Nukuikita, Koganei, 184-8795, Tokyo, Japan]
Voice:[+ 81 42 327 6876], FAX: [], E-Mail:[kasa@nict.go.jp]
Re: []
Abstract: [The aim of this contribution is to provide the candidate frequency bands for TG3d devices operating at THz frequency band.]
Purpose: [Discussion on the operational frequency bands for section 6 of TG3d Technical Requirements Document (TRD).]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Background
Several contiguous bands were discussed. [15-14-0613-01-003d]
The frequency range of 252-275GHz which are already allocated to mobile services were also discussed. [15-15-0038-00-003d]
In section 10 of TRD [15-14-0309-03-003d], the operational frequency bands are categorized into three bands, 60GHz, THz frequency band and free space optics.
This contribution is to provide the candidate frequency bands for TG3d devices operating at THz frequency band.

## Slide 3: Frequency Allocation below 275 GHz in Radio Regulation
Allocation to services | 
250-252 GHz | EARTH EXPLORATION-SATELLITE (passive) RADIO ASTRONOMY SPACE RESEARCH (passive) 5.340 5.563A
252-265 GHz | FIXED MOBILE MOBILE-SATELLITE (Earth-to-space) RADIO ASTRONOMY RADIONAVIGATION RADIONAVIGATION-SATELLITE 5.149 5.554
265-275 GHz | FIXED FIXED-SATELLITE (Earth-to-space) MOBILE RADIO ASTRONOMY

## Slide 4: Available contiguous bandwidth in the frequency range from 100 GHz to 1000 GHz

## Slide 5: Suitable frequency range and contiguous bandwidth
Frequency range (GHz) | Contiguous bandwidth (GHz) | Loss (dB/km)
(1) 200-320* | 120 | < 10
(2) 275-320 | 45 | < 10
(3) 335-360 | 25 | < 10
(4) 275-370 | 95 | < 100
(5) 380-445 | 65 | < 100
(6) 455-525 | 70 | < 100
(7) 625-725 | 100 | < 100
(8) 780-910 | 130 | < 100
* It is difficult to have contiguous bands below 252 GHz because there are many bands not allocated for mobile services.

## Slide 6
Proposal to section 10 of TRD
Not to identify the frequency band below 252 GHz for TG3d devices operating at THz frequency band.
Identify the frequency band of 252-275 GHz for TG3d devices operating at THz frequency band.
Further identify the frequency band of 275-325* GHz for TG3d devices operating at THz frequency band.
252GHz
275GHz
325GHz
Already allocated in RR
New frequency identification for TG3d devices
* The frequency of 325 GHz will be further studied by referencing Recommendation ITU-R P.676-9, “Attenuation by atmospheric gases”.