## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Information on ITU-R studies above 275 GHz]
Date Submitted: [13 September 2015]
Source: [Akifumi Kasamatsu, Iwao Hosako, and Hiroyo Ogawa]
Company: NICT
Address [4-2-1, Nukuikita, Koganei, 184-8795, Tokyo, Japan]
Voice:[+ 81 42 327 6876], FAX: [], E-Mail:[kasa@nict.go.jp]
Re: []
Abstract: [The aim of this contribution is to provide the information on activities currently studied by ITU-R WP1A, WP5A.]
Purpose: [To assist to develop the possible operational frequency bands for TG3d devices.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Background and Purpose
Several contiguous bands were discussed. [15-14-0613-01-003d].
The frequency range of 252-275GHz which are already allocated to mobile services were also discussed. [15-15-0038-00-003d].
Operational frequency bands for TG3d devices were recommended for section 10 of TRD. [15-15-0052-00-003d].
This contribution is to provide the information on activities currently studied by ITU-R WP1A, WP5A and WP5C, and to assist to develop the possible operational candidate frequency bands for TG3d devices.

## Slide 3: ITU-R WP1A activity
Study Question ITU-R 237/1, “Technical and operational characteristics of the active services operating in the range 275-1 000 GHz” were developed in 2013.
Report ITU-R SM.2352-0, “Technology trends of active services in the frequency range 275-3 000 GHz” were published.
Liaison statement was sent to IEEE802 which informed that;
  some bands in the frequency range 275-325 GHz are identified for the passive services by No. 5.565 of the Radio Regulations (RR).
  the studies are needed to review RR No. 5.565 for use of these bands by active services.
  the band 252-275 GHz is also allocated to the mobile and fixed services, and the additional contiguous bandwidth of 23 GHz could be utilized for terahertz communications.
The next WP1A meeting will be held on June 2016.

## Slide 4: ITU-R WP5A/5C activities
Question ITU-R 256-0/5, “Technical and operational characteristics of the land mobile service in the frequency range 275-1 000 GHz” was developed in 2015.
Question ITU-R 257-0/5, “Technical and operational characteristics of the fixed service in the frequency range 275-1 000 GHz” was developed in 2015.
A new section on THz wireless communication was created in the working document towards a preliminary draft revision of Report ITU-R F.2323-0 in 2015.
The next WP5A and WP5C meetings will be held on May 2016.

## Slide 5
Reply to ITU-R WP1A (WP5A and WP5C)
State agreement on its importance of the frequency range 252-275 GHz for TG3d devices.
Provide information on TG3d device characteristics in the frequency range 252-275 GHz, if available.
Provide possible frequency usgae plan in the frequency range 275-325 GHz and other additional frequency ranges for TG3d devices to make WP5A and WP5C identify these frequency bands for mobile and/or fixed services.
252GHz
275GHz
325GHz
Available frequency range for TG3d devices
New frequency identification for TG3d devices