## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [NBA-UWB MMS Compressed PSDU Details]
Date Submitted: [May 17, 2023]
Source: [Alexander Krebs, Robert Golshan, Moche Cohen, Sandeep Khare, Vinod Venkatesan, Santhosh Kumar Mani, Xiliang Luo, Yong Liu, Lochan Verma, Jinjing Jiang, SK Yong (Apple)]
Email: [a_krebs, rgolshan, …] @apple.com
Re: [Input to the Working Group]
Abstract: [Proposal of efficient MAC control signals suitable for a baseline feature set supported by low-rate O-QPSK narrowband PHYs.]
Purpose: []
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | Compressed PSDUs to initialize multi-millisecond ranging mode for NBA-UWB MMS
Enhanced native discovery and connection setup mechanisms | Compressed PSDUs to initialize multi-millisecond ranging mode for NBA-UWB MMS
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: Agenda
Generic PSDU concept
  Privacy protected addresses
  Message Control classes and versions
  Discovery, initialization, setup overview
Specific PSDU definitions
  PSDUs
  Fields

## Slide 4: Generic PSDU Concepts

## Slide 5: Compressed PSDU: Format Proposal
Generic compressed PSDU format
  1-octet PSDU ID (0-127, 128-255 reserved for 2-octet extension, …)
  Remaining PSDU content is ID specific

## Slide 6: Privacy Protected Addresses
Static MAC address in message header has privacy
Resolvable Private Address (RPA) protects against tracking
  IdentityResolvingKey[16] (IRK) is commonly known to PAN participants only
  prand[3] transmitted in POLL/ADV-POLL every ranging block
  hash[3] = AES-128-ECB(key=IRK[3], data=(0x000…[13] || prand[3])) every packet
POLL and ADV-POLL
Other packets

## Slide 7: Message Control
MessageControl[1] defines following of payload
  High nibble: 16 submessage (incl. 1 for generic error codes), for example:
  Low nibble: 16 versions (backward compatible) of message content, for example:

## Slide 8: Baltimore Refresher: MMS Initialization & Setup [3]
Initialization Concept:
3-packet exchange prior to NBA-UWB MMS ranging session
ADV-POLL, ADV-RESP, Start-of-Ranging (SOR) packets for discovery, initialization, and start of NBA-UWB MMS session

## Slide 9: MMS Initialization & Setup
Use
  optional features negotiation
  Future feature improvements and addons
Ex.: 0x02, 0x34, 0x56
  means: Initiator supports MsgCtl=0x30-0x34 and 0x50-0x56
ADV-POLL MsgCtl=0x00: Supported Message Control List (SMCL)
  Initiator enlists self supported MsgCtls
  Responder picks one MsgCtl (Responder version <= Initiator version) to be used later in ADV-RESP, SOR, POLL, RESP, REPORT

## Slide 10: MMS Initialization & Setup
Advertising Response (ADV-RESP)
  MsgCtl 0x00: Setup Request: Responder requests UNII-3/5 NB channel map, and MMS MAC PHY parameters
Start-of-Ranging (SOR)
    MsgCtl 0x00: Setup Response: Same format as ADV-RESP adding TimeOffset and ChannelSeed fields
      Initiator sets configuration for NBA-UWB MMS session and starts POLL after TimeOffset and switching channels
      Initiator picks configuration that is supported in responder’s supported feature set and regulatory constraint (-> pairing not in scope here)

## Slide 11: NBA-MMS UWB PSDU Definitions

## Slide 12: Advertising Poll (MsgCtl=0x00)
1-octet message ID (0x01: ”ADV-POLL”)
3-octet RPA hash + 3-byte RPA prand
1-octet message control, setting the following message content
  0x00: MessageContent = Len[SupportedMessageControlList] and SupportedMessageControlList=[0x00]
2-octet CRC16

## Slide 13: Advertising Response (MsgCtl=0x00)
1-octet message ID (0x02: “ADV-RESP”)
3-octet private address (RPA prand known from ADV-POLL)
1-octet message control, setting the following message content
  0x00 (Setup Request): Responder requests set of MMS ranging parameters
2-octet CRC16

## Slide 14: Start of Ranging (MsgCtl=0x00)
1-octet message ID (0x03: “SOR”)
3-octet private address (RPA prand known from ADV-POLL)
1-octet message control, setting the following message content
  0x00 (Setup Response): Initiator sets full set of MMS configuration parameters (same fields as ADV-RESP)
  Time Offset: Number of chips between end of SOR and beginning of first ranging block
  Channel Seed: initializes channel switching function
2-octet CRC16
Same format as ADV-RESP

## Slide 15: MMS Ranging: POLL, RESP, REPORT
MsgCtl=0x00 (Variant: “Unencrypted SS-TWR NBA-UWB MMS”, Version 0)
  12 bytes providing 576us total packet airtime @ 250k O-QPSK
  Turn-around-time (TAT) of Responder (“T_Reply” in 4z) / Round-trip-time (RTT) of Initiator (“T_Round” in 4z)
  Dynamically present, variable length arbitrary pass-through data (PTData) for providing minimal bi-directional data exchange functionality between MMS applications (higher layer)

## Slide 16: Poll (MsgCtl=0x00)
1-octet message ID (0x04: “POLL”)
3-octet RPA hash + 3-byte RPA prand
  Initiator may reset prand every every ranging block to obtain new RPA hash
1-octet message control, setting the following message content
  0x00: MessageContent = [0x00, 0x00], i.e., two octets for CFO estimation
2-octet CRC16

## Slide 17: Response (MsgCtl=0x00)
1-octet message ID (0x05: “RESP”)
3-octet RPA hash (prand known from POLL)
1-octet message control, setting the following message content
  0x00: MessageContent = [0x00, 0x00, 0x00, 0x00, 0x00], i.e., 5 octets for CFO estimation
2-octet CRC16

## Slide 18: Initiator Report (MsgCtl=0x00)
1-octet message ID (0x06: REPORT Initiator)
3-octet private session address (RPA prand known from POLL)
1-octet message control, setting the following message content
  0x00: MessageContent = RTT[5] + PTLen[1] + PTData[PTLen]
    Round-Trip-Time (RTT), 5 octets at resolution 1ps => range up to ~1s
    PTLen and PTData piggy-back up to 32 octets pass-through data to higher layer
      per-message optional field presence controlled by PHR Len
      12-44 octets, 576-1600 us total packet duration @ 250k, or 380-892us @ 500k K=7
2-octet CRC16

## Slide 19: Responder Report (MsgCtl=0x00)
1-octet message ID (0x07: REPORT Responder)
3-octet private session address (RPA prand known from POLL)
1-octet message control, setting the following message content
  0x00: MessageContent = TAT[5] + PTLen[1] + PTData[PTLen]
    Turn-Around-Time (TAT) at resolution 1ps
    PTLen and PTData piggy-back up to 32 octets pass-through data to higher layer
      per-message optional field presence controlled by PHR Len
      12-44 octets, 576-1600 us total packet duration @ 250k, or 380-892us @ 500k K=7
2-octet CRC16

## Slide 20: NBA-MMS UWB PSDU Fields

## Slide 21: Start-of-Ranging: Time Offset
Time Offset | 32 | Time offset in 1/499.2MHz resolution between end of SOR packet and beginning of first POLL packet of starting ranging session. Range: 0 to ~8.6 seconds
Field name | Length in bits | Description

## Slide 22: Setup: Channel Seed
Field name | Length in bits | Description
NB Channel Seed | 8 | 0-255: Sets key for switching function AES-128-ECB(key=Seed, …) referred to in section 1.4.3 (input MSBs zero-padded)

## Slide 23: Setup: Channel Select
Field name | Length in bits | Description
NB Channel Selection | 16 | Bits 0-1: UNII-3 border channel exclusion {0, 1, 3, 7}: Number of NB channels excluded from NBChannelAllowList counting from both lower and upper border of UNII-3 channels 0-49 Bits 2-4: UNII-5 low-side channel exclusion {0, 1, 3, 7, 15, 31, 63, 127}: Number of NB channels excluded from NBChannelAllowList counting from lower border of UNII-5 starting at channel 50. Bits 5-7: UNII-5 high-side channel exclusion {0, 1, 3, 7, 15, 31, 63, 127}: Number of NB channels excluded from NBChannelAllowList counting from upper border of UNII-5 starting at channel 249 Bits 8-12: low-side channel start offset (0-31): Number of NB channels excluded from NBChannelAllowList, extending on the exclusion signaled, counting from the lowermost included channels included after bits 0-4. Applies to both UNII-3 and UNII-5. Bits 13-15: Channel skip length {0, 1, 3, 7, 15, 31, 63, 127}: Number of channels periodically excluded after each first allowed channel following bits 0-12

## Slide 24: Setup: UWB PHY Config
Field name | Length in bits | Description
UWB PHY Config | 24 | Bits 0-5: Preamble Code Indexes {9, …, 48} if (9 <= Preamble Code Index <= 32) { Bits 6-12: Reserved } elseif (33 <= Preamble Code Index <= 48) { Bits 6-12: RSF complementary set zeros {0, …, 64} } Bits 13-15: N_MSR {32, 40, 48, 64, 128, 256} Bits 16-17: STS Segment Length x512 {32, 64, 128, 256} Bits 18-21: UWB channel 1-16 Bits 22-23: Reserved

## Slide 25: Setup: UWB MAC Config
Field name | Length in bits | Description
UWB MAC Config | 8 | Bits 0-2: {0,1,2,4,8,16} X RSFs Bits 3-5: {0,1,2,4,8} Y RIFs Bits 6: {1ms/2ms} Z RSF-to-RIF gap Bits 7: reserved

## Slide 26: Setup: NB PHY Config
Field name | Length in bits | Description
NB PHY Config | 8 | Sets O-QPSK PHY #1-#10 in section [2] {#1: 250k uncoded, …, #10} Bits 0-3: NB Control Phase Bits 4-7: NB Report Phase

## Slide 27: Setup: NB MAC Config
Field name | Length in bits | Description
NB MAC Config | 56 | Bits 0-2: Ranging Slot Duration {300, 600, …, 2400} RSTUs Bits 3-10: Ranging Round Duration 0-255 ranging slots Bits 11-18: Ranging Block Duration 0-255 ranging rounds Bits 19: Channel Switching: 0=Disabled, 1=Blockwise Bits 20: Measurement Report Request: 0=No, 1=Yes Bits 21-23: Reserved Bits 24-27: RcpPollSlots=0-15 Bits 28-31: RcpResponseSlots=0-15 Bits 32-43: RpDuration=0-4095 Bits 44-47: RpOffset=0-15 Bits 48-51: MrpFirstSlots=0-15 Bits 52-55: MrpSecondSlots=0-15

## Slide 28: Summary
Presented compressed PSDU concepts
  Resolveable Private Address (RPA) allows Initiator to rotate addresses regularly protect user’s privacy
  Message Control allows feature specific PSDU content and future backward compatible operation among standardized NBA-MMS-UWB devices
  Supported Message Control List handshakes use case dynamic parameters, such as ranging block length, NB channels to use, and most recently supported MsgCtl
Presented PSDUs for NBA-UWB MMS SS-TWR (unencrypted)
  One MsgCtl (0x00) each for ADV-POLL, ADV-RESP, SOR, POLL, RESP, REPORT
  Independent data rates for control and report phase
  Increased timestamp resolution over 15.4z
  Up to 32 bytes of pass-through data to higher layer application functions

## Slide 29: References
[1] A. Krebs et al., “NBA-MMS-UWB Compressed PSDU”, 15-22-0604-00-04ab.
[2] X. Luo (Apple), F. Leong (NXP), M. Lee (Samsung Electronics), et al., “NBA-UWB Technical Framework Proposal”, 15-22-0262-01-04ab.
[3] A. Krebs (Apple), L. Huang (Huawei), et al., “NBA-UWB ranging text proposal for 15.4ab TFD”, 15-22-0381-02-04ab.