## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Summary on Multiple Transmission in a slot
Date Submitted: July 11, 2023
Source: [Taeyoung Ha, Mingyu Lee, Youngwan So, Aniruddh Rao Kabbinale, Ankur Bansal, Clint Chaplin] Company [Samsung Electronics]
E-Mail: ty1115.ha@samsung.com
Abstract: Summary on Multiple RSF Transmissions in a Slot Scenario
Purpose: Increase air time efficiency by allowing the multiple MMRS transmission in a slot.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

## Slide 2: Motivation
There could be a time limit to meet the requirement of each applications
  An application needs additional devices (e.g., controllers of VR device)
  The duration of required ranging slots accommodating the certain number of devices may exceed the time limit
  Enhanced preamble codes are proposed [1][2]
  To support the application, multiple transmission in a ranging slot should be considered

## Slide 3: UWB Multiple RSF Transmission
In order to control the schedule of Multiple RSF Transmission, Scheduling IE can be used [3]
For Ranging report, current ranging report format (which is defined in 7.4.4.46 of 802.15.4z) can be used
Note that this procedures are not related with Multi-millisecond Ranging (MMR)

## Slide 4: NBA Multiple RSF Transmission
In order to schedule and trigger of Multiple RSF Transmission, Poll (one-to-many) message can be used
Scheduling and Trigger phase can be divided into two phase according to the purpose

## Slide 5: Aligned NB Message Format
In order to control the schedule of Multiple RSF Transmission, Poll (one-to-many) message can be used [5]
For Ranging report, ranging report of NB (which is defined in [6]) can be used
Message ID | Message Control | MessageConetents
0x10 (i.e., POLL (one-to-many) | 0x80 | Number of Responders[1], Request Bitmap[1], Presence Bitmap[1], List of {Responder Address[3], If Bit 0 of Presence Bitmap == 1 then {NbaChannelMap[6]}, If Bit 1 of Presence Bitmap == 1 then {NB PHY Config[1]}, If Bit 2 of Presence Bitmap == 1 then {NB MAC Config[7]}, If Bit 3 of Presence Bitmap == 1 then {UWB PHY Config[3]}, If Bit 4 of Presence Bitmap == 1 then {UWB MAC Config[2]}, If Bit 5 of Presence Bitmap == 1 then {StartSlotIndex[2], EndSlotIndex[2]}}

## Slide 6: Experimental Environment
In order to check the impact of body blockings, RSSI values are measured in 16 cases
  The location of Initiator (Receiver)'s antenna (leaned to Right or Left)
  The status of Initiator's antenna (Blocked by hand or Not Blocked)
  The status of Responder 1 (Right Transmitter)'s antenna (Blocked by hand or Not Blocked)
  The status of Responder 2 (Left Transmitter)'s antenna (Blocked by hand or Not Blocked)
Responder
Initiator
Antenna

## Slide 7: Experimental Results
Below figure shows the probability that the RSSI difference between Responder 1 and Responder 2 exceeds the 30 dB
  The worst case is that 1) the antenna of Initiator is located at the lower left and not blocked 2) Responder 1 is blocked by hand and Responder 2 is not blocked (i.e., yellow bar at the CASE 3)
  In this case, the probability that the RSSI difference between Responder 1 and Responder 2 exceeds the 30 dB is about 0.006

## Slide 8: Ranging Experimental Environment
In order to check the feasibility of the Multiple Transmission scenario in the VR scenario additional experiments were conducted
  Responder 1 (Right Transmitter) and Responder 2 (Left Transmitter) use different preamble code (Ipatov sequence, Length = 128)
  Responder 1 and Responder 2 transmit a packet to the Initiator simultaneously
  Initiator (Receiver) tries to detect the Responder 1’s preamble
  Due to the limitations in MAC protocol, Poll-Response method is used

## Slide 9: Ranging Experimental Environment
In order to check the feasibility of the Multiple Transmission scenario in the VR scenario additional experiments were conducted
  Experiments were proceeded according to the distance between Initiator and Responder 2 (i.e., Left Transmitter)
  The distance between Initiator and Responder 1 (i.e., Right Transmitter) is fixed as 90 cm
  Reference case means that there is only Responder 1 (i.e., Responder 2 do not transmit any signals)
90 cm
10 ~ 30 cm
Responder 1
Initiator
Responder 2

## Slide 10: Ranging Experimental Results
Below figure shows the probability that the Initiator successfully receives the packet of Responder 1 (i.e., Right Transmitter)
  For Reference case (i.e., no Responder 2), the probability of successfully receiving is 1.0 (i.e., No packet drop)
  As the distance between the Initiator and Responder 2 (i.e., Left Transmitter) decrease, the probability of successfully receiving packet decrease (Probability is about 0.95 when the distance between the Initiator and Responder 2 is 10 cm)

## Slide 11: Ranging Experimental Results
Below figure shows the average measured distance between the Initiator and Responder 1 (i.e., Right Transmitter)
  The exact distance between the Initiator and Responder 1 (i.e., Right Transmitter) is 90 cm
  As the distance between the Initiator and Responder 2 (i.e., Left Transmitter) decrease, the average measured distance increase (Average measured distance is about 95.6 cm when the distance between the Initiator and Responder 2 is 10 cm)

## Slide 12: Conclusion
In order to reduce the air time, Multiple Transmission scheme is proposed
Experimental results show the feasibility of proposed scheme

## Slide 13: References
[1] 15-21-0377-02 Preamble codes for Data Communications in 802.15.4ab
[2] 15-22-0405-03 Way Forward on Preamble Sequences beyond 4z Ipatov
[3] 15-23-0062-93 Text for Scheduling IE