## Slide 1
Project: IEEE P802.15 Working Group for Wireless Specialty Networks
Submission Title: Overview and convergence of MAC proposals for 15.6ma
Date Submitted: July 13th, 2023
Source: Minsoo Kim, Seong-Soon Joo, Takumi Kobayashi, Anzai Daisuke, Marco Hernandez, Ryuji Kohno
Company: YRP-IAI, KPST, CWC Oulu Univ, NIT, YNU
Address: (1)79-5 Tokiwadai, Hodogaya-ku, Yokohama, 240-8501 Japan,
(2) YRP1 Blg., 3-4 HikarinoOka, Yokosuka-City, Kanagawa, 239-0847 Japan
Voice:[+81-90-5408-0611] E-Mail:[minsoo@minsookim.com, kobayashi-takumi-ch@ynu.ac.jp, marco.hernandez@ieee.org, kohno@ynu.ac.jp, ssjoo@etri.sci.kr]
Re: In response to call for proposal
Abstract: Overview and convergence of MAC proposals for 15.6ma
Purpose: Material for discussion in P802.15.6ma TG
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: MAC Protocol Proposal for Multiple BAN Environmnet (Class 1), Proposal of control and data channels unification for 6ma MAC # 15-22-0639, #15-23-0387
Unifying control and data channels into a single channel, instead of utilizing Control Channel, is proposed.
Frames for Coordinator to Coordinator link, previously carried by control channel, is carried by newly defined time period in the single channel.
For networks require higher dependability, feature of simultaneously utilizing multiple channel may still remain as optional.
Time axis
Time period for C2C frames
Time period for Coordinator-to-Nodes frames
Superframe

## Slide 3: Proposed text for 6ma MAC – General framework elements, Beacon Access Phase, Frames and IEs for dependable BAN, and Interference Avoidance # 15-23-0322, # 15-23-0367, # 15-23-0369, # 15-23-0324
New terms are defined.
  beacon access phase (BAP), coordinator hub, dependable BAN, dependable BAN group, leaf hub.
General explanation are modified according to new scope/features.
  The revised standard will specify access coordination at the MAC sublayer between BANs.
Classes (1-3) of dependable BANs are defined.
  In terms of bounded latency, probability of loss, update rate.
Beacon Access Phase (BAP) is introduced.
  A coordinator hub (a.k.a. super-coordinator or coordinator of coordinators) manage beacon slot allocation for leaf hubs. The last slot of BAP is reserved for a BAN of the original std.
New features such as Access offset, Access Phase shifting are introduced.
  For mitigating the interference among coexisting dependable BANs, the start of access phase can be set differently.
Information Elements (IE) are added/defined according to the new features.

## Slide 4: Convergence
Proposal # 15-22-0639 is going to be modified. the MAC will be able to use single channel too.
  The fundamental difference of # 15-22-0639 and # 15-23-0322 series is already converged.
  The detailed differences need to be examined more deeply, but the convergence of such differences will be much easier.
The differences in terminology will be also converged.
  The two proposals have become very similar, but there are still many differences in terminology.
The convergence process will continue via teleconference prior to the September interim session, in order to complete the draft within the timeline.