## Slide 1
Project: IEEE P802.15 Working Group for Wireless Specialty Networks (WSN)
Submission Title: MMS Ranging Messaging
Date Submitted: 31 July 2023
Source: Carl Murray (Qorvo), Jarek Niewczas (Qorvo), Billy Verso (Qorvo)
Abstract: Recommendation for approach for MMS ranging messaging
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Notes: Jul 12, 2010
Page 1

## Slide 2
PAR Objective | 
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEV) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | 
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: MMS Ranging Phases
Discovery
Initialization
Control
Ranging
Report
Ranging Cycle

## Slide 4: Possible MMS Ranging Mechanisms
 | Discovery | Initialization | Control | Ranging | Report
NBA | O-QPSK | O-QPSK | O-QPSK | UWB | O-QPSK
UWB-only | UWB | UWB | UWB | UWB | UWB
NBA offload1 | O-QPSK | O-QPSK | O-QPSK | UWB | UWB
NBA offload2 | O-QPSK | O-QPSK | UWB | UWB | UWB
OOBA3 | OOB | OOB | UWB | UWB | UWB
Offload NB data to UWB (15-23-0372-01)
Further offload NB data to UWB– minimize the impact on Wi-Fi due to NBA hopping (hopping for interference mitigation is harmful to Wi-Fi – comment made during discussion of 15-23-0285-00)
“Alternatively, different PHYs other than O-QPSK can assist UWB as well by exploiting the open interfaces provided by MAC services.” 15-23-0100-02
  e.g. standard ranging with increased first-path (FP) dynamic range
15.4 PHY, non-15.4 PHY

## Slide 5: Recommendations
To effectively respond to the various possible alternative mechanisms presented in the previous slide the following recommendations are proposed for consideration -
The protocol should be such that each phase could be implemented by a selected PHY from the list in the table in the previous slide
15.4 messages should be designed so they can be efficiently used by either the O-QPSK PHY or the UWB PHY for each relevant phase
All 15.4 PHYs should use a common 15.4 MAC (e.g. extended frame format or similar)
This “modular approach” (i.e. flexible choice of PHY for each phase) would also address the requirement that “different PHYs other than O-QPSK can assist UWB” as each phase is decoupled from a protocol perspective
Use a term like MMS-Control PHY rather than NBA PHY where appropriate to make the MMS text more generic