## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Use cases for Next Generation SUN PHYs]
Date Submitted: 12 July 2023
Source: Hiroshi Harada (Kyoto University)
Address Yoshidahonmachi. Sakyo, Kyoto, 606-8501, Japan
Voice: +81-75-753-5317 , E-Mail: hiroshi.harada@i.kyoto-u.ac.jp
Re: [Wireless Next Generation, Long Range extension enhancements to 802.15.4-2020]
Abstract: Introduce basic transmission characteristics of IEEE 802.15.4 SUN-FSK and SUN-OFDM and their deployment in various applications with improved reception schemes, and show items necessary for future extensions. A part of this contribution was supported from the commissioned research (No.05101) by National Institute of Information and Communications Technology (NICT) , Japan.
Purpose: Propose use for the new standardization of Next Generation SUN PHYs
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Use cases for Next Generation SUN PHYs
Jan 16, 2024
Hiroshi Harada, Ph.D.

## Slide 3: Background
Wireless SUN is expected to be used in various fields other than smart metering
This contribution will focus on a variety of areas beyond smart metering and propose use cases for Next Generation SUN PHYs
Wide-area communications will require the use of VHF bands, etc., rather than Sub-GHz

## Slide 4
Use-Case Name | Description | Device Density | Data Rate | Typical packet size | Packets per hour | Transmit Range | Frequency Range
Disaster prevention Monitoring : High-speed | Cliff collapse and water level monitoring using moving images | 10 per km^2 | Up to 10 Mbit/s | 2000 byte | Always connected | Up to 10 km | Sub-GHz VHF band
Disaster prevention Monitoring : Low-speed | Environmental sensing using acceleration sensors, rainfall sensors, etc. | 1000 per km^2 | Up to 100 kbit/s | 500 byte | 60 | Up to 20 km | Sub-GHz VHF band
Infrastructure monitoring : High-speed | Structural health monitoring using moving and still images | 0.1 per m^2 | Up to 10 Mbit/s | 2000 byte | Always connected | Up to 10 km | Sub-GHz VHF band
Infrastructure monitoring :Low-Speed | Structural health monitoring of bridges, buildings, and so on using acceleration sensors, tilt sensors, vibration sensors, etc. | 1 per m^2 | Up to 100 kbit/s | 500 byte | 3600 | Up to 10 km | Sub-GHz VHF band
Medical application : High-speed | Telemedicine system using video and still images | 100 per km^2 | Up to 10 Mbit/s | 2000 byte | Always connected | Up to 10km | Sub-GHz VHF band
Medical application : Low-speed | Biological monitoring such as blood pressure, fever, etc.on in hospital wards and nursing homes | 0.1 per m^2 | Up to 100 kbit/s | 500 byte | 1 | Up to 100m | Sub-GHz VHF band
Proposed Use Cases

## Slide 5
Use-Case Name | Description | Device Density | Data Rate | Typical packet size | Packets per hour | Transmit Range | Frequency Range
Factory : High-speed | Connection of sequencers to assembly and processing equipment in the plant | 10 per m^2 | Up to 5 Mbit/s | 2000 byte | Always connected | Up to 1km | Sub-GHz
Factory : Low-speed | Environmental monitoring of temperature, humidity, air, etc. in the factory | 1 per m^2 | Up to 100 kbit/s | 500 byte | 100 | Up to 1km | Sub-GHz
Agriculture : High-speed | Crop growth monitoring using still and moving images | 1000 per km^2 | Up to 5 Mbit/s | 2000 byte | 10000 | Up to 10km | Sub-GHz VHF band
Agriculture : Low-speed | Environmental monitoring using various sensors on farms and fields | 10000 per km^2 | Up to 100 kbit/s | 500 byte | 10 | Up to 10 km | Sub-GHz VHF band
Fisheries : High-speed | Growth monitoring at aquaculture sites using still and moving images | 100 per km^2 | Up to 5 Mbit/s | 2000 byte | 10000 | Up to 20 km | Sub-GHz VHF band
Agriculture : Low-speed | Environmental monitoring using various sensors on farms and fields | 1000 per km^2 | Up to 100 kbit/s | 500 byte | 10 | Up to 20 km | Sub-GHz VHF band
Proposed Use Cases

## Slide 6
Use-Case Name | Description | Device Density | Data Rate | Typical packet size | Packets per hour | Transmit Range | Frequency Range
Intelligent transport systems: High-speed | Monitoring of traffic conditions on the road, low latency control information for automated operations (e.g. automated vehicle) | 10000 per km^2 | Up to 5 Mbit/s | 2000 byte | Always connected | Up to 10 km | Sub-GHz VHF band
Intelligent transport systems: Low-speed | Roadside monitoring with environmental sensors: temperature, humidity, air, etc. in the factory Transmission of traffic-related information to vehicles (e.g. automated vehicle) | 10000 per km^2 | Up to 100 kbit/s | 2000 byte | 5000 | Up to 10km | Sub-GHz VHF band
Proposed Use Cases