## Slide 1
  Protocol discussion version 2.0
Document Number: IEEE 802.16-13-0198-00-03R0
Date Submitted: 2013-12-12
Source:
  Antonio Bovo Voice: +390497623908
  TEKCOMMS E-mail: antonio.bovo@tekcomms.com
  *<http://standards.ieee.org/faqs/affiliationFAQ.html>
Re: 16-13-0198-00-03R0
Base Contribution:
Purpose: WG discussion
Notice:
  This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein.
Copyright Policy:
  The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>.
Patent Policy:
  The contributor is familiar with the IEEE-SA Patent Policy and Procedures:
      <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>.
  Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat >.

## Slide 2: Round table discussion on protocols for 802.16.3 WG
Content:
  Recap of strategy for identifying the suitable protocol(s).
  Potential protocol candidates.
  Example of protocol handshake choosing one of the best candidates.
  Basic IE content proposal for the different message handshakes.

## Slide 3: Recap of strategy for identifying the suitable protocol(s)
The protocol(s) to be adopted has/have to support the following functionalities:
  Registration
  Authentication
  Encryption
  Measurements transfer
  Configuration
  Commands/Notifications
Other basic requirements are related to the mobile device domain:
  Simplicity, to minimize the resources dedicated to communication tasks.
  Possibly already adopted even for other purposes on UE devices.

## Slide 4: Some Protocol options and functionalities
Protocol | Basics on protocol | Comments
XCAP | Extensible Markup Language (XML) Configuration Access Protocol. XML payload, structured protocol, adopted in Telecom environments. Typically used for configuration and manipulation of per-user data. HTTP/HTTPS based. | It can support registration and authentication. Encryption can be supported with HTTPS. Data Configuration is exactly the scope of the protocol. The measurements results could be transferred directly via HTTP, for example.
TR-069 | XML payload, structured protocol, adopted in Telecom environments. Typically used for auto-configuration and provisioning and also for sharing statistical measurements. SOAP/HTTP based. | The protocol supports registration, authentication and encryption via TLS. Commands and notifications can be plugged using the protocol. Measurement transfer is directly supported allowing a synchronization between the file transfer and the peers’ dialogue.
Parlay/ OSA | Parlay/Open Service Access. XML payload, structured protocol, adopted in Telecom environments. Typically used for configuration/query of network services and applications. SOAP/HTTP based | It is typically used as a network framework to authenticate and manage applications. SOAP can be based on HTTPS to manage security.
OMA DM | Open Mobile Alliance Device Management XML payload, structured protocol, adopted in several domains (e.g. WiFi domain). Typically used for configuration of devices, remote command execution and SW download. | Commands, notifications and download of information are possible. The measurement transfer could be based directly on HTTP.
JSON over HTTP | JavaScript Object Notation. Simple, not structured protocol. Typically used for serialization of structured data. It’s more a set of formatting rules than a protocol. | Authentication and security have to be supported separately from the protocol itself.
MQTT | Message Queuing Telemetry Transport. It is a M2M protocol to exchange messages between subscribed devices. | It is a publish/subscribe messaging protocol suitable for entities with limited processing capabilities and connected even with low bandwidth. Security could be supported using SSL.
SIP | Session Initiation Protocol. SIP with extensions can support even PUBLISH, UPDATE, REGISTER. Already used on mobile devices. | SIP with extensions is suitable for registration and event notifications. Measurement transfer could be based on mechanisms similar to those detailed in RFC 6035. With these mechanism, it is possible to report via SIP the RTP Control Protocol Extended Reports] metrics

## Slide 5: Example of implementation with TR-069
Let’s take one of the candidates, TR-069 protocol, and figure out a possible schematic message flow for the different 802.16.3 basic functionalities.
In addition, let’s focus on the possible parameters needed in the different message handshakes.

## Slide 6: Registration handshake (1/3)
DNS
(Controllers)
DNS
(Public)
DNS Request/Response
UE
Controller
DNS Request/Response
Open connection
SSL initiation
HTTP POST (TR-069 INFORM REQUEST
(DeviceID, EventType = Registration, …)
HTTP Response (TR-069 INFORM RESPONSE (…)

## Slide 7: Registration handshake (2/3)
UE
Controller
HTTP POST (empty)
HTTP Response (TR-069 GETPARAMETERNAMES
(ParameterPath of Registration parameters,…)
HTTP POST (TR-069 GETPARAMETERNAMESRESPONSE
(ParameterList with parameters’ names ,… )
HTTP Response (TR-069 GETPARAMETERVALUES
(ParameterNames of registration parameters,…)
HTTP POST (TR-069 GETPARAMETERVALUESRESPONSE
( Parameterlist with name-value pairs ,… )
Major parameters | Meaning
RegTime | Time/day registration
RAT | Radio Access Technology in use
LastRegTime | Time of last registration
Last S-ID | Last Test Session ID
P-ID | Permanent Client ID
Last T-ID | Last Temporary Client identifier
S- Loc | Subscriber Location
… | …

## Slide 8: Registration handshake (3/3)
UE
Controller
HTTP Response (TR-069 SETPARAMETERVALUES
(Parameterlist with name value pairs,…)
HTTP POST (TR-069 SETPARAMETERVALUESRESPONSE
( Status ,… )
HTTP Response (empty)
Close connection
Major parameters | Meaning
Outcome | Registration outcome
Cause | Optionally, cause of failure
New T-ID | New Temporary Client-ID assigned
New S-ID | New assigned Test session identifier
S-Time | Session lifetime
… | …

## Slide 9: Configuration handshake (1/2)
UE
Controller
SSL Initiation
HTTP GET(TR-069 CONNECTIONREQUEST (…)
…
HTTP Response (e.g. OK 200)
If configuration is
initiated by the Controller
HTTP POST (TR-069 INFORM REQUEST
(DeviceID, EventType = Connection Request or UE-initiated configuration, …)
HTTP Response (TR-069 INFORM RESPONSE (…)

## Slide 10: Configuration handshake (2/2)
UE
Controller
HTTP POST (empty)
HTTP Response (TR-069 GETPARAMETERNAMES
(ParameterPath of Configuration parameters,…)
HTTP POST (TR-069 GETPARAMETERNAMESRESPONSE
(ParameterList with parameters’ names ,… )
HTTP Response (TR-069 SETPARAMETERVALUES
(ParameterList with name-value pairs,…)
HTTP POST (TR-069 SETPARAMETERVALUESRESPONSE
( Status,… )
Major parameters | Meaning
Time/day | Time of configuration
S-Addr | Path to Public (Private) server
C-Addr | Path to Public (Private) data collector
Conf-Time | Period for checking configuration changes
Data usage limit | Max bytes the client will transfer in a month
… | …
HTTP Response (empty)
Close connection

## Slide 11: Measurement upload
UE
Controller
SSL Initiation
HTTP POST (TR-069 INFORM REQUEST
(DeviceID, EventType = Autonomous transfer complete , …)
HTTP Response (TR-069 INFORM RESPONSE (…)
Collector
Open connection
HTTP POST (TR-069 AUTONOMOUSTRANSFERCOMPLETE
(…, TransferURL, IsDownload, FileType, FileSize, TargetFileName, …)
HTTP Response (TR-069 AUTONOMOUSTRANSFERCOMPLETERESPONSE (…)
Measurement file transfer
HTTP Response (empty)
Close connection
Major parameters | Meaning
Time/day | Time of file production
S-ID | Session ID
T-ID | Client ID
MPB | Measurement protected bundle
Meas.type | Measurement execution type
… | …

## Slide 12: Deregistration handshake (1/2)
DNS
(Controllers)
DNS
(Public)
DNS Request/Response
UE
Controller
DNS Request/Response
Open connection
SSL initiation
HTTP POST (TR-069 INFORM REQUEST
(DeviceID, EventType = Deregistration, …)
HTTP Response (TR-069 INFORM RESPONSE (…)

## Slide 13: Deregistration handshake (2/2)
UE
Controller
HTTP POST (empty)
HTTP Response (TR-069 GETPARAMETERNAMES
(ParameterPath of Configuration parameters including ClientID,…)
HTTP POST (TR-069 GETPARAMETERNAMESRESPONSE
(ParameterList with parameters’ names ,… )
HTTP Response (TR-069 SETPARAMETERVALUES
(ParameterList with name-value pairs,…)
HTTP POST (TR-069 SETPARAMETERVALUESRESPONSE
( Status,… )
Major parameters | Meaning
Time/day | Time of deregistration
P-ID | Permanent Client ID
T-ID | Temporary Client ID
S-ID | Session ID to be deregistered
… | …
HTTP Response (empty)
Close connection
Major parameters | Meaning
Time/day | Time of deregistration
Outcome | Successful, Failure of the deregistration
Cause | Optional. Cause of failure
… | …

## Slide 14: Basic Information Elements related to Client registration
REGISTRATION IE | UE  CONTROLLER | Meaning
RegTime | UE  CONTROLLER | Registration day/time
RAT | UE  CONTROLLER | Radio Access Technology currently in use
LastRegTime | UE  CONTROLLER | Last Registration day/time. This is to limit the number of subsequent registrations.
LastS-ID | UE  CONTROLLER | Last Test Session ID, assigned to the client or, alternatively, a “null” identifier signalling the first registration to the system.
P-ID | UE  CONTROLLER | Permanent Client-ID
LastT-ID | UE  CONTROLLER | Last Temporary Client-ID assigned
S-Loc | UE  CONTROLLER | Subscriber Location (current)
… | … | …
REGISTRATION IE | CONTROLLER  UE | Meaning
Outcome | CONTROLLER  UE | Registration outcome (successful, failure)
Cause | CONTROLLER  UE | Failure cause (optional) Values could be according to RFC 2616 or specifically defined.
New T-ID | CONTROLLER  UE | New Temporary Client ID assigned to the UE Scope: unique within the Controller. It can be reused once it is released.
New S-ID | CONTROLLER  UE | New Test Session ID assigned to the UE Scope: the same as T-ID.
S-Time | CONTROLLER  UE | Session Lifetime This is the active time assigned to the session. When it expires, then the registration is considered automatically closed. It is possible also to deregister explicitly from the test session.
… | … | …

## Slide 15: Basic Information Elements related to Server registration
REGISTRATION IE | SERVER  CONTROLLER | Meaning
RegTime | SERVER  CONTROLLER | Registration day/time
LastRegTime | SERVER  CONTROLLER | Last Registration day/time
Address(es) of the server | SERVER  CONTROLLER | Path to the server (IP addresses or FQDN)
Meas-C | SERVER  CONTROLLER | Measurement capabilities of the server (e.g. which measurements, which granularity)
… | … | …
REGISTRATION IE | CONTROLLER  SERVER | Meaning
Outcome | CONTROLLER  SERVER | Registration outcome (successful, failure)
Cause | CONTROLLER  SERVER | Failure cause (optional)
S-Time | CONTROLLER  SERVER | Session Lifetime This is the active time assigned to the session. When it expires, then the registration is considered automatically closed. However, an explicit deregistration is possible.
… | … | …

## Slide 16: Basic Information Elements related to commands
Command IE | SERVER  CONTROLLER | Meaning
Command type | SERVER  CONTROLLER | Type: {Start, Stop, …} Allows to inform the Controller about the start of measurements or stop of measurements at Server side.
CommandTime | SERVER  CONTROLLER | Command day/time
… | … | …
Command IE | CONTROLLER  SERVER | Meaning
Outcome | CONTROLLER  SERVER | Command outcome (successful, failure)
Cause | CONTROLLER  SERVER | Failure cause (optional)
… | … | …
Command IE | UE  CONTROLLER | Meaning
Command type | UE  CONTROLLER | Type: {Start, Stop, …} Allows to inform the Controller about the start of measurements or stop of measurements at UE side.
CommandTime | UE  CONTROLLER | Command day/time
… | … | …
Command IE | CONTROLLER  UE | Meaning
Outcome | CONTROLLER  UE | Command outcome (successful, failure)
Cause | CONTROLLER  UE | Failure cause (optional)
… | … | …

## Slide 17: Basic Information Elements related to Client configuration
CONFIGURATION IE | CONTROLLER  UE | Meaning
ConfTime | CONTORLLER  UE | Time/day of configuration
S-Addr | CONTROLLER  UE | IP address or FQDN. Path to public/private server
C-Addr | CONTROLLER  UE | IP address or FQDN. Path to Public/Private data collector
Conf-Time | CONTROLLER  UE | How often client should check Controller for configuration changes
Data Usage Limit | CONTROLLER  UE | Data usage Limit: the max number of bytes the Client will transfer in one month.
Distance-Threshold | CONTROLLER  UE | Distance threshold: land distance from previous test a Client must exceed to perform its next test set
Time-Threshold | CONTROLLER  UE | Time since previous test a Client must exceed to perform its next test set
Location Threshold | CONTROLLER  UE | Accuracy threshold above which Client will not initiate test set
Test Set | CONTROLLER  UE | List of indexes of tests to conduct
Test Parameters | CONTROLLER  UE | List of test-specific parameters
Registration Interval | CONTROLLER  UE | How often Client should re-register with Controller
[Re-registration trigger parameters] | CONTROLLER  UE | tbd
Battery Threshold | CONTROLLER  UE | The battery level below which the Client will not submit to Data Collector
[additional conditional triggering parameters] | CONTROLLER  UE | tbd
Sampling user plane | CONTROLLER  UE | 1=Sampling 0=No sampling. This field allows configuring the sampling of user plane in measurements.
Sampling type | CONTROLLER  UE | {uniform, session beginning, adaptive, …} It is the configuration of the specific sampling type.
Time/day of last configuration | CONTROLLER  UE | 
… | … | …

## Slide 18: Basic Information Elements related to Server configuration
CONFIGURATION IE | CONTROLLER  SERVER | Meaning
ConfTime | CONTORLLER  SERVER | Time/day of configuration
C-Addr | CONTROLLER  SERVER | IP address or FQDN. Path to Public/Private data collector
Conf-Time-S | CONTROLLER  SERVER | How often server should check Controller for configuration changes
Test Set | CONTROLLER  SERVER | List of indexes of tests to conduct
Test Parameters | CONTROLLER  SERVER | List of test-specific parameters
Registration Interval | CONTROLLER  SERVER | How often Server should re-register with Controller
[Re-registration trigger parameters] | CONTROLLER  SERVER | tbd
[additional conditional triggering parameters] | CONTROLLER  SERVER | tbd
Sampling user plane | CONTROLLER  SERVER | 1=Sampling 0=No sampling
Sampling type | CONTROLLER  SERVER | {uniform, session beginning, adaptive, …}
Time/day of last configuration | CONTROLLER  SERVER | 
… | … | …

## Slide 19: Basic IEs related to UE measurements
MEASUREMENTS IE | UE  COLLECTOR | Meaning
S-ID | UE  COLLECTOR | Test Session ID
T-ID | UE  COLLECTOR | Client identity assigned by the Controller to the UE.
Measurement protected bundle (MPB) | UE  COLLECTOR | It signals that the measurements payload is encrypted or in clear text. 1=Encrypted 0=Clear text Encrypted could be typically used for Private Server not for Public Server. If security is assured by underlay TLS or if it is not important at all, then this field will be = 0.
Measurement execution type | UE  COLLECTOR | 1=Public Server 0=Private Server
Length of Meas. Data body | UE  COLLECTOR | Start of Meas. data body. From this point on, the message is encrypted if the previous flag MPB is set.
Controller Identifier | UE  COLLECTOR | Identifier of the destination Controller (IP address or FQDN)
Start time of measurements | UE  COLLECTOR | 
Stop time of measurements | UE  COLLECTOR | 
Progressive meas. interval | UE  COLLECTOR | Progressive number assigned to the measurement results, in case of periodical sending.
Test ID | UE  COLLECTOR | Specific Test Identifier
>Application ID | UE  COLLECTOR | Application ID indicated with a string (e.g. DNS, HTTP, POP3/SMTP, …)
>Length of Application data | UE  COLLECTOR | Length in byte of the entire Application ID measurements (excluding this Length field)
>>Meas.Container ID | UE  COLLECTOR | Progressive # of the Container including the specific measurement identifier.
>>Meas. Identifier | UE  COLLECTOR | Measurement identifier
>>> Meas. Type | UE  COLLECTOR | 
>>> Meas. Param. | UE  COLLECTOR | 
>>> Meas.Value | UE  COLLECTOR | 
>>> Meas. Value 2 | UE  COLLECTOR | In some cases it would be needed to provide two values for a specific measurements, for example in case of goodput (bytes, time).
… | … | …

## Slide 20: Basic IEs related to SERVER measurements
MEASUREMENTS IE | UE  COLLECTOR | Meaning
S-ID | SERVER  COLLECTOR | Test Session ID (to be decided if it is the test session of the server, grouping multiple UE access, or if it is referring to the specific UE Test session, measured at the server endpoint)
Server identity | SERVER  COLLECTOR | Server identity
Measurement protected bundle (MPB) | SERVER  COLLECTOR | It signals that the body of the measurements is encrypted or in clear text. 1=Encrypted 0=Clear text Encrypted can be typically used for Private Server not for Public Server. If security is assured by underlay TLS or if it is not important at all, then this field will be = 0.
Measurement execution type | SERVER  COLLECTOR | 1=Public Server 0=Private Server
Length of Meas. Data body | SERVER  COLLECTOR | Start of Meas. data body. From this point on, the message is encrypted if the previous flag MPB is set.
Controller Identifier | SERVER  COLLECTOR | Identifier of the destination Controller (IP address or FQDN)
Start time of measurements | SERVER  COLLECTOR | 
Stop time of measurements | SERVER  COLLECTOR | 
Progressive meas. interval | SERVER  COLLECTOR | Progressive number assigned to the measurement results, in case of periodical sending.
Test ID | SERVER  COLLECTOR | Specific Test Identifier
>Application ID # | SERVER  COLLECTOR | Application ID indicated with a string (e.g. DNS, HTTP, POP3/SMTP, …)
>>Length of Application data | SERVER  COLLECTOR | Length in byte of the entire Application ID measurements (excluding this Length field)
>>Meas.Container ID | SERVER  COLLECTOR | Progressive # of the Container including the specific measurement identifier
>>Meas. Identifier | SERVER  COLLECTOR | Measurement identifier
>>> Meas. Type | SERVER  COLLECTOR | 
>>> Meas. Param. | SERVER  COLLECTOR | 
>>> Meas.Value | SERVER  COLLECTOR | 
>>> Meas. Value 2 | SERVER  COLLECTOR | In some cases it would be needed to provide two values for a specific measurements, for example in case of goodput (bytes, time).
… | … | …