## Slide 1
  Standardization of Mobile Wireless Small Cell Backhaul (SCB)
Document Number:
  IEEE 802.16-14-0075-00-000r
Date Submitted:
  2014-09-17
Source:
  Junhyeong Kim, Hee-Sang Chung, and Il Gyu Kim
  Electronics and Telecommunications Research Institute (ETRI)
  E-mail: jhkim41jf@etri.re.kr, hschung@etri.re.kr, igkim@etri.re.kr
Re:
  Call for Contributions (16-14-0064-01-000r)
Base Contribution:
  16-14-0071-00-000r, 16-14-0074-00-000r
Purpose:
  To review the draft PAR and discuss whether to modify the existing PAR or to propose a new PAR
Notice:
  This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein.
Copyright Policy:
  The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>.
Patent Policy:
  The contributor is familiar with the IEEE-SA Patent Policy and Procedures:
      <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>.
  Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat >.

## Slide 2: Proposed draft PAR for Development of Mobile Wireless Small Cell Backhaul (SCB)
Proposed draft PAR
  Modified based on the existing PAR document (P802.16r, IEEE 802.16-12-0587-05-Gdoc)
  Five Criteria

## Slide 3: Scope of the project (1/2)
Operating in licensed or unlicensed bands from 3 to 40 GHz
Bandwidth
  Up to 1 GHz
  Backhaul radio operates far enough outside the band of the small cells that interference is negligible

## Slide 4: Scope of the project (2/2)
Modulation order
  Only 256 QAM is added
  Higher order modulation (512QAM/1024QAM) is hard to implement in millimeter-wave and high-speed moving environment
    Phase noise
    Low-power source
    Doppler effect

## Slide 5: Need for the project
Bandwidth : wide spectrum
  A vast amount of radio spectrum remains underutilized
  Allow for larger bandwidth channels and greater data speeds.
  Key point : network capacity improvement
    high order modulation and large bandwidth
Mobile wireless backhaul for high-speed moving environment (moving small cell)
  High-speed train, subway, bus, and etc

## Slide 6: Five Criteria
1. Broad Market Potential
2. Compatibility
3. Distinct Identity
4. Technical Feasibility
5. Economic Feasibility

## Slide 7: Five Criteria (3. Distinct Identity)
P802.16r
  Air interface based on IEEE Std 802.16-2012
Proposing standard
  New RAT (Radio Access Technology) based on millimeter-wave

## Slide 8: Five Criteria (4. Technical Feasibility) (1/2)
(a) Demonstrated system feasibility
  60GHz : WiGig, IEEE 802.11ad
  E-band : millimeter-wave fixed wireless system
(b) Proven technology, reasonable testing
  Higher MIMO orders
  Higher frequency with larger bandwidth
  High-speed moving environment
(c) Confidence in reliability
  Unchanged

## Slide 9: Five Criteria (4. Technical Feasibility) (2/2)
4.1 Coexistence of IEEE 802 LMSC wireless standards specifying devices for unlicensed operation
  Coexistence Assurance (CA) document

## Slide 10: Five Criteria (5. Economic Feasibility)
(a) Known cost factors, reliable data
  Higher order modulation
  Higher frequency with larger bandwidth (millimeter-wave)
(b) Reasonable cost for performance
  A vast amount of radio spectrum with relatively low cost remains underutilized in millimeter-wave
(c) Consideration of installation costs
  Unchanged

## Slide 11: Standardization of Mobile Wireless Small Cell Backhaul (SCB)
PAR
  Modify the existing PAR or propose a new PAR