## Slide 1: APAC update – December 2021
Author:

## Slide 2: Background
This slide deck provides a high-level overview of the activities in APAC (related to Wi-Fi and WPAN) between November 2021 and December 2021.

## Slide 3: Hong Kong HKCA (1)
Creation of a Class Licence for Regulating the Use of and Trade in 6 GHz Devices for Wireless Local Area Network and Variation to the Class Licence for Provision of Public Wireless Local Area Network Services
  Consultation period: November 26 to December 24, 2021
    https://www.coms-auth.hk/filemanager/en/content_711/cp20211126_e.pdf

## Slide 4: Hong Kong HKCA (2)
  Summary
    HKCA proposes the maximum EIRP of 24 dBm (250 mW) for indoor use; and 14 dBm (25 mW) for outdoor use.
    HKCA proposes to update its relevant specification HKCA 1081 by referencing ETSI EN 303 687.
    HKCA notes that some countries and regions designate the entire 6 GHz band for Wi-Fi. Wi-Fi devices from these countries and regions that “could operate in the 6425 – 7125 MHz band, if illegally imported and used in Hong Kong, would cause in-band interference to the future 5G services”. In view of this, the consultation seeks public opinions to impose compulsory certification requirements for APs to ensure that “such devices to be used in Hong Kong should comply with the relevant specification (i.e. HKCA 1081), in particular that they do not operate in the 6425 – 7125 MHz band which may be used for 5G services in Hong Kong in the future.”

## Slide 5: Hong Kong HKCA (3)
  Remarks
    HKCA’s view on the potential use of 6 GHz bands (paragraphs 17 and 25):
      SSAC Members noted that such low power devices should not cause interference to the existing fixed-satellite service (“FSS”) (Earth-to-space) operating in the designated 6 GHz band and generally support the release of the band for use of WLAN devices in uncoordinated and unprotected manner in Hong Kong.
      As for the 6425 – 7125 MHz band, the CA will consider the use of this band, or parts thereof, for 5G services in Hong Kong subject to the outcome of WRC-23 and other considerations including co-existence with the incumbent services and frequency coordination with the neighbouring regions

## Slide 6: Hong Kong HKCA (4)
  Remarks (Cont’d)
    HKCA emphasizes on the importance to control non-compliant devices (paragraphs 18 and 19):
      In this connection, Hong Kong has encountered similar interference problem due to the use of illegal DECT 6.0 cordless phones that users brought from overseas had caused interference to the public mobile services and OFCA has spent tremendous efforts to keep the situation under control. Although the US imposed requirements for the relevant access points of WLAN devices to be under control of an automated frequency coordination (“AFC”) system or a contention-based protocol so as to ensure protection to fixed services and facilitate sharing of spectrum among different devices/services, the effectiveness of such technical provisions to protect the future 5G services outside the US, particularly in Hong Kong, is still uncertain.
      The measures may include more stringent certification and labelling requirements to be imposed on the sale of Wi-Fi 6E devices in Hong Kong as compared with the conventional WLAN products working in the 2.4 GHz and 5 GHz bands.

## Slide 7: Indonesia MCIT
RPM Public Consultation regarding the Table of Allocation of the Indonesian Radio Frequency Spectrum
  Consultation period: November 18 to November 27, 2021
    https://www.kominfo.go.id/content/detail/38184/siaran-pers-no-402hmkominfo112021-tentang-konsultasi-publik-rpm-mengenai-tabel-alokasi-spektrum-frekuensi-radio-indonesia/0/siaran_pers
  Summary
    The table of frequency allocation is updated as per the 2020 edition of Radio Regulations by ITU and the promulgation of Presidential Regulation No. 92 of 2021 concerning the Ratification of the Final Acts of WRC-19.

## Slide 8: Japan MIC (1)
Announcement of the “frequency reorganization action plan”
  Released on November 15, 2021
    https://www.soumu.go.jp/menu_news/s-news/01kiban09_02000421.html
  Of interest to us:
    MIC recommended to allocate 1 GHz for unlicensed uses by 2025. The frequency band under consideration is 6 GHz.
    MIC recommended that nearly 30 MHz spectrum is allocated for V2X by 2025. The frequency band under consideration is 5.9 GHz.
    MIC recommended to continue studying the possibility of allocating 7025 MHz to 7125 MHz band to 5G by referring to the studies of ITU-T and 3GPP.

## Slide 9: Japan MIC (2)
Consultation on the technical conditions for the introduction of 5.2 GHz band in-vehicle wireless LAN
  Consultation period: November 17 to December 16, 2021
    https://www.soumu.go.jp/menu_news/s-news/01kiban12_02000132.html
  Selected finding:
    Channel placement between 5150 MHz and 5250 MHz:
      20 MHz width or less: 5180 MHz, 5200 MHz, 5220 MHz, 5240 MHz
      Over 20 MHz width and below 40 MHz width: 5190 MHz, 5230 MHz
      Over 40 MHz width and below 80 MHz width: 5210 MHz
    Usage conditions:
      Master station: Installed in a car. EIRP should be 40mW or less.
      Slave station: It shall be controlled and communicated by the master station installed in the car.

## Slide 10: Korea MSIT (1)
Administrative notice (2021-0931) related to a partial revision of table of frequency allocation
  Consultation period: November 17, 2021 to January 16, 2022
    https://www.msit.go.kr/bbs/view.do?sCode=user&mId=109&mPid=103&pageIndex=&bbsSeqNo=84&nttSeqNo=3179348&searchOpt=ALL&searchTxt=
  Summary
    There is an increasing use of the 76–81 GHz frequency band for object detection sensors in various application fields, such as collecting biometric information.
    The proposed change is to enable radar devices to operate in the 70 GHz band by updating the domestic note K40A that allows the 76 to 81 GHz frequency band to be used for object detection.

## Slide 11: Korea MSIT (2)
Administrative notice (2021-0933) related to a partial revision of technical standards
  Consultation period: November 17, 2021 to January 16, 2022
    https://www.msit.go.kr/bbs/view.do?sCode=user&mId=109&mPid=103&pageIndex=&bbsSeqNo=84&nttSeqNo=3179352&searchOpt=ALL&searchTxt=
  Summary
    It is related to the administrative notice 2021-0931 with proposed technical requirements as shown in the next page.

## Slide 12: Korea MSIT (3)
Administrative notice (2021-0933) related to a partial revision of technical standards
  Selected proposed technical requirements
    Peak power: 100mW or less (including antenna absolute gain)
    Average power density is -16 dBm / MHz
    Spurious emission limit:
      Less than 1 GHz: -36 dBm with reference bandwdith of 100 kHz
      1 GHz or larger: -30 dBm with reference bandwidth of 1 MHz
    It is prohibited to use in moving objects such as automobiles, aircraft, ships, railways.
    This device is intended for use in buildings. If it is installed within a radius of 2 km from the radio astronomical antenna, prior consultation with the observatory is required.

## Slide 13: New Zealand RSM (1)
Draft five year spectrum outlook 2022-2026
  Consultation period: November 29, 2021 to February 28, 2022
    https://www.rsm.govt.nz/projects-and-auctions/consultations/five-year-spectrum-outlook-2022-2026/
  3 main questions RSM ask for opinions:
    Have we identified the range of technological advancements and probable new demands relevant to New Zealand?
    Have we prioritised the right issues that we will need to actively manage through our work programme (to the extent this is possible to predict now)?
    Are there other matters that we should cover?

## Slide 14: New Zealand RSM (2)
Draft five year spectrum outlook 2022-2026
  Of interest to us:
    4 main technological areas and the corresponding priorities on spectrum are presented:
      Satellites
      Cellular mobile – 5G
        Page 15: RSM will continue to proactively engage in ITU, APT and international trade matters relating to spectrum including monitoring and responding to developments in the 6.425 – 7.125 GHz band for mobile and Wi-Fi.
      IoT / M2M
        Page 16: The standardisation of wireless technology is creating a trend of convergence around wireless 3GPP and IEEE standardised technologies to replace proprietary technologies and land mobile systems in some sectors.
      Private networks

## Slide 15: New Zealand RSM (2)
Draft five year spectrum outlook 2022-2026
  Of interest to us (Cont’d #2)
    Spectrum sharing
      Page 22: We will continue to monitor the demand for different tools and levers to allow more innovative approaches to spectrum sharing.
      Consider sharing models when developing future spectrum bands is one of the RSM’s planned work plan priorities
    User of higher frequencies
      Page 22: This includes the frequency ranges recently identified for mmWave 5G in the 26 GHz, 40 GHz and 66-71 GHz bands
      Page 22: There is growing interest in the use of even higher frequency ranges (eg above 100 GHz) with the latest technological advancements.
      Monitor use of multigigabit wireless systems in the 66-71 GHz range is one of the RSM’s planned work plan priorities

## Slide 16: New Zealand RSM (2)
Draft five year spectrum outlook 2022-2026
  Of interest to us (Cont’d #3)
    Licensing approaches enabling new technologies
      Consider updates to General User Licences, particularly for short-range devices and monitor developments in the use of 6 GHz for Wi-Fi 6E is one of the RSM’s planned work plan priorities
      Consider a General User Licencing regime when developing higher frequency bands is another RSM’s planned work plan priority in this category.