## Slide 1: APAC update – March 2022
Author:

## Slide 2: Background
This slide deck provides a high-level overview of the activities in APAC (related to Wi-Fi and WPAN) between January and March 2022.

## Slide 3: China MIIT
Notice of the MIIT on adjusting the frequency use planning and radio management of microwave communication systems
  Consultation period: January 26 ~ February 27, 2022
    Link
  Asks for public opinion on:
    adjusting the frequency bands of the microwave communication system as follows:
      4500~4800 MHz, 7125~7725 MHz, 7725~8500 MHz, 10.7~11.7 GHz, 12.75~13.25 GHz, 14.5~15.35 GHz, 21.2~23.6 GHz, 71~76 GHz, 81~86 GHz
    technical requirements for radio transmitting equipment of microwave communication system operating in the above-mentioned frequency bands
    the frequency bands of the microwave communication system involved in coordination with space radio services

## Slide 4: Japan MIC
Call for opinions: Technical conditions for the introduction of 6 GHz band wireless LAN
  Consultation period: March 3 ~ April 1, 2022
    Link
  Selected summary:
    Frequency band: 5925 ~ 6425 MHz
    Modes of operation: low power indoor, very low power
    EIRP (antenna power) should be 200 mW or less in LPI mode and 25 mW or less in VLP mode.
    Many technical conditions of 6 GHz LPI will follow those of 5 GHz
    For 6425 ~ 7125 MHz, further coexistence studies are required.

## Slide 5: Malaysia MCMC
Class Assignment No. 1 of 2022
  Published and is effective since January 19, 2022
    https://www.mcmc.gov.my/skmmgovmy/media/General/CA-No-1-of-2022_-signed_19012022.pdf
  Of interest to us is the updated class assignment on short range devices operating between 5925 MHz and 6425 MHz.

## Slide 6: Thailand NBTC
U.S. - Thailand 6 GHz Spectrum Virtual Workshop
  February 17~18, 2022
    https://www.nbtc.go.th/News/Information/52494.aspx
    https://www.standardsportal.org/usa_en/toolbox/US%E2%80%93Indo-Pacific-STCP.aspx
    During the workshop, a NBTC representative shared the information that NBTC has agreed on a policy that 5.925~6.425 GHz is for unlicensed use with an expected public consultation in Q2/Q3 this year. 6.425~7.125 GHz is under consideration subject to the outline of the WRC-23 meeting.