## Slide 1: IEEE 802.18 45 GHz Ad Hoc Proposal
Date: 2022-08-04
Authors:
August 2022
Notes: September 2012

## Slide 2: Abstract
August 2022
IEEE is an international organization, and as such should consider developing the Ultra High Reliability standard in a way that makes it universally available. There are mmWave bands that offer sufficient spectrum to support future throughput requirements that are or could be made available globally. The 45 GHz band (42.5 – 48 GHz) meets these requirements and should be included as part of the UHR SG and be supported by an Ad Hoc RR-TAG group.
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 2

## Slide 3: Executive Summary
IEEE is an international organization
In 2012, TGad was developing a 60 GHz standard in spectrum not available in China
As a result, a parallel project, TGaj was required to make this standard an international standard
The 6 GHz band is also not available in China and limited elsewhere, where the burgeoning Fiber Internet market has increasing throughput demands
The next generation after 802.11be should do its best to provide a standard that may be used globally
IEEE 802.11aj used spectrum in the 45 GHz band
IEEE 802.18 should consider supporting this as part of the UHR SG work
August 2022
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 3

## Slide 4: Problem Statement #1
Fiber deployment is increasing and increasing potential internet speeds
  FTTR is becoming a major focus in China and elsewhere
Throughput projections will surpass 802.11be capabilities
  As they pass the 100 Mbps range, mmWave bands begin to look more suitable
  Increased use of the 6 GHz band with 320 MHz wide channels will quickly create congestion, even in 1.2GHz of spectrum; we are pushing mid-band limits
August 2022

## Slide 5: Problem Statement #2
The recent and future 802.11 standards focus on the 6 GHz band
  This band is limited to ~500 MHz in many regulatory domains
  China and other countries have no spectrum available for unlicensed use in this band
  IEEE 802.11 created the 11aj standard for operation in the 45 GHz band (CMMW) and should consider it for future 802.11 standards
mmWave band spectrum can support these requirements for years to come
  Over 5 GHz of spectrum could be made available globally in the 45 GHz band
August 2022

## Slide 6: IEEE 802.11aj
Study Group (CMMW) started in January 2012
Task Group started in September 2012
  Finished work in November 2017
Primarily focused 802.11ad functionality in the 45 GHz band because China’s 60 GHz band is limited
  Actual range: 42.5 to 49 GHz
August 2022

## Slide 7: IEEE 802.11aj Operating Classes
Channel set for the 45 GHz band
August 2022

## Slide 8: The 45 GHz Band (High Level)
 | ITU-R Radio Regs | The US (FCC) | Europe (ECO)
42.5 – 43.5 GHz | Fixed Fixed Satellite (Earth to Space) Mobile (except aeronautical mobile) Radio-Astronomy | Fixed Fixed Satellite (Earth to Space) Mobile (except aeronautical mobile) Radio-Astronomy | Fixed Fixed Satellite (Earth to Space) Mobile (except aeronautical mobile) Radio-Astronomy
43.5 – 47 GHz | Mobile Mobile Satellite (Earth to Space) Radionavigation Radionavigation-Satellite | Mobile Mobile Satellite (Earth to Space) Radionavigation Radionavigation-Satellite | Mobile Mobile Satellite (Earth to Space) Radionavigation Radionavigation-Satellite
47 – 47.2 GHz | Amateur Amateur Satellite | Amateur Amateur Satellite | Amateur Amateur Satellite
47.2 – 47.5 GHz | Fixed Fixed Satellite (Earth to Space) Mobile | Fixed Fixed Satellite (Earth to Space) Mobile | Fixed Fixed Satellite (Earth to Space) Mobile
47.5 – 47.9 GHz | Fixed Fixed Satellite (Earth to Space) Fixed Satellite (Space to Earth)* Mobile | Fixed Fixed Satellite (Earth to Space) Mobile | Fixed Fixed Satellite (Earth to Space) Fixed Satellite (Space to Earth)* Mobile
47.9 – 48.2 GHz | Fixed Fixed Satellite (Earth to Space) Mobile | Fixed Fixed Satellite (Earth to Space) Mobile | Fixed Fixed Satellite (Earth to Space) Mobile
*Region 1 only
August 2022

## Slide 9: 45 GHz Ad Hoc Activities
Detailed incumbent study
Determine if and where regulations may need changes
Support UHR SG mmWave band discussions
August 2022

## Slide 10: References
US FCC Table of Frequencies
  https://transition.fcc.gov/oet/spectrum/table/fcctable.docx
European Table of Frequency Allocations
  https://docdb.cept.org/download/2ca5fcbd-4090/attachments/2013_ERCRep025.pdf
  ECO Frequency Information System (cept.org)
ITU-R Radio Regulations
  https://www.itu.int/pub/R-REG-RR
August 2022