## Slide 1: 60GHz Regulatory Overview for mmWave Ad Hoc
Notice: This document has been prepared to assist IEEE 802.18. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Date: 2022-10-12
Authors:

## Slide 2: Abstract
This contribution provides a high-level overview of regulatory requirements for 60GHz (57-71GHz) band for consideration by 802.18 mmWave ad hoc.
This contribution covers the following areas, it is early draft and will be revised in the future.
  ITU The Radio Regulations, Edition of 2020; including the results of WRC-19
  Regional Regulatory Status
  Summary Regulatory Requirements
  Existing Mobile Services Technologies in 60GHz
  TBD

## Slide 3: Radio Regulation: Articles-Frequencies Regions 1-3 (1/2)
57-58.2 EARTH EXPLORATION-SATELLITE (passive) FIXED INTER-SATELLITE 5.556A MOBILE 5.558 SPACE RESEARCH (passive) 5.547 5.557
58.2-59 EARTH EXPLORATION-SATELLITE (passive) FIXED MOBILE SPACE RESEARCH (passive) 5.547 5.556
59-59.3 EARTH EXPLORATION-SATELLITE (passive) FIXED INTER-SATELLITE 5.556A MOBILE 5.558 RADIOLOCATION 5.559 SPACE RESEARCH (passive)
59.3-64 FIXED INTER-SATELLITE MOBILE 5.558 RADIOLOCATION 5.559 5.138
64-65 FIXED INTER-SATELLITE MOBILE except aeronautical mobile 5.547 5.556
65-66 EARTH EXPLORATION-SATELLITE FIXED INTER-SATELLITE MOBILE except aeronautical mobile SPACE RESEARCH 5.547
66-71 INTER-SATELLITE MOBILE 5.553 5.558 5.559AA MOBILE-SATELLITE RADIONAVIGATION RADIONAVIGATION-SATELLITE 5.554

## Slide 4: Radio Regulation: Articles-Frequencies Regions 1-3 (2/2)
5.557 Additional allocation: in Japan, the band 55.78-58.2 GHz is also allocated to the radiolocation service on a primary basis. (WRC-97)
5.558 In the bands 55.78-58.2 GHz, 59-64 GHz, 66-71 GHz, 122.25-123 GHz, 130-134 GHz, 167-174.8 GHz and 191.8-200 GHz, stations in the aeronautical mobile service may be operated subject to not causing harmful interference to the inter-satellite service (see No. 5.43). (WRC‑2000)
5.559 In the band 59-64 GHz, airborne radars in the radiolocation service may be operated subject to not causing harmful interference to the inter-satellite service (see No. 5.43). (WRC‑2000)
5.559AAThe frequency band 66-71 GHz is identified for use by administrations wishing to implement the terrestrial component of International Mobile Telecommunications (IMT). This identification does not preclude the use of this frequency band by any application of the services to which this frequency band is allocated and does not establish priority in the Radio Regulations. Resolution 241 (WRC‑19) applies. (WRC‑19)

## Slide 5: RESOLUTION 241 (WRC‑19) Use of the frequency band 66-71 GHz for International Mobile Telecommunications and coexistence with other applications of the mobile service
considering
a) that International Mobile Telecommunications (IMT), including IMT‑2000, IMT‑Advanced and IMT‑2020, and other wireless access systems are intended to provide telecommunication services on a worldwide scale regardless of location and type of network or terminal;
b) that the evolution of IMT is being studied within the ITU Radiocommunication Sector (ITU‑R);
c) that harmonized worldwide frequency bands and harmonized frequency arrangements are highly desirable in order to achieve global roaming and the benefits of economies of scale;
d) that adequate and timely availability of spectrum for IMT and supporting regulatory provisions are essential to realize the objectives in Recommendation ITU‑R M.2083;
e) that IMT systems are envisaged to provide increased peak data rates and capacity that may require a larger bandwidth;
f) that there is a need to protect existing services and to allow for their continued development,
resolves
1 that administrations wishing to implement IMT make available the frequency band 66‑71 GHz identified in No. 5.559AA for use by the terrestrial component of IMT;
2 that administrations wishing to implement IMT in the frequency band 66-71 GHz, identified for IMT under the provisions in No. 5.559AA, which also wish to implement other applications of the mobile service, including other wireless access systems in the same frequency band, consider coexistence between IMT and these applications,

## Slide 6: RESOLUTION 241 (WRC‑19) Use of the frequency band 66-71 GHz for International Mobile Telecommunications and coexistence with other applications of the mobile service
invites the ITU Radiocommunication Sector
1 to develop harmonized frequency arrangements for the implementation of the terrestrial component of IMT in the frequency band 66-71 GHz;
2 to develop ITU‑R Recommendations and/or Reports, as appropriate, to assist administrations in ensuring the efficient use of the frequency band through coexistence mechanisms between IMT and other applications of the mobile service, including other wireless access systems, as well as between the mobile service and other services;
3 to regularly review, as appropriate, the impact of evolving technical and operational characteristics of IMT systems (including base-station density) and those of systems of space services on sharing and compatibility, and to take into account the results of these reviews in the development and/or revision of ITU‑R Recommendations/Reports addressing, inter alia, if necessary, applicable measures to mitigate the risk of interference into space receivers,

## Slide 7: Regional Regulatory Status

## Slide 8: Summary Regulatory Requirements

## Slide 9: Mobile Services Technologies in 60GHz: WiGig
Wi-Fi Technology currently uses the 66-71 GHz band as licensed exempt spectrum and Wi-Fi Alliance started certification of Wi-Fi CERTIFIED WiGig devices in October of 2016.
Wi-Fi CERTIFIED WiGig™ expands the Wi-Fi® experience for virtual reality, multimedia streaming, gaming, wireless docking, and enterprise applications requiring high speed, data-intensive connections.
Since 2016, different category of products from various device manufacturers, including the following, have been certified and introduced to market:
  Connectivity,
  Computers and Accessories,
  Televisions and Set Top Boxes,
  Gaming,
  Media and Music
Some popular uses for WiGig products include:
  Wireless docking between devices like smartphones, laptops, projectors, and tablets
  Simultaneous streaming of multiple, ultra-high definition videos and movies
  More immersive gaming, augmented reality and virtual reality experiences
  Fast download of HD movies
  Convenient public kiosk services
  Easier handling of bandwidth intensive applications in the enterprise

## Slide 10: Mobile Services Technologies in 60GHz: Radar
TBD

## Slide 11: Mobile Services Technologies in 60GHz: IMT
No country has adopted 66-71 GHz for licensed IMT as a result of WRC-19
CEPT had already decided before WRC-19 to use 66-71 GHz for license-exempt and still supported the IMT identification at WRC-19 (which some thought makes no sense).
After WRC-19 there was a question from the EU to CEPT to see if that WRC-19 decision would lead to any further change in regulation in CEPT and the clear answer was “No”.

## Slide 12: References
ITU-R Radio Regulations
  https://www.itu.int/pub/R-REG-RR
US FCC Table of Frequencies
  https://transition.fcc.gov/oet/spectrum/table/fcctable.docx
European Table of Frequency Allocations
  https://efis.cept.org/ [search by frequency, country, etc.]
  https://efis.cept.org/sitecontent.jsp?sitecontent=ecatable
European National Frequency Tables
  https://efis.cept.org/views2/national_frequency_table.jsp