## Slide 1: Unofficial translation of selected contents of the two Taiwan MoDA consultations
Date: 4 May 2023
Author:

## Slide 2: Disclaimer
The contents presented in this slide deck are the author’s unofficial translation of selected contents of the two recent Taiwan MODA consultations: Draft amendment of “Table of Radio Frequency Allocations of the Republic of China (Taiwan)” and Draft amendment of “Radio Frequency Supply Plan”.
Please refer to the administration’s website for the exact contents (in traditional Chinese) of the consultations.

## Slide 3: First consultation (1)
Consultation: Draft amendment of “Table of Radio Frequency Allocations of the Republic of China (Taiwan)”
  Publication date: 24 April 2023
  Closing date for response: 26 June 2023
    Internal 802.18 deadline to allow for 10 day EC ballot: 8 June 2023
For details, please visit
  https://join.gov.tw/policies/detail/90281604-5f51-4591-bbf6-4885842fb2b4
Overview
  Considering that major countries in the world, including the United States, Canada, Brazil, South Korea, the United Kingdom, and the European Union, allow part or all of the 6 GHz frequency band for unlicensed low-power wireless information transmission equipment, such as Wi-Fi 6E, the administration proposed to revise Item 3, Article 52 of the Telecommunications Management Law such that
    5945 MHz to 6425 MHz is allowed for indoors/outdoors low power wireless information transmission without causing harmful interference to existing authorized communications and without protection from any interference caused by existing authorized communications.

## Slide 4: First consultation (2)
First proposed changes: To add the following text to the section 2 of the table of frequency allocation:
ITU-RR | Taiwan | 
Region 3 | Service allocation | Remarks
5925.0000-6700.0000 Fixed (primary), Fixed satellite (Earth to Space) (primary), Mobile (primary) | 5925.0000-6700.0000 Fixed (primary), Fixed satellite (Earth to Space) (primary), Mobile (primary) | 5925 - 6425 for the use of the public communication relay network. WRC-03 also resolved to allow ESVs (aircraft/shipboard earth station) to use. 5925 - 6425 for low-power U-NII equipment that operates no greater than 14 dBm outdoor or no greater than 23 dBm indoors without causing harmful interference to existing authorized communications and without protection from any interference caused by existing authorized communications. Remote control drones are not allowed to use this frequency band. Devices using this band must have interference avoidance mechanisms, e.g., Listen-Before-Talk (LBT). 6336 - 7920 for the use of low-power UWB in secondary conditions

## Slide 5: First consultation (3)
Second proposed changes: To add the following text to the appendix “Low-power RF devices” in the table of frequency allocation:
Usage | Frequency band
For low-power U-NII equipment that operates no greater than 14 dBm outdoor or no greater than 23 dBm indoors without causing harmful interference to existing authorized communications and without protection from any interference caused by existing authorized communications. Remote control drones are not allowed to use this frequency band. Devices using this band must have interference avoidance mechanisms, e.g., Listen-Before-Talk (LBT). | 5945-6425 (MHz)

## Slide 6: Second consultation (1)
Consultation: Draft amendment of “Radio Frequency Supply Plan”
  Publication date: 24 April 2023
  Closing date for response: 26 June 2023
    Internal 802.18 deadline to allow for 10 day EC ballot: 8 June 2023
For details, please visit
  https://join.gov.tw/policies/detail/bde426d7-55e2-4cd3-8873-4692fe04f607
Overview
  In aligning with the plan to allow 5945 MHz to 6425 MHz for use by U-NII equipment, the administration proposed to revise Item 3, Article 52 of the Telecommunications Management Law such that:
    6425 MHz to 7125 MHz is allowed for experimental network trials, for example, mobile communications, technology research and development, product development and application services of unlicensed low-power wireless information transmission.
    a further review on the use of 6425 MHz to 7125 MHz is conducted after the development trend of international communication technology and the demand for service use on this frequency band are certain

## Slide 7: Second consultation (2)
Proposed changes: To add the following text to the section “Experimental network” in the table of frequency allocation:
Specific experiment frequency (MHz) | Purpose of the experiment | Specific experimental field | Other test conditions
6425 - 7125 | For mobile communications, unlicensed low power wireless information transmission and other experimental network trials | Taiwan | Do not cause harmful interference to existing authorized communications. Do not receive protection from any interference received from the existing authorized communications