## Slide 1: Unofficial translation of selected contents of the China MIIT consultation on 802.11be
Date: 1 June 2023
Author:

## Slide 2: Disclaimer
The contents presented in this slide deck are the author’s unofficial translation of selected contents of the China MIIT consultation: Technical requirements and test methods for new type approval of wireless LAN equipment adopting IEEE 802.11be technical standards
Please refer to the administration’s website for the exact contents (in simplified Chinese) of the consultation.

## Slide 3: Technical Requirement: Multi-band Operation (MLO)
In the multi-band concurrent state, the operating frequency of the relevant radio transmitting equipment and out-of-band emission power shall comply with the and the MIIT’s “Notice on Strengthening and Regulating Radio Management in the 2400MHz, 5100MHz and 5800MHz Frequency Bands” (Ministry of Industry and Information Technology No [2021] No. 129)
Operating frequencies
  2400 MHz - 2483.5 MHz, 5150 MHz – 5350 MHz, 5725 MHz – 5850 MHz
Out-of-band transmit power
  The maximum equivalent isotropic radiated power at the upper and lower limits of the operating frequency is not greater than -80 dBm/Hz
Limit value of EVM
  4096 QAM: 0.016%
Notes: ,

## Slide 4: Technical Requirement: MRU spectrum mask (1)
Punctured spectrum mask of an edge subchannel position
Frequency offset from the edge of occupied subchannel, f | Limit value (NOTE: PSD is linearly distributed with frequency)
0 MHz ≤ f < 0.5 MHz | 0 to 20 dBr
0.5 MHz ≤ f < 0.5Me MHz (Me: frequency separation between the lower edge of the lowest occupied subchannel and the upper edge of the highest subchannel) | 20 to 28 dBr
Notes: ,

## Slide 5: Technical Requirement: MRU spectrum mask (2)
Punctured holes at non-edge positions and the bandwidth of the punctured subchannel is greater than 40 MHz
Frequency offset from the edge of occupied subchannel, f | Limit value (NOTE: PSD is linearly distributed with frequency)
0 MHz ≤ f < 0.5 MHz | 0 to 20 dBr
0.5 MHz ≤ f < 0.5Mm MHz (Mm: contiguous occupied bandwidth adjacent to punctured subchannels) | 20 to 25 dBr
Notes: ,

## Slide 6: Technical Requirement: MRU spectrum mask (3)
The non-edge position is punctured and the bandwidth of the punctured subchannel is 20 MHz
Frequency offset from the edge of occupied subchannel, f | Limit value (NOTE: PSD is linearly distributed with frequency)
0 MHz ≤ f < 0.5 MHz | 0 to 20 dBr
0.5 MHz ≤ f < 10 MHz | 20 to 23 dBr
10 MHz ≤ f < 19.5 MHz | 20 to 23 dBr
19.5 MHz ≤ f < 20 MHz | 0 to 20 dBr
Notes: ,

## Slide 7: Technical Requirement: MRU spectrum mask (4)
The non-edge position is punctured and the bandwidth of the punctured subchannel is 20 MHz (cont’d)
Notes: ,

## Slide 8: Testing methodologies: Multi-band Operation (MLO) (1)
Block diagram:
Notes: ,

## Slide 9: Testing methodologies: Multi-band Operation (MLO) (2)
Test steps
  Build the test environment as shown in the previous slide
  Configure the device under test to work in multi-link operation
  Establish a data link between the device under test and the paired device
  Use measurement equipment with real-time spectrum analysis capabilities to ensure that the device under test transmits on the declared operating frequency band
  Use spectrum analyzer to measure the frequency range and out-of-band emission
Notes: ,

## Slide 10: Testing methodologies: EVM (1)
Block diagram:
Notes: ,

## Slide 11: Testing methodologies: EVM (2)
Test steps:
  Connect the device under test to the measurement device with demodulation function through the RF line measuring equipment
  Set the device under test to send 4096 QAM modulated signal
  Measure average EVM test results by the measuring equipment
  The measurement results should meet the above technical requirements
Notes: ,

## Slide 12: Testing methodologies: MRU spectrum mask (1)
Block diagram (the same block diagram as EVM):
Notes: ,

## Slide 13: Testing methodologies: MRU spectrum mask (2)
Test steps:
  Connect the device under test to the test device with demodulation function through the RF line measuring equipment
  Adjust the center frequency of the measuring device to the center of the device under test’s frequency, set RBW to 100 kHz, VBW to 7.5 kHz, and set the detection method to RMS
  Spectrum envelope of the signal emitted by the device under test shall comply with the above-mentioned spectrum mask requirements
Notes: ,