## Slide 1: Proposed Changes to Response 6GHz U-NII FCC Second FNPRM
Date: 17 January 2024
Author:

## Slide 2: References and Links
https://mentor.ieee.org/802.18/dcn/23/18-23-0134-07-0000-draft-response-to-rspg-s-consultation-on-work-programme-for-2024-and-beyond.pdf
https://www.federalregister.gov/documents/2024/02/26/2023-28620/unlicensed-use-of-the-6-ghz-band-and-expanding-flexible-use-in-mid-band-spectrum-between-37-and-24

## Slide 3: Minor Things
Change title to: Proposed Comments on FCC Second Further Notice of Proposed Rulemaking for 6GHz U-NII
Explanation:
  There are three (that I know of) rule parts that authorization unlicensed use of the 6 GHz band, three of which are used by implementations of 802 wireless standards: Part 15.250, 15 Subpart E (U-NII) and 15 Subpart F. As an 802 position we should be accurate that we’re addressing U-NII while acknowledge that standards-based unlicensed use exists via the other rule parts (802.15.4)
Check for other places we need to clarify the different types of unlicensed use

## Slide 4: Less Minor Issues
Summary:
  Agree that Client to Client (C2C) is a good thing.
  Disagree that raising VLP power is a good thing
Explanation (overview):
  Client to Client has many advantages, including reduced overall traffic and potentially using less transmit power when clients are near, reducing interference impact and enabling more VLP devices in a given area and more efficient use of the spectrum.
  Raising VLP power is counter to on of these benefits (maybe both)
  The proposed power levels are inconsistent with current VLP rules for Transmit Power Control (TPC)

## Slide 5: VLP Power Considerations (1)
Explanation (Details):
Benefits of VLP include lower traffic load and potentially less interference
Ability to reduce traffic by not passing every packet through AP is good
  Reduces traffic and potential congestion
  Enables more efficient use of the channel (more useful capacity)
  Reduces overall energy used
  Supports network topologies that can address some use cases much more efficiently
  And reduces interference potential both ways (fewer to step on, fewer to step on others)
Raising VLP power eliminates the last three benefits
  In many scenarios the client devices are closer to each other and in near line of sight so Less power needed than reaching the AP both ways
  The interference footprint is greatly reduced with lower power
    The unintended receiver sphere of influence is smaller
    Which enables more devices in a given space (spatial reuse) and makes everything work better
  Higher power reduces spatial and spectral reuse from the ability to use less power to close the C2C link
  Higher power results in greater interference to and from uncoordinated overlapping networks, resulting in more packet retransmissions and thus undermines the “less traffic” benefit somewhat.

## Slide 6: VLP Power Considerations (2)
Explanation (Details):
The proposed power levels are inconsistent with current VLP rules requiring Transmit Power Control (TPC)
  Currently 6 dB of TPC authority is required (which 802 supported)
  A 24 dBm capable VLP device with dB of TPC would still be 4dB higher than current VLP device at minimum power
  Greatly increases potential for negative impacts and undermines much of the arguments given for VLP in the first place (supporting 14 dBm as safe)
  Negative impact on existing VLP and other users (including 802.15.4 UWB and other systems)
Lower power is always better when you don’t need more
  Unless there’s only 2 devices in the space. Which seldom happens on Earth and never with the use cases we cite
Idea: Suggest amended TPC
  Minimum authority of 16 dB to be equivalent to present VLP (low of 8 dBm)

## Slide 7: VLP Power Considerations (3)
Explanation (Details):
Raising power may undermine prior arguments and requests for more channels
  Arguing that APs must be closer together suggests smaller interference footprint is needed to avoid AP to AP interference, thus we need more channels because the APs interfere anyway and we need more power to make sure of it
  Also contradicts much of the claims we have made for contention based protocol benefits
  Also neglects the many techniques in 802.11 to achieve spatial reuse and improve link distance without more power
If we argue that more channels (e.g. extending U-NII above 7 GHz) requires more power we create an unsustainable situation
  More power requires more channels – more channels requires more power – endlessly?
24 dBm de-differentiates VLP from LPI (2 dB is “very”?)
  Which further undermines the rational we’ve given for VLP: Are we now saying our justification for 14 dBm back in the original record is wrong?

## Slide 8: VLP Power Considerations (4)
Conclusions:
The arguments for more VLP power undermine much of what we’ve argued before
It could be hard to defend moving forward
Does not speak well for 802 as “experts” on coexistence
  Ignores all the other 802 stuff we already have operating in the band:
    Current 802.11 under U-NII VLP rules
    UWB rules (2 parts)
    Other 802.15.4 under U-NII VLP
  Doesn’t include any considerations for coexistence

## Slide 9: Other Things
320 MHz channel limit
  802.11 is already talking about 480 MHz channels
  Might be good to mention while we’re asking for things?
Could use more on how 802 is leading coexistence
  If we don’t someone else will