Presentation Material
- PAR
- 5 Criteria
- ✔	Problem tutorial
  - ✔	Why VoIP doesn't work today
  - ✔	What is needed to fix it
  - ✔	Working with ECRIT should be at least an
    80% solution
- Possible technical concepts

---
TUTORIAL (1)
Why 802 needs an Emergency Services Project and what we think it should look like.
Geoff Thompson/InterDigital
Scott Henderson/RIM
802 ES-ECSG

---
TUTORIAL (2)
SUPPORT OF EMERGENCY SERVICES and THEIR (present and future) REGULATORY REQUIREMENTS FOR PACKET NETWORKS IS A HUGE, COMPLEX PROBLEM FOR WHICH THE PROBLEM ITSELF IS NOT YET FULLY DEFINED.

---
TUTORIAL (3)
There are pieces of the ES problem that:
- Are well defined today
- Have existing regulatory requirements
- Are not addressed across 802.

---
TUTORIAL (4)
The biggest piece:
- 802 originated (and VoIP originated) “calls” to the PSTN don't carry the information required for emergency calls (e.g. 911 calls)
  (There are proprietary exceptions)
- There are existing regulatory requirements for these calls that are not being met.

---
TUTORIAL (5)
The IETF – ECRIT group has taken on the task of solving this problem for the upper layers
802 needs to work with ECRIT to provide a complete solution.
The solution should look the same to ECRIT without regard to which 802 technology is in use.

---
TUTORIAL (6)
Regulatory Requirements:
- Call request directed to the correct PSAP
- Provide calling party location
- Non-subscriber access to network
- PSAP can call back
- Very high priority
- Call integrity (no drop, spoof-proof)

---
TUTORIAL (7)
What does ECRIT need from 802 to meet these requirements?
- Provide better location than just the router
- Emergency calls should be given network priority
- Callback is currently a problem
- Spoofing and security are issues
- Provide LOCAL connection (e.g. bypass various tunneling schemes)
- Provide service to unauthenticated user

---
TUTORIAL (8)
Why VoIP doesn't work today:
- The Internet was designed to be “location neutral”.
- Traditional “911” was designed around and serviced by a localized static wired infrastructure (end office circuit switched systems)
- VoIP services are highly decentralized and often cross national boundaries
  (regulatory problem)

---
TUTORIAL (9)
Why VoIP doesn't work today (cont'd):
- Today, the VoIP service provider has no knowledge of the callers location within the Internet (almost true)
- A PSAP has no prior knowledge that a caller is within their service area.
- Therefore associating caller and proper PSAP is a big problem
- VoIP service provider are not yet fully regulated, there are significant technical, geopolitical and legal jurisdiction problems involved.