## Slide 1: 802 EMERGENCY SERVICES TUTORIAL
Why 802 needs an Emergency Services Project and what we think it should look like.
802 ES-ECSG
Geoff Thompson/InterDigital Scott Henderson/RIM Stephen McCann/RIM for 802.11 Phil Barber/Huawei for 802.16

## Slide 2: Agenda
Introduction Emergency Service ECSG
Presenting for 802.11 - Stephen McCann
Presenting for 802.16 - Phil Barber
Emergency Services EC Study Group
  Presenter 1/Geoff Thompson
  Presenter 2/Scott Henderson
Wrap up
  Q & A
  Straw Polls

## Slide 3: Technical/Regulatory Problem Statement
(US Historical Case) 911 Call Origination Identification: Originally based on the wireline legacy incumbent local exchange carriers' databases of their customers.
The legacy system in its original form was seriously compromised as:
  Local phone service ceased to be dominated by a wireline monopoly.
  Cellular phones became significant. (They had no built-in location mechanism. They also had a weakened sense of just where they wanted to call for 911.)
  VoIP phone services grew. VoIP has no inherent caller or call target physical location knowledge.
  Wireless inherent authentication was weakened.

## Slide 4: Technical Problem Statement
US Regulations require Emergency Service calls:
Be directed to the appropriate PSAP
Carry originating location information
Provide sufficient information for PSAP call-back
Not required but possibly desirable to consider
Subscriber station authentication
Service to unauthenticated users (though not in all countries)
Assured access capability for Emergency Service calls

## Slide 5: FCC Consumer Info Sheet
http://www.fcc.gov/cgb/consumerfacts/voip911.pdf

## Slide 6: (Example:) US Requirement (adapted from: www.fcc.gov / cgb / consumerfacts / voip911.pdf
The US FCC has imposed the following requirement:
All interconnected VoIP providers must automatically provide 911 service to all their customers as a standard, mandatory feature without customers having to specifically request this service. VoIP providers may not allow their customers to “opt-out” of 911 service.

## Slide 7: Requirements: Other countries
Other countries have similar requirements.
There are national differences, especially with respect to:
  Emergency numbers other than “911”.
  See: http://www.sccfd.org/travel.html.
  Some countries have several numbers
  Some countries prohibit location info.
  Other details

## Slide 8: Defined Problem lies in Multiple Domains
IP, routing and higher layer portions of the problem belong to the IETF.
These problems are being addressed primarily by IETF ECRIT.
The below Layer 3 portion of the problem is for 802 to address.
802.11 and 802.16 have already done some explicit work in this area.
Needs to be handled uniformly across 802.

## Slide 9: 802 Problem
IEEE 802 needs a single standard so that IP applications “should” not need to know which 802 MAC is currently being used.
This is envisioned as a “shim layer” that goes between an 802 end station MAC and its upper layer client.
There may be similar pieces required for 802.1 relays to add per-hop location information (may be required for location back-up information when no end-location information is provided).

## Slide 10: “Complex Problem?”
SUPPORT for the full scope of EMERGENCY SERVICES and THEIR (present and future) REGULATORY REQUIREMENTS FOR PACKET NETWORKS IS A HUGE, COMPLEX PROBLEM FOR WHICH THE PROBLEM ITSELF IS NOT YET FULLY DEFINED.
The scope for this project is much smaller and well defined i.e.: Only support VoIP citizen-to-authority calls.

## Slide 11: How Complex?
There are pieces of the ES problem that:
Are well defined today
Have existing regulatory (or derivative) requirements
Are not addressed across 802.

## Slide 12: LOCATION
The biggest piece:
802 originated (and VoIP originated) “calls” to the PSTN don't carry the information required (e.g. location) for emergency calls (There are proprietary exceptions)
There are uncoordinated pieces within some WGs.
There are existing IETF requirements for these ES calls that are not being met.

## Slide 13: More about Location
Why VoIP doesn't work for ES calls today:
The Internet was designed to be “location neutral”.
Traditional “112/911” was designed around and serviced by a localized static wired infrastructure (end office circuit switched systems)
VoIP services are highly decentralized and often cross national boundaries (regulatory problem)

## Slide 14: More about Location (2)
Why VoIP doesn't work well for ES today (cont'd):
Today, the VoIP service provider has no knowledge of the caller's location within the Internet (almost true).
A PSAP has no prior knowledge that a caller is within their service area.
Therefore, associating caller and proper PSAP is a big problem
VoIP service providers are not sufficiently regulated to fully handle the ES problem; there are significant technical, geopolitical and legal jurisdiction problems involved (language too).

## Slide 15: IETF & Emergency Services
The IETF – ECRIT group has taken on the task of solving this problem for the upper layers.
See: ietf.org/dyn/wg/charter/ecrit-charter.html
7 Internet drafts, 7 RFCs
Includes “Requirements”, “Framework” and “Best Current Practices”
See also R. Barnes/Hannes Tschofenig IETF preso: geopriv.dreamhosters.com/esw6/PEACE-Vortrag_v5.ppt

## Slide 16: ECRIT
The IETF – ECRIT group has taken on the task of solving this problem for the upper layers.
802 needs to liaise with ECRIT to
Provide a complete solution that encompasses 802 end networks.
Agree precisely on requirements for 802
The solution should look the same to ECRIT without regard to which 802 technology is in use.

## Slide 17: ECRIT (2)
What does ECRIT need from 802 to meet these requirements?
What might IEEE 802 provide to ECRIT to meet these requirements?
Provide location of and/or to end station.
Offer Layer 1 & 2 element location information
Prefer LOCAL connection (e.g. bypass various tunneling schemes)
Provide service to unauthenticated user (Initiate & handover/callback)
Spoofing and security are issues