## Slide 1: IEEE 802.11 Emergency Services
Stephen McCann, RIM
Slide <number>
Date: 2010-03-15
Authors:
Notes: doc.: IEEE 802.11-10/xxxxr0
January 2010
        Stephen McCann, RIM
Page <number>

## Slide 2: Abstract
Stephen McCann, RIM
Slide <number>
This is a summary of IEEE 802.11 features which assist Emergency Services
Notes: doc.: IEEE 802.11-10/xxxxr0
January 2010
        Stephen McCann, RIM
Page <number>

## Slide 3: IEEE 802.11 overview
An IEEE 802.11 infrastructure by itself cannot ensure that all factors are compatible for an Emergency Service call to actually take place.
The client device may have to register with a call manager (SIP agent or some other signaling endpoint) for the call to be placed successfully.
Different signaling systems such as SIP, H.323, etc., can be deployed for supporting Emergency Service calling.
Higher layers can also verify an Emergency Service call is being placed so that appropriate level of resources can be granted to the emergency call.
Voice endpoints (e.g., non-AP STAs) can use different codecs such as G.711, AMR, and iLBC.
Notes:         <footer>Stephen McCann, RIM
<header>doc.: IEEE 802.11-10/xxxxr0
<date/time>January 2010

## Slide 4: Emergency Calling (IEEE 802.11u)
Stephen McCann, RIM
Slide <number>
Local Emergency Call Number provisioning of STA
STA signaling of Emergency Service to AP
  Expedited bandwidth request
STAs in Open Authentication hotspots, are able to place emergency calls.
STAs without proper security credentials, for secure hotspots, are able to place emergency calls.
  Interworking information element which can be included in association request frames in order to bypass the IEEE 802.1X port at an AP for un-authenticated access to emergency services.
Notes: doc.: IEEE 802.11-10/xxxxr0
January 2010
        Stephen McCann, RIM
Page <number>

## Slide 5: Location Services (IEEE 802.11v)
Stephen McCann, RIM
Slide <number>
Provides both STA and AP location
  Geo (x,y,z)
  Civic (address)
  Accuracy reporting
  Public URI (provides location when de-referenced)
  location MIB
Provides STA motion
Notes: doc.: IEEE 802.11-10/xxxxr0
January 2010
        Stephen McCann, RIM
Page <number>

## Slide 6
IEEE 802 ES SG and IEEE 802.11 held a joint meeting in January 2010. It concluded:
  IEEE 802.11u covers most emergency service MAC requirements
    Access
    Priority
  IEEE 802.11v covers most location requirements
Little need to do anything else.
January 2010 Joint Meeting

## Slide 7: IETF ECRIT
Stephen McCann, RIM
Slide <number>
Features from provided input to the IETF ECRIT document “draft-schulzrinne-ecrit-unauthenticated-access-07.txt”
IETF emergency services architecture assumes that the calling device has acquired rights to use the access network or that no authentication is required for the access network.
Subsequent protocol interactions, location information, learning the address of the PSAP and the emergency call itself are decoupled from the underlying network access procedures.
Document addresses devices which do not have credentials for network access, do not have a VoIP provider or application service provider, or the credentials have become invalid, e.g., because the user has exhausted their prepaid balance or the account has expired.
Notes: doc.: IEEE 802.11-10/xxxxr0
January 2010
        Stephen McCann, RIM
Page <number>

## Slide 8: Emergency Alerts (IEEE 802.11u)
Stephen McCann, RIM
Slide <number>
Notification of emergency alert
  Notification avoids broadcast flood
  Availability of alert transmitted to STA
  Unique hash to identify duplicates
Notes: doc.: IEEE 802.11-10/xxxxr0
January 2010
        Stephen McCann, RIM
Page <number>

## Slide 9: Further work
Stephen McCann, RIM
Slide <number>
Emergency Service provisioning in IEEE 802.11 MESH (11s)
Wake-on-LAN provision (energy saving)
Harmonisation of IEEE 802.11 & IEEE 802.1 location services
Notes: doc.: IEEE 802.11-10/xxxxr0
January 2010
        Stephen McCann, RIM
Page <number>