## Slide 1: TUTORIAL (n)
802.16 support for citizen-to-authority emergency services:
For terminal currently disconnected from the network:
  bit indication during initial network entry to identify that the purpose of a network entry event is to make an emergency services VoIP call
For currently active terminal:
  service encoding to identify that a specific service flow is identified for ES services; reserved for ES
Support for Location Based Services (LBS); GPS based, network based, and GPS with network assist

## Slide 2: TUTORIAL (n+1)
802.16 air interface hooks are only part of a total solution
Need the network component:
  WiMAX Forum, an industry forum implementing the 802.16 air interface, has created an end-to-end specification for ES

## Slide 3: TUTORIAL (n+2)
WiMAX Forum end-to-end spec:
  Uses initial network entry ES service indication bit/active terminal ES flow traffic indication to:
    Bypass full subscription authentication in regulatory environments that require bypass
    Hotline the terminal to a local ES VoIP gateway server to direct the user traffic to the ES service; for INE ES events this is the only permitted service for unauthenticated access

## Slide 4: TUTORIAL (n+3)
WiMAX Forum end-to-end spec:
  Still has limitations
    Limited to specific carrier supported VoIP services
    Supported VoIP services vary across terminals and carriers
    No unified, common VoIP service across all WiMAX networks/terminal form factors (laptop chipset, USB dongle for laptop, workpad, smartphone, SIM based phone, etc…)
    Diversity of terminal form factors confounds common VoIP service solution
    Retail distribution model where operator does not have direct relationship with terminal vendor confounds VoIP service solution

## Slide 5: TUTORIAL (n+4)
WiMAX Forum end-to-end spec:
  Universal VoIP service requires common, certifiable VoIP implementation (default client basic functionality, voice CODEC, session protocol); still in development