## Slide 1
General Security Topics
A dedicated VLAN sidesteps some of the issues associated with security.
Providing location information is forbidden in some countries, mandatory in others.
Provided location information is considered to be sensitive information.
Information integrity across the call is a security issue.
Information needed for call back is considered to be sensitive.
The actual content of the call may be considered to be sensitive.

## Slide 2: Security (2)
The security considerations for ECRIT are put forth in IETF RFC-5069
There are a few problems which seem to be intractable in a wireless environment with unauthenticated users.
Originating call location information from unauthenticated users will be visible (“Hollywood Paparazzi Problem”) unless we encrypt (at least) the over-the-air portion of those calls.
  We believe that the current population of public access points has no way to provide encryption for unauthenticated users.
  We believe that the current population of 802.11 access points has no way to preserve security while switching SSIDs (for further investigation).

## Slide 3: Security (3)
First hop encryption is a significant challenge.
First hop encryption will possibly require changes from the wireless MAC groups.
First hop encryption standardization should not be allowed to delay work on the primary functionality of “getting the call through”.
Establishing first hop encryption should not be allowed to significantly delay the primary functionality of “getting the call through”.

## Slide 4: Issues
U.S. Public safety agency preference is for infrastructure based location over human supplied location and end station based location information.
802.11 service leaking into adjacent properties is a well known problem. That is, the goal is to provide the accurate street address information of the caller as opposed to that of the access point.
802.16 distance and angle measurements are not of sufficient accuracy to meet the requirements E911 & NG911.
Notes: (GPS reliability in cities and inside buildings is a problem, as is spoofing.)

## Slide 5: Issues (2)
Emergency Services and its features are all a contentious technical area, both from a feature/content point-of-view and from a division of work/layer/SDO assignment point-of-view.
Just what are the regulatory requirements (from around the world)?
What technical work needs to be done first/now? (We can't just wait until everything is written in stone to start.)
What pieces will get done:
  in what layer?
  In what SDO?
Getting good answers to all of these is the first task for the group.

## Slide 6: End of “technical presentation”
We can discuss PAR if desired.

## Slide 7: PAR Material
2.1 Title: Standard for Local and Metropolitan Area Networks- Emergency Services for Internet Protocol (IP) Based Citizen to Authority Communications.
5.2 Scope: This standard defines a mechanism that supports compliance within IEEE 802 to applicable civil authority requirements for citizen-to-authority emergency services packet data communications. Specifically, it supports the need for consistent data that is required for citizen-to-authority emergency services packet data encoded session initiation requests. A new MAC or PHY is outside the scope of this effort.

## Slide 8: PAR Material (2)
5.4 Purpose: The purpose of this standard is to support compliance to civil authority requirements complementary to IETF ECRIT specifications for citizen to authority emergency services functionality. This standard intends to encompass voice, data and multi-media requests across IEEE 802 using a new Layer 2 entity and associated behaviors and provide a uniform Structure of Management Information (SMI) for transferring required data for emergency services requests.

## Slide 9: PAR Material (3)
5.5 Need for the Project: VoIP emergency calls are currently less effective than those provided by traditional wireline and cellular networks. Emergency calls across IEEE 802 technologies need to support regulatory requirements to assure successful completion (and all associated requirements) of these calls to the correct Public Service Access Point (PSAP), and to do so utilizing the existing set of IEEE 802 PHYs and MACs.