## Slide 1: Sub-1GHz Coexistence Study Update
March 6, 2018

## Slide 2: History of the Coexistence Study
Presented coexistence issues to 802.15 WNG in September 2017
  1 802.15.4g network and 3 802.11ah networks
  Straw poll indicated that 802.19 WG is proper WG
Made same presentation to 802.19 WG in November 2017
Presented coexistence issues to 802.19 WG in January 2018
  4 node simulation

## Slide 3: Study Purpose and Methodology
Evaluate potential impacts between 802.15.4 SUN (15.4g) and 802.11ah in the sub-1GHz bands used by these standards
  Primarily around 900 MHz
Used simulation based on
  Use cases from 802.15.4g application e.g. smart utility applications
  Use cases from 802.11ah development
  Use cases from previous 802.19 meetings

## Slide 4: Update
Ran additional scenarios suggested in January 802.19 meeting
  Use same data volume for both services
  Use same duty cycle for both services
Presented and discussed in 802.19
  Consensus was to initiate an interest group in 802.19 to for further evaluation, determine if a standards activity should be initiated
Reference: IEEE 802.19-18/0016r0

## Slide 5: Technical Highlights
Both services are significantly impacted by each other under realistic scenarios
  802.11ah impact on 802.15.4g manifests as packet loss
  802.15.4g impact on 802.11ah manifests as latency increases

## Slide 6: Next Steps
Interest Group in 802.19
  Review results so far
  Evaluate use cases and scenarios for further study
  Consider useful standards activities: possibilities could include:
    New project in 802.19 (coexistence methods)
    New projects in 802.15 and/or 802.11 enhancing coexistence properties
    Other?
  IG Output: recommendations to WGs