## Slide 1
OmniRAN Wi-Fi Hotspot Roaming Use Case |  |  | 
Date: 2013-03-17 |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Max Riegel | NSN | +49 173 293 8240 | maximilian.riegel@nsn.com
Notice: This document does not represent the agreed view of the OmniRAN EC SG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
The presentation addresses the deployment of the OmniRAN architecture for the specification of open interfaces for roaming between Wi-Fi hotspot operators.
The possibility to get access to communication services in other service providers’ networks has been one of the main reasons for the overwhelming success of cellular communication and is considered as necessary function also for public Wi-Fi access networks.

## Slide 2: Wi-Fi Hotspot Roaming Use Case
OmniRAN use case contribution
Max Riegel, NSN

## Slide 3: Deployment Domain: Wi-Fi Roaming
Roaming is a well know functionality in cellular networks allowing us to use our cellular phones worldwide without hassle.
Roaming among Wi-Fi hotspots belonging to different operators is seen a prerequisite to further develop Wi-Fi access service to a cellular like experience
Wireless ISPs
AC
3GPP2
MNO
HLR
3GPP
MNO
Home
ISP
Roaming
Broker
Users

## Slide 4: Use case description: Joe’s Seamless Wi-Fi Service
Joe is a road worrier always keen to make best use of the time he has to spend for traveling and sitting around waiting for the next flight or ride. Therefore he has a subscription with a local Wi-Fi service provider which has best coverage throughout his home town due to a phletora of Wi-Fi APs installed in nearly every public place in town including the airport and public transport vehicles, which Joe frequently uses.
As Joe is regularly using Wi-Fi for making phone calls and participating in conference calls, he went for the premium subscription option providing him a priorized traffic path over Wi-Fi to his VoIP provider.
Luckily his Wi-Fi provider is early adopter of the Hotspot 2.0 technology providing not only secured air links but also seamless service experience when moving around in his home town. Due to the many roaming contracts, which Joe’s local Wi-Fi operator has established some major Wi-Fi operator and hugh Wi-Fi roaming consortia, Joe’s seamless Wi-Fi service does not break when he is out of town.
Usually his Wi-Fi devices just automatically connect to available Wi-Fi by making use of the enhanced network detection and selection features of Hotspot 2.0 and the credentials, he got from his Wi-Fi service provider, for automatic log-on. Even more, Joe enjoys the same high quality VoIP connectivity when he is roaming into the networks of the major Wi-Fi operators with direct contracts to his home Wi-Fi service provider.

## Slide 5: Wi-Fi Roaming Scenarios
The following roaming scenarios are considered:
Home operator has roaming agreement with other operator. Traffic is routed via other operator’s core into the Internet
Home operator has roaming agreement with other operator. Traffic is routed back to the home operator’s core network.
Home operator has Wi-Fi access sharing agreement with other operator allowing to serve customers like within the own access infrastructure
Home operator has agreement with roaming consortia which enables to use credentials for access to all other operators’ Wi-Fi access, which belong to the roaming consortia.

## Slide 6: OmniRAN Architecture Mapping
Core
Internet
R1
R3
Terminal
R2
Access
Home Operator
Core
Internet
R3
R5
Access
Other Operator w/ own core
Access
Access Operator
R3

## Slide 7: 1. Home operator has roaming agreement with other operator. Traffic is routed via other operator’s core into the Internet
Core
Internet
R1
R3
Terminal
R2
Access
Home Operator
Core
Internet
R3
R5
Access
Other Operator w/ own core
R2
only control

## Slide 8: 2. Home operator has roaming agreement with other operator. Traffic is routed back to the home operator’s core network.
Core
Internet
R1
R3
Terminal
R2
Access
Home Operator
Core
Internet
R3
R5
Access
Other Operator w/ own core
R2

## Slide 9: 3. Home operator has Wi-Fi access sharing agreement with other operator allowing to serve customers like by the own access infrastructure
Core
Internet
R1
R3
Terminal
R2
Access
Home Operator
Access
Access Operator
R3

## Slide 10: 4. Home operator has agreement with roaming consortia which enables to use credentials for access to all other operators’ networks belong to the roaming consortia.
Core
Internet
R1
R3
Terminal
R2
Access
Home Operator
Core
Internet
R3
R5
Access
Other Operator w/ own core
Core
R5
Roaming Consortia

## Slide 11: Requirements for OmniRAN:
All different flavors of Wi-Fi roaming can be handled with just 2 Reference Points of the OmniRAN architecture:
  R3, when terminal is anchored in the home network
    Default router in the home network
  R5, when terminal is anchored in the visited network
    Default router in the visited network
When terminal is anchored in the visited network, it doesn’t matter for OmniRAN whether traffic is routed back into the home network or not
  Routing is statically configured and independent of terminal attachment
There may be configurations, which require further considerations, but can still be handled by OmniRAN
A Roaming Consortium usually deploys R5 for inter-connection of all the involved operators.

## Slide 12: Conclusion
OmniRAN provides the specifications to establish Wi-Fi Roaming with all its different flavors.
R5 is mainly a AAA interface designed for inter-operator roaming.
R3 can be used when forced traffic forwarding into the home is required.