## Slide 1: Current IEEE 802.1CQ Project status
802.1CQ group
Latest Update: 12/09/2018

## Slide 2: Scenarios
Functional Scenarios
  Stateless/Statefull Assignment of addresses to End-stations
    802.11
    802.3
    VMs/Containers
  Stateless/Statefull Assignment of addresses to Bridges/APs
    Including Assignment of groups of addresses
  Statefull Assignment of pools of addresses to Proxies from Servers
Network Scenario
  Hypervisor scenario
  Container scenario
  WLAN scenario

## Slide 3: Supported functions
Complete Stateless (advertising+DaD)
  Complete and with .1CQ defined prefix (fixed)
Stateless with prefix
Support for Mobility of MAC addresses
  Reuse of an assigned MAC address at a different point of attachment with a different Proxy
  Mechanism to detect if you are in the same LAAP domain (LAN?)
  (more to be added, and way more to be discussed)
Pre-association Discovery in IEEE 802.11
LAAP protocol in wired environment (IETF DHCP extension)
DaD/Wireless DaD
Notes: No mobility for wired devices, as long as the interface is down, MAC address loses validity
Server ID
Proxy should be able to verify a machine has a MAC address belonging to its pool in a proactive way
Maybe have the same protocol at the wired counterpart inside PAD

## Slide 4: Discussion on proposal for LAAP and .11aq
Refer to latest revision of omniran-18-0071-00-CQ00
Do we want to separate the actual service advertise and if it is mandatory or not?
Open questions to check with .11
  What to do if mandatory LAAP needs to be enforcedMAC filtering and blocking at the AP
    Proposal: add informative annex about this
    What do we do with legacy STAs
  Posibility of using different protocols different than ANQP
  What are the src addresses used in GAS? Randomize address?

## Slide 5: Discussion on the Protocol
Security considerations: shall we add an ID and how do we protect from man in the middle.
  Possibly related to liaison regarding randomization of addresses from WBA (https://mentor.ieee.org/802.11/dcn/18/11-18-1579-00-0000-2018-09-liaison-from-wba-re-mac-randomization-impacts.docx)
DoS attacks, consider adding considerations about rate limiting

## Slide 6: Next Steps
As per September 2018:
  Next step is to discuss with .11aq (25th of September AC)
  Present proposal at .11 architecture meeting
  Possibly present on .15 WNG, to gather attention from .15 groups