## Slide 1: MAC address assignment in IEEE 802.11 through IEEE 802.11aq
Date: 2018-11-14
Author:
November 2018
Antonio de la Oliva, IDCC, UC3M

## Slide 2: IEEE 802.1CQ Scope
As defined in the PAR:
“This standard specifies protocols, procedures, and management objects for locally-unique assignment of 48-bit and 64-bit addresses to ports in IEEE 802 networks”
Actually, we are working on mechanisms for the distribution of Local MAC addresses (in the 802c defined SAI space) including stateful and stateless procedures, on a per-technology basis.

## Slide 3: Scenarios
Functional Scenarios
  Stateless/Stateful Assignment of addresses to End-stations
    802.11
    802.3
    VMs/Containers
    802.15 (if expertise appears)
  Stateless/Stateful Assignment of addresses to Bridges/APs
    Including Assignment of groups of addresses
  Stateful Assignment of pools of addresses to Proxies from Servers
Network Scenario
  Hypervisor scenario
  Container scenario
  WLAN scenario

## Slide 4: Motivation for a specific mechanism in IEEE 802.11
MAC address is part of the state information required for the association and security in WLAN
  Any modification of MAC address in WLAN forces a new association and security association establishment
If MAC assignments are required in a given network, it is required to discover the address in pre-association

## Slide 5: Proposal
Use IEEE 802.11aq mechanisms to discover LAAP services and provide MAC address assignment in pre-Discovery state
  Use of Service Hint/Hash to advertise LAAP service
  Use new protocol within Service Information Request/Response Element in IEEE 802.11aq modified ANQP to negotiate MAC address
Advertisement of MAC address allocation plans can be done through pre-association Discovery.
Assignment of MAC addresses using LAAP, would require changes to IEEE 802.11 authentication and association procedures.
  Security association is established with IEEE 802.11 authentication with FILS and SAE.
  Security association is established after IEEE 802.11 association with RSN (IEEE 802.1X)

## Slide 6: IEEE 802.11 MAC assignment service
IEEE 802.11aq defines two mechanisms for the distribution of information about services available
  Service Hint: The Service Hint element provides a probabilistic representation of a set of services that are available to the BSS (Bloom filter).
  Service Hash: The Service Hash element contains one or more service hashes.
How to compute both is defined in Clauses 11.25a.4 and 11.25a.5 of IEEE 802.11aq
Proposal:
  Define the following service names following RFC6335
    Ieee-8021cq-LAAP-server
    Ieee-8021cq-Self-Assignment
    Ieee-8021cq-Self-Assignment-with-prefix
    Ieee-8021cq-LAAP-server-optional
  PAD-enabled STA will advertise the above services when available

## Slide 7: Exchanging messages with the LAAP Proxy ServerArchitecture

## Slide 8: Exchanging messages with the LAAP Proxy ServerProtocol
Need to define a new secure protocol on top of Authentication/Association, coupled with IEEE 802.1CQ
Value | Description
0 | Request
1 | Rebind
2 | Response
3-255 | Reserved

## Slide 9: Backup

## Slide 10: Exchanging messages with the LAAP Proxy ServerProcedure (.11aq compatible)
Although not secure maybe useful for self-configured addresses in a pool