## Slide 1: Investigating the Multicast Usage Model for P802.1CQ
Roger Marks (EthAirNet Associates)
2019-01-24

## Slide 2: Multicast for P802.1CQ: History
The initial P802.1CQ draft PAR was "Local Addresses Assignment”
Later, it was changed to "Multicast and Local Address Assignment"
As I recall, the TG Chair stated that there was a need to add multicast address assignments for TSN streams.
Nothing about multicast was added to the Scope, or to the CSD.
The following text added to the Purpose:
  Multicast flows also need addresses to identify the flows. They will benefit from a set of protocols to distribute multicast addresses.

## Slide 3: Multicast for P802.1CQ: History
IEEE 1722-2011 ("Transport Protocol for Time-Sensitive Applications in Bridged Local Area Networks") includes specification of the "MAC Address Acquisition Protocol" (MAAP) that seems intended for this purpose.
  1722 was revised in 2016
MAAP is not referenced in 802.1Q, 802.1BA, or 802.1CA
  although 802.1Q cites IEEE 1722
  MAAP was mentioned in some 802.1 contributions (2008 and 2009)

## Slide 4: Multicast for P802.1CQ: History
Avnu (based on 802.1 TSB) uses 1722 MAAP:
  Multicast MAC addresses or locally administered unicast addresses are required by AVTP for the transmission of media streams. Because AVTP runs directly on a layer 2 transport, there is no existing protocol to allocate multicast MAC addresses dynamically. MAAP is designed to provide a way to allocate dynamically the multicast MAC addresses needed by AVTP. MAAP is not designed to allocate locally administered unicast addresses.
    “AVNU Milan Network redundancy interoperability specification”
    June 5, 2018 Revision 1.3

## Slide 5: Discussion with TSN Chair
I discussed this with TSN Chair.
He noted that multicast MAC addresses are part of the Stream ID in Audio Video Bridging
  inherited by TSN
  has been developed further by 802.1CB
  P802.1CBdb will add further possibilities
TSN Chair recommended that we ask TSN for views.

## Slide 6: Questions for TSN
From a TSN perspective, is there a need to specify multicast address assignment beyond the IEEE 1722 MAAP?
If so, could we discuss a way forward to reach an understanding of the usage model and requirements?
If not, should P802.1CQ simply include suitable references to IEEE 1722?