## Slide 1
WiFi Privacy network experiment at IETF91 |  |  | 
Date: [2015-01-13] |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Carlos Jesús Bernardos | UC3M |  | cjbc@it.uc3m.es
Fabio Giust | UC3M |  | fgiust@it.uc3m.es
Antonio de la Oliva | UC3M |  | aoliva@it.uc3m.es
Juan Carlos Zúñiga | InterDigital |  | JuanCarlos.Zuniga@InterDigital.com
Notice: This document does not represent the agreed view of the IEEE 802 EC Privacy Recommendation SG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
The present document reports on the trial performed at IETF91 and presents some results

## Slide 2: Experiment goals
Carry out a Wi-Fi MAC randomization trial/experiment at IETF91
  Evaluating support of different OSes (Windows, Mac OS X and Linux)
  Analyzing the impact of L2 address randomization on the user experience and the network infrastructure
    Specially in case of L2 address collision
  Learn from this initial experience so we can gather further information in subsequent trials

## Slide 3: Network setup
A specific SSID (ietf-PrivRandMAC) was deployed on the wireless IETF Internet infrastructure
  Deployed on all IETF physical APs, as an additional virtual AP
  WPA PSK security, to avoid non participants to accidentally connect to our trial WLAN
  Connected via a different VLAN to the DHCP server and Internet gateway
    Provides certain isolation to the rest of the infrastructure
    Isolated pool of IPv4 addresses

## Slide 4: Trial setup
Participants were asked to notify their participation to a mailing list (ietf91-mac-privacy@ietf.org)
WLAN address randomization scripts developed and provided for 3 different OSes:
  Microsoft Windows (tested on Windows 7)
  Apple Mac OS X (tested on Version 10.10, alias Yosemite)
  GNU Linux (tested on Debian testing/unstable, Ubuntu 13.10, and Fedora 20)
Use of DHCP client identifier for debugging
https://www.ietf.org/registration/MeetingWiki/wiki/91privacy

## Slide 5: Participants’ statistics
Participation increased significantly throughout the week
  Around 3x at the end of the week (Mon-Thu)
OS distribution
Chart: 
| Windows | Mac OS X | Linux
 | 0.066667 | 0.53333 | 0.4

## Slide 6: DHCP logs
685 Local MACs seen during the week
  631 Local MACs were seen on the trial’s WLAN network
  125 Local MACs were also seen on regular IETF WLAN networks
Based on the number of non-Local MAC seen on the trial’s WLAN and other metrics (e.g., # different IP addresses allocated and DHCP hostnames provided) we estimate that between 50 and 100 people participated in the trial
  Method for better keeping track the number of participants should be provided in the future (e.g., use of IEEE 802.1X access setup)

## Slide 7: IP address assignments
542 IP addresses were assigned to Local MAC addresses
  530 IP addresses assigned to a single Local MAC address
    E.g., because no DHCP client ID was used by the client
  12 IP addresses assigned to multiple Local MAC addresses
Chart: # MAC addresses for IP address
| 130.129.20.221 | 130.129.20.236 | 130.129.20.240 | 130.129.20.241 | 130.129.20.242 | 130.129.22.231 | 130.129.22.233 | 130.129.22.234 | 130.129.22.241 | 130.129.22.248 | 130.129.22.249 | 130.129.22.251
# MAC addresses associated to a single IP address | 5 | 12 | 3 | 2 | 3 | 2 | 38 | 9 | 4 | 8 | 10 | 5

## Slide 8: Lifetime of Local MACs
Hard to estimate based on available logs
Most of the Local MACs (575) never tried to renew the DHCP lease
Only 56 Local MACs tried to renew the lease/obtain a new IP
  This might have been caused by a change of AP/WLAN network, or a suspend/wake-up, etc
    Impact of the OS and user behavior
  Max between first and last DHCP exchanges: 41 hours 51 min 41 sec
  Average: 4 min 46 sec

## Slide 9: Next steps
Prepare a “wish list” for network administrators of future trial experiments
  Logged information: we are working on potential additional logs that would help us getting more precise information
  Access setup: use IEEE 802.1X to easily track the participation
  Increased frequency poll of logs at the routers (netdisco)
  Decrease DHCP lease time
    Pros: better estimation of the lifetime of a Local MAC address
    Cons: harder to evaluate the number of participants (though this could be improved with a different access setup)
    Does a 1h lease time provide a granularity good enough?
Prepare address randomization tools for more platforms/OSes, including mobile ones (e.g. Android)
Make a more detailed study of collision effects under different scenarios