## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Some Expectations for THz
Date Submitted: 18 July 2011
Source: Rick Roberts, Intel Labs, richard.d.roberts@intel.com
Abstract: This document poses some expectations for THz as an emerging technology
Purpose: Kick-off of a living document that captures THz expectations
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Question: What makes a successful emerging communications technology?
Opinion: It needs to solve a “real problem” in an optimal manner.
Rhetorical Question: What are the expectations for THz?
Rick Roberts, Intel Labs

## Slide 3
An example of an expectation: Let’s consider a wireless version of IEEE802.3ba … 40Gb/s and 100Gb/s ethernet
Possible solutions:
a) 60 GHz
  actually lacks the bandwidth without going to extreme bps/Hz ratios
  based upon 2 GHz bandwidth, the ratio is respectively 20 bps/Hz and 50 bps/Hz
b) THz
  potentially has the RF bandwidth
  demod electronics bandwidth is problematic
  needs coherent detection, square law detector severely limits range
c) Infrared
  has ample RF bandwidth
  demod electronics bandwidth is problematic
  coherent detection is complex, square law detector severely limits range
Rick Roberts, Intel Labs

## Slide 4
Coherent Detector vs. Square Law Detector
The power transfer function for a coherent detector is Watt / Watt
The power transfer function for a square law detector is Watt / Watt2
Comparison of propagation path loss
  Coherent Detection: 20*log10(D)
  Square Law Detection: 40*log10(D)
Rick Roberts, Intel Labs

## Slide 5
Resulting expectations for THz
1. Expected to support coherent demodulation
2. Expected that MODEM electronics must be able to support the bandwidth
3. Expected that the resulting modulation rates exceed what is already available
Rick Roberts, Intel Labs