8.1 Overview and History
IEEE 802 has included universally unique addresses from initial drafts of its early standards. Over the decades, terminology has evolved and the need and uses of unique identifiers has expanded beyond use as universally unique addresses. The IEEE Registration Authority (IEEE RA) supports the creation of Extended Unique Identifiers (EUI) and defines two lengths: EUI-48 and EUI-64. A universal address in canonical representation (see Annex C) is an EUI-48 or an EUI-64.
For many years, the only way for an equipment manufacturer to create EUIs was with an Organizationally Unique Identifier (OUI). An OUI is a three octet (24 bit) value assigned by the IEEE RA to an organization. An OUI assignee appends a unique three-octet value to create an EUI-48, or five-octet value to create an EUI-64, or two octets to create a Protocol Identifier. 48-bit based addressing is required if interoperability through bridges is required for a standard (typically using EUI-48 universally unique addresses. New standards that only require routed connectivity should use 64 bit addressing and EUI-64.
IEEE 802 also allows addresses to be locally administered as well as supporting multicast addresses. This is done by special use of two bits of the first byte of an address as shown in Figure 9.
Figure 9—Structure of an OUI
The LSB of the first octet may be set to one or zero depending on the application. The next-to-LSB of the first octet is zero for all universal addresses. The remaining 22 bits of the OUI are as assigned by the RAC. Uses other than addresses where only 22 bits of the OUI are used are deprecated.
Because the assignment of the OUI in effect reserves a block of derivative identifiers (i.e., blocks of EUI-48s, EUI- 64s, group addresses, and protocol identifiers), the number of addresses that can be derived from an OUI is large (~16 million EUI-48s). Not all companies need this many EUIs, and consequently the IEEE RA now offers smaller sizes of address blocks. These smaller address blocks allow similar creation of EUI-48s and EUI-64s, but the assignee may not use the first three octets of the assignment as a unique identifier for their organization.
The universal administration of MAC addresses began with the Xerox Corporation administering Block Identifiers (Block IDs) for Ethernet addresses. Block IDs, referred to as OUI by the IEEE, were assigned by the Ethernet Administration Office and were 24 bits in length. An organization developed addresses by assigning the remaining 24 bits. For example, the address as represented by the six octets P-Q-R-S-T-U comprises the Block ID, P-Q-R, and the locally assigned octets S-T-U.
The IEEE, because of the work in IEEE 802 on standardizing networking technologies, has assumed the responsibility of defining and carrying out procedures for the universal administration of OUIs. The IEEE has also been designated by ISO/IEC to act as the registration authority for the ISO/IEC 8802 series of standards.
The responsibility for defining the procedures for OUI usage is discharged by the IEEE Registration Authority Committee (RAC), which is chartered by the IEEE Standards Association Board of Governors. In IEEE 802 networks, the term MAC address may mean EUI-48, or it may not as only universally unique MAC addresses can properly be referred to as an EUI-48. The same principle holds for use of EUI-64. In some IEEE 802 standards, the term extended address refers to EUI-64.