## Slide 1: IEEE 802 EC 5G / IMT-2020 Standing Committee Report
Glenn Parsons - Ericsson
glenn.parsons@ericsson.com +1 613 963 8141
July 2016

## Slide 2: Table of Contents
2
Introduction
Authorized Scope
Views of 5G
Actions Considered
  A. IEEE “5G”
  B1. IMT-2020 – single technology
  B2. IMT-2020 – set of technologies
  B3. IMT-2020 – external proposal
Conclusions
Next Steps
Appendices
  Appendix 1: Authorization by EC Ballot
  Appendix 2: Meeting History
  Appendix 3: Process
  Appendix 4: Cost/Benefit Approach
  Appendix 5: Relevant IEEE 802 Standards and Projects

## Slide 3: Introduction
3
The IEEE 802 EC 5G/IMT-2020 Standing Committee was chartered (Feb - July 2016) by EC ballot
  see Appendix 1
Glenn Parsons served as Chair
The Standing Committee held face-to-face and electronic meetings
  see Appendix 2
      documents:
        https://mentor.ieee.org/802-ec/documents?is_group=5GSG
      Standing Committee web site:
        http://ieee802.org/Stand_Com/5G
This document provides the requested report

## Slide 4: Authorized Scope
4
To provide a report on the following items to the EC:
  Costs and benefits of creating an IEEE 5G specification
  Costs and benefits of providing a proposal for IMT-2020, considering possible models of a proposal:
    as a single technology,
    as a set of technologies,
    or as one or more technologies within a proposal from external bodies (e.g., 3GPP)
During its lifetime, to act as the communication point with other IEEE organizations on this topic.

## Slide 5: Views of 5G
5
5G is understood many ways.
Facets that distinguish 5G may include:
  Technology: radical new technologies or technology sets
    could include spectrum-related technology issues
      millimeter wave spectrum
      technologies designed for unlicensed use
  Service: provides new services or new service sets
  Performance: new levels of performance to users, or to operators
  Operator ecosystem, either:
    next step for the existing 2G/3G/4G incumbent mobile operators
    an opportunity for new operators
  Standards: set of interoperability standards rolled out by an ecosystem according to a roadmap
  Other Characteristic: a marketing label, a revolution, etc.
Scope of an “IEEE 5G specification” would likely differ from scope of other 5G endeavors.

## Slide 6: 5G Context for this study
6
Action A: creating an IEEE 5G specification
  could support incumbent mobile operators
    via existing cellular ecosystem
  could support new operators
    creation/support of new ecosystems
      this might be a very different 5G
      would need to identify requirements
  could do both
Action B: providing a proposal for IMT-2020
  supports the 5G of the existing cellular ecosystem
  usage scenarios and requirements specified in IMT-2020 process
    802 could help shape requirements (needs to act soon)
Actions A and B are not contradictory or exclusive

## Slide 7: IMT-2020 (per ITU-R M.2083)
7

## Slide 8: Cost benefit analysis of options/actions
8

## Slide 9
Action A: IEEE “5G” specification
Candidate Approach
• specify an 802 access network
  could be based on P802.1CF
    “network reference model defines a generic foundation for the description of IEEE 802 access networks, which may include multiple network interfaces, multiple network access technologies, and multiple network subscriptions, aimed at unifying the support of different interface technologies, enabling shared network control and use of software-defined networking (SDN) principles”
  provides an external view into general 802 access network
  could support many 802 MACs and PHYs
  could plug into incumbent mobile operator networks
    for example, expand the notion of LWA so that the cellular network supports 802 rather than 802.11
    gives 802 a strong supporting role in cellular 5G networks
  could support integration into other operator networks
    e.g. cable TV or fixed telecom
    gives 802 a central role in non-cellular 5G networks
  feasible for 802 access network to support both
  need not promote it as an “IEEE 5G” network
9

## Slide 10
P802.1CF Interface option to 5G
10
Source: IEEE 802-EC-16-0083-00-5GSG

## Slide 11: Action A: Routes to success 802 Access Network
11
engage with 3GPP to specify interface details
  could support many 802 MACs and PHYs
engage with other parties to specify interface details
  build partnership with other operator communities
support internationalization
  standardize within partner communities
  standardize in JTC1
  standardize in ITU-R (WP 5A) in support of spectrum needs
    WP 5A: “Land mobile service excluding IMT”
    refer to WP 5A’s “Guide to the use of ITU-R texts relating to the land mobile service, including wireless access in the fixed service”
  could standardize in ITU-R IMT-2020 (see Action B)

## Slide 12: Action A: Possible partners 802 Access Network
12
IEEE
  Communications Society standards activities; e.g. IEEE 1904 Access Networks Working Group
3GPP
ITU-R (WP 5A; WP 5D)
IETF, Broadband Forum, CableLabs, MEF, ETSI BRAN, Open Networking Foundation, Wi-Fi Alliance, ZigBee Alliance, Ethernet Alliance, WiMAX Forum, CPRI, …

## Slide 13
Action A – IEEE 802 Access Network
13
Objective
Adoption of IEEE 802 Access Network specification in multiple disparate operator networks.
Strength | Weakness | Opportunity | Threat
1. Builds on traditional 802 presentation of interface to support many networks | 1. Could require compromises in the support of any specific network | 1. Can be applied in both 3GPP networks and in alternative networks | 1. Coordination efforts required– may not be accepted
2. Enhances interoperation with identified end-to-end networks | 2. Requires liaison activity to coordinate interface requirements. | 2. Offers an advantage for end-to-end networks to use 802 | 2. Specifications may come too late or under-perform
3. Could be leveraged to promote spectrum for non-IMT systems; e.g. WAS | 3. May require development of uses cases and requirements | 3. Increases value of the entire range of 802 MAC/PHYs; could support spectrum expansion | 3. Non-802 technologies may be used at the specified interface
Description
Specify an IEEE 802 Access Network, incorporating IEEE 802 MAC/PHYs and supporting standards, with a unified interface to end-to-end networks. Promote standardization of the integration of the IEEE 802 Access Network into end-to-end networks.
Cost | Benefit
IEEE 802 needs to develop Access Network spec; 802 MAC/PHYs may need to develop new amendments; external ecosystems need to be developed | Makes IEEE 802 the central player in heterogeneous access and in access networks for 5G of all forms; IEEE has no responsibility to specify end-to-end

## Slide 14: Action B: IMT-2020 proposal Candidate Approaches
14
B1: Direct IMT-2020 – single technology
  Develop and submit an IEEE proposal to adopt some IEEE 802.11 radio interface technology into IMT-2020 RIT.
B2: Direct IMT-2020 – set of technologies
  Develop and submit an IEEE proposal to adopt coherent set of IEEE 802 radio interface technologies into IMT-2020 RIT, possibly integrated in an IEEE 802 Access Network.
B3: IMT-2020 – external body proposal
  Support development of a 3GPP proposal incorporating references to the use of IEEE 802.11, or an IEEE 802 Access Network.

## Slide 15: Action B1: single technology Candidate Approach: more detail
15
IEEE 802.11 radio interface technology based on IEEE P802.11ay
  Addressing eMBB usage scenario
  Targeting indoor hotspot test environment

## Slide 16: Action B3: external partner proposal Candidate Approach: more detail
16
Support development of a 3GPP proposal incorporating reference to the use of IEEE 802.11, or an IEEE 802 Access Network.
Reference 802 network presumed to operate in non-IMT bands
  for example, 802.11ax in 5 GHz bands, 802.11ay in 60 GHz, etc.
  for example, evolution of LWA, eLWA, LWIP
  would not be proposed as IMT-2020 RIT
Does not preclude parallel action B1 or B2 to propose IMT-2020 RIT
Serves as a feature enhancement to 3GPP network operation
  not evaluated against IMT-2020 technical requirements
  3GPP meets IMT-2020 technical requirements with 3GPP SRIT
  requires technical analysis to select appropriate architectural models for integration with 3GPP network
    Identify Interfaces to IEEE 802 technologies
  requires coordination with 3GPP on details

## Slide 17: Potential 3GPP NextGen Core & New RAT
3GPP is developing a new 5G “New RAT” (NR) and a new 5G Core Network (“NextGen Core”)
Several candidate architectures might allow 802.11 integration into 3GPP 5G network, e.g.:
(1) 802.11 WLAN interfaces directly to NextGen Core
(2) 802.11 WLAN interfaces with NR base station, e.g., similar to “dual connectivity” architecture used by LWA/eLWA/LWIP
[see R2-163969]
(3) 802.11 WLAN data plane interfaces with NR base station, while control plane interfaces with NextGen Core
Source: IEEE 802-EC-16-0099-01-5GSG

## Slide 18: Integration of 802.11 in 3GPP 5G networks
Different architectures may suit different operator deployments and use cases, e.g.
  Some architectures imply increased load on backhaul
  “Dual connectivity” architectures may not allow for macro coverage if NR base station operates at higher frequency than WLAN
Availability of specifications for the different architectures depends on future 3GPP progress, decisions and specification timeline
  Out of the control of IEEE
Commercial deployment of the different architectures depends on handset vendor roadmaps, cellular infrastructure vendor roadmaps and network operator decisions
  Out of the control of IEEE
Any technical activities for 5G undertaken by 802 should focus on enablers / building blocks / interfaces that are as generic as possible and can be utilized by any architecture.
  Consider gap analysis for any necessary specification work

## Slide 19
Action B1 – IMT-2020 proposal,
single technology
19
Objective
IMT-2020 recognition for some IEEE 802.11 radio interface.
Strength | Weakness | Opportunity | Threat
1. An 802.11 radio interface can be recognized as IMT-2020 | 1. Difficult application process; may require new standards to meet requirements | 1. IMT-2020 recognition can add marketing value | 1. May become more difficult to convince regulators to identify more RLAN spectrum
2. Allows independent IEEE proposal | 2. Requires 3GPP to agree to merge result into a SRIT | 2. Allows 802.11 to optimize proposal | 2. 3GPP may prefer alternative and may not agree
3. Allows IEEE to propose use of unlicensed technology for IMT | 3. Unclear how technologies built for unlicensed use would fit into IMT spectrum | 3. IMT recognition can promote use of that 802.11 radio interface in IMT spectrum | 3. RIT simulation modeling required by ITU-R may fail to produce convincing results
Description
Develop and submit an IEEE proposal to adopt some form of IEEE 802.11 radio interface technology into IMT-2020.
Cost | Benefit
Developing standards, preparing and pitching proposal, developing administration support, supporting evaluations, negotiating SRIT, perpetual maintenance | Marketing value. Possibility of better access to spectrum, particularly by targeting a specific segment of new mm-wave spectrum to be identified for IMT

## Slide 20
Action B2 – IMT-2020 proposal,
set of technologies
Objective
20
Objective
IMT-2020 recognition for several IEEE 802 radio interfaces.
Strength | Weakness | Opportunity | Threat
1. 802 radio interfaces can be recognized as IMT-2020 | 1. Difficult application process; may require new stds, and internal coordination, to meet requirements | 1. IMT-2020 recognition can add marketing value | 1. May become more difficult to convince regulators to identify more 802-friendly spectrum
2. Allows independent IEEE proposal | 2. Requires 3GPP to agree to merge result into a SRIT | 2. Allows 802 to optimize proposal | 2. 3GPP may prefer alternative and may not agree
3. Allows IEEE to propose use of unlicensed technology for IMT | 3. Unclear how technologies built for unlicensed use would fit into IMT spectrum | 3. IMT recognition can promote use of those 802 radio interfaces in IMT spectrum | 3. RIT simulation modeling required by ITU-R may fail to produce convincing results
Description
Develop and submit an IEEE proposal to adopt coherent set of IEEE 802 radio interface technologies into IMT-2020, possibly integrated in an IEEE 802 Access Network.
Cost | Benefit
Developing standards, preparing and pitching proposal, developing administration support, supporting evaluations, negotiating SRIT, perpetual maintenance | Marketing value. Possibility of better access to spectrum, particularly by targeting a specific segment of new mm-wave spectrum to be identified for IMT

## Slide 21
Action B3 – IMT-2020 proposal,
external proposal
21
Objective
3GPP incorporation of IEEE 802 features, referenced in IMT-2020.
Strength | Weakness | Opportunity | Threat
1. IEEE 802 technologies are referenced in IMT-2020, aligning with industry momentum | 1. 3GPP would make the final decisions about the details of the proposal | 1. Encourages use of IEEE 802 in 3GPP 5G networks | 1. Focus on 3GPP may reduce applicability of 802 radio interfaces to non-cellular networks
2. No need for IEEE 802 radio interfaces to meet IMT-202o requirements or be evaluated in ITU-R WP 5D | 2. IEEE 802 radio interfaces are not identified as IMT-2020 and are not applicable to IMT spectrum, including future mm-wave IMT spectrum | 2. A peripheral role in IMT-2020 | 2. IEEE 802 radio interfaces would be in a weaker position than IMT-2020 radio interfaces for IMT spectrum, including future mm-wave IMT spectrum
3. align with industry momentum |  | 3. 3GPP includes IEEE 802 technology autonomously with minimal effort from IEEE 802 | 3. 3GPP changes IEEE 802 functionality
Description
Support development of a 3GPP proposal for IMT-2020 incorporating references to integration of IEEE 802.11 or an IEEE 802 Access Network.
Cost | Benefit
Development of the interface, and coordination with 3GPP on integration of the interface | Encourages use of IEEE 802 in 3GPP 5G networks; aligns with industry momentum.

## Slide 22: Proposed Approach – 2 prongs:
Action B3: Ensure relevant IEEE 802 technologies are part of the incumbent mobile operator 5G universe
  Complementary - Propose we recommend only world class winning technologies that already have a foothold in mobile community to ensure credibility with 3GPP.
  Focus on some specific use cases/test environments, e.g. in-home entertainment, indoor hotspot, outdoor hotspot, community
  Liaise with 3GPP as the Release 13/14 features and specifications evolve into Release 15/16/NR/…
    IMT-2020 requirements will evolve in ITU-R and need to be tracked
    IEEE deliverables must ensure that a 5G network including 3GPP and IEEE technologies support the appropriate IMT-2020 requirements
Action A: Ensure IEEE 802 technologies interface with networks of new wireless operators as well as incumbent mobile operators

## Slide 23: Next Steps
23
Actions toward B3 (for Mobile Incumbents)
  Encourage review and technical analysis within the WGs
  “Exploring further involvement of IEEE in this work should be initiated by liaison to 3GPP”
    Suggested by 3GPP representatives in IEEE 802-EC-16-0065-10-5GSG
Actions towards A
  Encourage review and technical analysis within the WGs
  Consider a common interface with Action B3
Identify those who will actually perform the Actions

## Slide 24: Summary, Conclusion & Next Steps

## Slide 25
Summary
25
The Standing committee benefitted from a wide breadth of contributions and views that helped derive the cost-benefit analysis and conclusion of this report.

## Slide 26
Conclusions
26
The four Actions addressed under the Standing Committee scope are not mutually exclusive.
There is a preference for Action B3, with a secondary desire to progress Action A.
  This is confirmed by the straw poll results (25 July) presented on following slide.

## Slide 27
Straw Poll Results – 25 July
27
Support the following Actions (Chicago rules)
  A: 30
  B1: 6
  B2: 2
  B3: 46
  None: 6
Preference for one Action
  A: 22
  B1: 0
  B2: 0
  B3: 29
  None: 2

## Slide 28: Recommendation: Next Steps
Declare success and disband 5G SC
Action A
  Organized by 802.1 WG (Industry Connections project)
Action B3
  Organized by 802.11 WG (Liaison with 3GPP)
Spectrum issues handled by 802.18
Joint 802.1/802.11 meetings as necessary for coordination of actions A & B3

## Slide 29
Straw Poll Results – 26 July
29
Support the Next Steps Recommendation
  40 Yes
  0 No
  ~10 Did not vote
Commit to participate in the development of action A
  13
Commit to participate in the development of action B3
  13

## Slide 30: Appendices

## Slide 31
Appendix 1:
Authorization by EC Ballot
Motion: Approve the creation of the IEEE 802 5G/IMT-2020 standing committee (per 5.6 2 of the LMSC P&P) with the following scope and organization:
To provide a report on the following items to the EC:
  Costs and benefits of creating an IEEE 5G specification
  Costs and benefits of providing a proposal for IMT-2020, considering possible models of a proposal:
        as a single technology,
    as a set of technologies, or as one or more technologies within a proposal from external bodies (e.g., 3GPP)
During its lifetime, to act as the communication point with other IEEE organizations on this topic.
Organization: The committee is chartered for 6 months (i.e., due July 2016 at the 802 plenary) as an EC SC (type 2). Any 802 WG voting member may participate as a voting member of the committee.
Start of ballot: Monday January 25, 2016
Close of ballot: February 4, 2016 11:59PM AOE
31

## Slide 32
Appendix 2:
Meeting History
March 30 – 10am ET
April 13 - 10am ET
April 20 – 6pm ET
April 27 – 10am ET
May 11 – 10am ET
May 20 – 1-4pm HAST
May 25 – 9-12 CEST
June 1 – 10am ET
June 8 – 6pm ET
June 15 – 10am ET
June 24 – 9-12 ET
June 29 – 6pm ET
July 20 – 10am ET
July 25 & 26
32

## Slide 33
Appendix 3: Process
33
Discuss options
  Applicable to the four actions to be analyzed
Include and describe at least one Candidate Approach to each proposed action
Expand cost/benefit for each
Standing Committee conclusions
  Straw-poll views on the possible actions
  Recommend way forward for preference
  Consensus sought

## Slide 34
Appendix 4: Cost/Benefit Approach
34
Provide requested cost-benefit analysis
  But without monetary cost, only relative costs
  Strengths, Weaknesses, Opportunities and Threats
Brainstorm all costs and benefits
  e.g., resource cost, standards development cost, installation cost, operational cost, energy cost, etc.
  Are there unexpected costs?
  Are there unanticipated benefits?
Estimate value relative to a baseline

## Slide 35
Appendix 5: IEEE 802 Standards or Projects of Possible Relevance
35
802.1
  P802.1CF – OmniRAN architecture
  P802.1CM – TSN for Fronthaul
802.3
802.11
  P802.11ax – high aggregate throughput. High density of users.
  IEEE Std 802.11ad – high individual throughput, short range
  P802.11ay – next generation of 802.11ad
  P802.11ah - <1 GHz for IoT requirements
802.15
  P802.15.3d
  100Gb/s THz project
  P802.15.7 REVa, Optical Wireless Communications
  P802.15.4 family
802.16
  802.16
  802.16.1
802.21
  P802.21.1