## Slide 1: IETF Sidemeeting: Large Scale Data Center HPC/RDMA
Paul Congdon (Tallac Networks)
Notes: 1. Current congestion control in RoCEv2 (ECN):
- Packets are just marked, based on a queue threshold
- Long notification delays: packets have to reach destination, be processed at the NIC, NIC has to send notification to the source NIC 2. Consequences:
- Closed-loop control system with long delay in the feedback chain - By the time the source NIC reacts, the congestion tree has grown significantly - Reaction based on possibly obsolete information - Overreaction due to delayed notifications - Oscillations in the injection rate ---> Low throughput 3. How can we improve it? - By providing more detailed feedback from the switches - By distinguishing in-network from incast congestion - By speeding up notifications - By implementing fast-response mechanisms in the switches 4. More detailed feedback - More accurate detection of packets really contributing to congestion (separate them from victim packets) - Record accumulated packet delay in the packet headers and include this information in the notifications

## Slide 2: IETF Note Well https://www.ietf.org/about/note-well/
This is a reminder of IETF policies in effect on various topics such as patents or code of conduct. It is only meant to point you in the right direction. Exceptions may apply. The IETF's patent policy and the definition of an IETF "contribution" and "participation" are set forth in BCP 79; please read it carefully.
As a reminder:
By participating in the IETF, you agree to follow IETF processes and policies.
If you are aware that any IETF contribution is covered by patents or patent applications that are owned or controlled by you or your sponsor, you must disclose that fact, or not participate in the discussion.
As a participant in or attendee to any IETF activity you acknowledge that written, audio, video, and photographic records of meetings may be made public.
Personal information that you provide to IETF will be handled in accordance with the IETF Privacy Statement.
As a participant or attendee, you agree to work respectfully with other participants; please contact the ombudsteam (https://www.ietf.org/contact/ombudsteam/) if you have questions or concerns about this.
Definitive information is in the documents listed below and other IETF BCPs. For advice, please talk to WG chairs or ADs:
BCP 9 (Internet Standards Process)
BCP 25 (Working Group processes)
BCP 25 (Anti-Harassment Procedures)
BCP 54 (Code of Conduct)
BCP 78 (Copyright)
BCP 79 (Patents, Participation)
https://www.ietf.org/privacy-policy/ (Privacy Policy)

## Slide 3: Join us for further discussion
Side Meeting: Monday 8:30AM – 9:45AM – Notre Dame
  NOTE on side meetings:
    Open to all
    Meeting minutes will be publicly posted
    Not under NDA of any form
  Remote participation is available:
    https://zoom.us/j/294652109
    Dial by your location
      +1 669 900 6833 US (San Jose)
      +1 646 876 9923 US (New York)
    Meeting ID: 294 652 109
    Find your local number: https://zoom.us/u/aeo5yUZXgm

## Slide 4: Agenda
Welcome – Paul Congdon – 5 mins
Strategies to drastically improve congestion control in high performance data centers: next steps for RDMA - Jesus Escudero Sahuquillo (presenter) – 15 mins
Discussion – 15 mins
An Open Congestion Control Architecture with network cooperation for RDMA fabric - Yan Zhuang (presenter) – 15 mins
Discussion – 15 mins
Next steps – 10 mins

## Slide 5: Strategies to drastically improve congestion control in high performance data centers: next steps for RDMA
Paul Congdon (Tallac Networks), Jesus Escudero Sahuquillo (UCLM), Pedro Javier García (UCLM), Francisco J. Alfaro (UCLM), Francisco J. Quiles (UCLM) and Jose Duato (UPV)
Notes: 1. Current congestion control in RoCEv2 (ECN):
- Packets are just marked, based on a queue threshold
- Long notification delays: packets have to reach destination, be processed at the NIC, NIC has to send notification to the source NIC 2. Consequences:
- Closed-loop control system with long delay in the feedback chain - By the time the source NIC reacts, the congestion tree has grown significantly - Reaction based on possibly obsolete information - Overreaction due to delayed notifications - Oscillations in the injection rate ---> Low throughput 3. How can we improve it? - By providing more detailed feedback from the switches - By distinguishing in-network from incast congestion - By speeding up notifications - By implementing fast-response mechanisms in the switches 4. More detailed feedback - More accurate detection of packets really contributing to congestion (separate them from victim packets) - Record accumulated packet delay in the packet headers and include this information in the notifications

## Slide 6: Motivation Data center congestion is unique
Congestion
HOLB
PFC
The Internet
The High-Performance Data Centers
Congestion
Congestion
Data centers have…
A much different bandwidth-delay product
Different DCN switch implementations and buffer configurations from Routers
More homogeneity with the network design and topology
A high concentration of high-speed links, compute and storage
Different traffic profiles with a higher degree of correlation
Fewer management domains (typically a single management)
Congestion in the DCN environment is different than in the Internet

## Slide 7: Motivation Congestion in Datacenter Networks (DCNs)
Datacenter Use Cases (OLDI services, Deep Learning, NVMeoF and Cloudification [Congdon18]), require convergent networks.
RDMA for higher throughput and lower latency.
  Lossless or low loss: Priority Flow Control (PFC).
Large DCNs connecting thousands of server nodes:
  Efficient topologies (rich path diversity and reduced diameter).
  Efficient routing algorithms (load and path balancing).
Congestion dramatically threatens DCNs performance, due to its negative effects: HOL blocking.

## Slide 8: Motivation Mitigating DCN Congestion [Garcia05][Garcia19]
Traditional solution | Strategy | Pros | Cons
ECMP Load-balancing | Avoid congestion by spreading flow on multiple paths | Exists and is easy | Not congestion aware Not flow-type aware Doesn’t help incast congestion
ECN | Adjust traffic injection by reacting to congestion signals from the network | Exists and is easy | Long reaction time in DCNs Limited information from the switch Un(not-well)defined for non-TCP use
ECN + PFC (lossless) | Eliminate packet loss by signaling back pressure | Exists | Congestion spreading  HoL blocking Hard to configure and tune
Congestion in the data center is dynamic (i.e. the congestion root can move)
Roots of congestion can occur anywhere in the fabric (front, middle, back)
There are two types of congestion depending on where the root is:
  in-network
  Incast
Multiple roots can exist

## Slide 9: Motivation DCNs need low-latency, low-overhead, high-throughput and high-efficiency
In-common with the Internet is the trend to run more things over UDP…
Would we benefit from some Quic-like (Quic-lite) data center transport with some DCCP-like congestion layer for the DCN?
Hardware offload-able (less emphasis on security and threading).
Common congestion control targeting unique DCN congestion.
In-DC-Network visibility, marking and signaling from switches.
…Leverage the IETF’s expertise and not leave congestion control design to the applications

## Slide 10: Problems with current CC Explicit Congestion Notification (ECN) [RFC 3168]
DataCenter
Network (DCN)
Source end-node
(ECN-enabled)
Destination end-node
(ECN-enabled)
Switch A
(ECN-enabled)
Switch B
(ECN-enabled)
CE Transmitted
to sender
Packets are marked
(CE set)
Traffic flows
are throttled
Congestion
Experienced (CE)
1
2
Marked packets reach destination end-node
3
4
5
Notes: I want to illustrate with this slide the the delay introduced by the ECN closed-loop approach.
By the time the actual congestion occurs, the traffic status in the network, and by so the congestion dynamics may have changed.
Let’s think about the nature of DCNs: size or number of sever nodes interconnected, the network topology and offered paths diversity, the routing algorithm. All these properties, make it more difficult for ECN to react property.
Configuration and tuning in these environments can be painful.

## Slide 11: Problems with current CC Explicit Congestion Notification (ECN) [RFC 3169]
We identify the following problems:
Packets marking is based on a queue occupancy threshold that triggers the congestion detection.
Long notification delays between packets marking and the actual injection throttling.
Injection throttling may be based on obsolete information due to congestion dynamics and long notification delays.
ECN does not directly approach HoL blocking:
  HoL blocking actually happening while congestion trees are throttled.

## Slide 12: How can we improve it?
Augmenting ECN to enable Data Center focused UDP based congestion control:
By providing more detailed feedback from the switches and packet headers.
By distinguishing in-network from incast congestion.
By speeding up notifications.
By implementing fast-response mechanisms in the switches.

## Slide 13: Some ideas to consider open for discussion
More detailed feedback
  Switches indicate more details on congestion status.
  Record accumulated packet delay in the packet headers and include this information in the notifications
Distinguish in-network from incast congestion
  Understand switch position in topology
  Identify when congestion root appears
Speeding up congestion notifications
  Notifications directly from switches backwards to other switches and end-nodes.
Fast-response congestion mechanisms at switches
  Congestion Isolation (in progress – P802.1Qcz)

## Slide 14: References
[Congdon18] Paul Congdon et al: The Lossless Network for Data Centers. NENDICA “Network Enhancements for the Next Decade” Industry Connections Activity, IEEE Standards Association, 2018.
[Garcia05] P. J. Garcia, J. Flich, J. Duato, I. Johnson, F. J. Quiles, and F. Naven, “Dynamic Evolution of Congestion Trees: Analysis and Impact on Switch Architecture,” in High Performance Embedded Architectures and Compilers, ser. Lecture Notes in Computer Science. Springer, Berlin, Heidelberg, Nov. 2005, pp. 266–285.
[Garcia19] Pedro Javier Garcia, Jesus Escudero-Sahuquillo, Francisco J. Quiles and Jose Duato, “Congestion Management for Ethernet-based Lossless DataCenter Networks“ DCN: 1-19-0012-00-Icne.
[Karol87] M. J. Karol, M. G. Hluchyj, S. P. Morgan, "Input versus output queuing on a space-division packet switch", IEEE Trans. Commun., vol. COM-35, no. 12, pp. 1347-1356, Dec. 1987.
[RFC 3168] K. Ramakrishnan et al. The Addition of Explicit Congestion Notification (ECN) to IP. RFC 3168, Year 2001: https://tools.ietf.org/html/rfc3168.
[Congdon19Qcz] Paul Congdon: P802.1Qcz – Congestion Isolation. Standard for Local and Metropolitan Area Networks — Bridges and Bridged Networks — Amendment: Congestion Isolation. PAR approved 27 Sep 2018.
[Escudero11] Jesús Escudero-Sahuquillo, Ernst Gunnar Gran, Pedro Javier García, Jose Flich, Tor Skeie, Olav Lysne, Francisco J. Quiles, José Duato: Combining Congested-Flow Isolation and Injection Throttling in HPC Interconnection Networks. ICPP 2011: 662-672.
[Rocher17] Jose Rocher-Gonzalez, Jesús Escudero-Sahuquillo, Pedro Javier García, Francisco J. Quiles: On the Impact of Routing Algorithms in the Effectiveness of Queuing Schemes in High-Performance Interconnection Networks. Hot Interconnects 2017: 65-72.
[Escudero19] Jesús Escudero-Sahuquillo, Pedro Javier García, Francisco J. Quiles, José Duato: P802.1Qcz interworking with other data center technologies. IEEE 802.1 Plenary Meeting, San Diego, CA, USA July 8, 2018 (cz-escudero-sahuquillo-ci-internetworking-0718-v1.pdf)

## Slide 15: Backup Slides

## Slide 16: Introduction In-Network Congestion
It usually occurs when congestion is light (i.e. it exceeds available link bandwidth by a small integer factor at most).
There are two basic scenarios:
  A few nodes injecting traffic at full rate towards the same destination.
  Many nodes injecting traffic at low rates towards the same destination.
Egress ports of in-network congested switches work at full capacity and may contend with other flows for downstream switches, eventually moving the root of congestion downwards.
Root of Congestion
In-network congestion
First
Stage
Second
Stage

## Slide 17: Introduction Incast Congestion
Many nodes start to send packets at full rate towards the same destination, almost at the same time (e.g. OLDI services)
Incast congestion occurs at the ToR switch where the node that multiple parties are synchronizing with is connected, and grows from ToR switches to upstream switches.
Alternatively, in CLOS networks many small congestion trees concurrently appear at first-stage switches, later merging at second-stage switches and finally forming a larger congestion tree.
Root of Congestion
Incast congestion
scenario
First
Stage
Second
Stage

## Slide 18: Introduction Traditional approaches
Load balancing: spread traffic flows across the multiple paths in order to balance the load and hopefully avoid congestion (load balancing).
Problems:
  Spreading traffic does not take into account whether the selected path is congested, generating collisions of traffic flows in paths already congested.
  The nature of flows matters: elephant flows increase the chance of creating in-network congestion.
  Traditional load balancing (e.g. ECMP) does not work when incast congestion appears.

## Slide 19: Introduction Traditional approaches
ECN + PFC: The DCN network equipment reacts to congestion using ECN + PFC and smart buffer management in an attempt to eliminate the congestion tree.
Problems:
  Large DCN networks have more hops, increasing the closed-loop reaction time of ECN.
  More traffic in flight makes it difficult for ECN to react to sudden traffic bursts.
  PFC generates HoL blocking in upstream switches.
  Injection throttling may be triggered at sources not contributing to congestion.
Non-congested flows advance at the same speed as congested ones
Congestion affects
sources that do not
cause congestion
PFC

## Slide 20: Current congestion control Head-of-Line (HOL) Blocking problem [Karol87]

## Slide 21: Current congestion control Head-of-Line (HOL) Blocking problem [Karol87]

## Slide 22: Introduction HOL Blocking the main negative effect
The problem is not the congestion itself but the Head-of-Line (HoL) blocking [Karol87] that spoils the traffic flows performance (throughput and latency).
By preventing the HoL blocking, congestion becomes harmless [Garcia05][Garcia19].
Traditional approaches for congestion control do not deal with the HoL blocking entirely.
Notes: A successful strategy for reducing congestion impact on network performance should be focused on preventing HOL blocking immediately, while congestion trees are drained (e.g. by an ECN-like approach).

## Slide 23: Motivation Congestion tree dynamics [Garcia05][Garcia19]
  It is crucial to understand them to propose better solutions.
  Congestion originates at some initial, intermediate or final stage in the network, and it changes a lot the perspective.
Root of Congestion
Incast congestion
Root of Congestion
In-network congestion
First
Stage
Second
Stage
First
Stage
Second
Stage
Notes: Studying congestion dynamics is crucial to face congestion problems

## Slide 24: Motivation Traditional approaches
Load balancing: spread traffic flows across the multiple paths in order to balance the load and hopefully avoid congestion.
ECN + PFC react to congestion using and smart buffer management in an attempt to eliminate the congestion tree.
Current solution | Pros | Cons
ECMP Load-balancing | Exists and is easy | Not congestion aware Not flow-type aware Doesn’t help incast congestion
ECN | Exists and is easy | Long reaction time in DCNs Limited information from the switch Un(not-well)defined for non-TCP use
ECN + PFC (lossless) | Exists | Congestion spreading  HoL blocking Hard to configure and tune

## Slide 25: Problems with current CC Consequences
Closed-loop control system with long delay in the feedback chain:
  The delay from congestion detection to actual traffic throttling can be very long.
  Depending on the DCN topology diameter and routing, this delay may be even worse.
By the time the source NIC reacts, the congestion tree has grown significantly:
  When delayed congestion notifications reach the NIC, then the throttling has to be more aggressive to reduce the already formed congestion tree.

## Slide 26: Problems with current CC Consequences
Reaction based on possibly obsolete information:
  Throttling at NICs may be disproportional with the network traffic status.
  By the time the closed-loop mechanism actually reacts at NICs the congestion trees may have evolved (movable roots and branches).
Overreaction due to delayed notifications
  Aggressive throttling causes that flows throughput may be reduced excessively when congestion trees are disappearing or moving.
  Inadequate reaction in case of transient congestion.
ECN works work end-to-end (e2e), so that transient congestion may still spoil network performance.

## Slide 27: Problems with current CC Consequences
The result are the oscillations in the injection rate, so that the DCN obtains low throughput and poor latency:
  ECN is very difficult to tune as it depends on the traffic pattern [Escudero11].
Simulation results:
64-node 3-level CLOS
75% Uniform/Random traffic
25% Hot-spot traffic
4 incast situations [1ms-2ms]
Network configurations:
  1Q: one queue per buffer
  ITh: ECN-like technique
  VOQnet (ideal): one queue per server node (64 queues)
incast
starts
incast
ends

## Slide 28: How can we improve it? More detailed feedback
More accurate detection of packets really contributing to congestion at switches (separate them from victim packets):
  Packet at the queue head, packet with longest accumulated delay.
  Avoid false positives.
To record accumulated packet delay in the packet headers and include this information in the notifications:
  The longer the packet latency, the more intense the congestion, and more aggressive the injection throttling needs to be.
Notes: IPPM for packet header stamping at swtiches.

## Slide 29: How can we improve it? Distinguishing in-network from incast congestion
Load balancing alleviates in-network congestion, but it does not work properly with incast congestion.
ECN reduces incast scenarios but has several issues: signaling delays, oscillations, etc.
Congestion isolation can be combined not only with ECN, but other techniques for load balancing and destination scheduling to work together.

## Slide 30: How can we improve it? Distinguishing in-network from incast congestion
Simulation results:
11664-node 3-level CLOS,
90% Uniform/Random traffic
10% incast traffic (one congestion tree)
Network configurations:
  D-mod-k: Deterministic routing.
  Oblivious: Random/exploits path diversity.
  Adaptive: Fully adaptive routing.
  Adaptive-th: Limits adaptivity.
Load balancing is counterproductive when incast scenarios appear. It is better to limit this balancing under certain scenarios [Rocher17].

## Slide 31: How can we improve it? Speeding up congestion notifications
The closed-loop approach is slow, as marked packets have to cover the path length to reach the destination end-node, and then the congestion notifications (e.g. CNPs, TCP ACKs, etc.) need to travel backwards to reach the source end-nodes:
  Notifications directly from switches backwards to other switches and end-nodes will speed up the congestion notification to both switches and NICs.
The congestion notification mechanism can be in sync with ECN and congestion isolation, so that they leverage CNPs to work better.

## Slide 32: How can we improve it? Fast-response mechanisms in the switches
Fast congestion detection mechanisms.
Fast reaction once congestion is detected, by isolating the congested flows at switch buffers:
  While ECN reacts, HoL blocking can be immediately prevented if the congested flows are isolated.
ECN reaction will be focused only on congested flows, already isolated in special buffer space at switches:
  The reaction time of ECN is not so critical anymore.
  ECN helps congestion isolation to release the resources used to isolate congested flows, making them available for future congestion.

## Slide 33: Conclusions
End-to-end solutions suffer from intrinsic notification delays and have a slow response when congestion appears.
We have analyzed the pros and cons of ECN, identifying several ways to improve its design:
  More detailed feedback.
  Distinguish in-network from incast congestion.
  Speeding up congestion notifications.
  Fast-response congestion mechanisms at switches.
ECN can be combined with fast-response mechanisms at switches to prevent HoL-blocking immediately, while the congestion tree is reduced thanks to ECN's injection throttling.

## Slide 34
An Open Congestion Control Architecture with network cooperation for RDMA fabric
draft-zhh-tsvwg-open-architecture-00
draft-yueven-tsvwg-dccm-requirements-00
IETF 105, Montreal, Canada
Yan Zhuang (presenter),Rachel Huang
Yu Xiang, Roni Even
Huawei Technologies
34

## Slide 35: An open congestion control architecture with network cooperation for RDMA fabric
Scope
  Managed datacenter networks
  RDMA traffics for applications, such as HPC and storage….requiring low latency, high throughput…
Motivation, requirements and use cases
  Incast traffic cause severe congestion in the data center network.
  Mixture of RDMA traffic and TCP traffics effects each other.
  More efficient and effective congestion controls are needed to support the scalability and high performance.
Objectives
  Define an open congestion architecture with network cooperation to enable more effective congestion controls for RDMA fabrics.
2

## Slide 36: Open Architecture Overview
3
Open to network cooperation
Open to congestion control algorithms deployment and management

## Slide 37: Protocol Stack Overview
3
Solution should be RDMA transport agnostic.
Ethernet Link Layer
IP
UDP
IB Transport protocols
Net2Nic channel
Ethernet/IP Management
OFA Stack
RDMA Application/ULP
TCP
iwarp
Other
applications
......

## Slide 38
Open for Network Cooperation
38
What?
  Net-control module inside network nodes (e.g. switches) can signal back to senders’ NIC directly, and further incorporated into NICs’ transmit control.
Why?
  Fast Convergence: reduce the CC feedback/control time.
  Accurate congestion awareness: as congestion point, network aware of the degree of the ongoing and expected congestion and can requests for proper moderation of the selected flows.
How?
  A Net2Nic control channel can be used to collect congestion information from the network nodes to be further incorporated to the congestion control of sender NICs.

## Slide 39
Open for Congestion control deployment and management
39
What?
  Deploy/manage congestion control algorithms in a common way regardless of the detailed hardware implementation.
Why?
  More flexibility: Traffic patterns may differ in CC choices.
  Easy to deployment in HW: New CC algorithms are suggested to be implemented in hardware easily.
How?
  A system CC interface is provided to the operators to deploy CCs through a common platform and then be mapped to local actions/functions.
  Local functions related to congestion controls can be implemented as function blocks (in hardware) and interact with each other through internal interfaces to achieve the final congestion controls.

## Slide 40
Next Step
Solicit more feedbacks/comments/interests on this open architecture.
40