## Slide 1: Use Cases and Requirements for Managed LAN as a Service (MLaaS)
August 2019, Nendica
Wei Qiu, Huawei
Ron Insler, RAD

## Slide 2: Presentation Objectives
Outline initial use cases and requirements of Managed LAN as a Service
Discuss current gaps and expectations

## Slide 3: Making MLaaS Business Case
Managed LAN as a Service (MLaaS)
  LAN is planned, implemented, operated & maintained by a remote service provider.
  A natural expansion of Managed Service Provider (MSP) business
Key factors to make MLAAS profitable
  LAN deployment efficiency improvement (use case 1)
    Build more sites within the same time
    Require less skilled personal on sites
  LAN SLA assurance (use case 2)
    Attract more customers while remaining high margin
    Less truck roll for troubleshooting
    Less penalty for SLA violation

## Slide 4: Use Case 1 –Underlay Network Automation
Currently underlay + overlay solution is widely adopted for campus LAN
  Underlay provides simple and high available connectivity and forwarding
  Overlay (i.e VxLAN) provides flexible and virtual functionality, such as segmentation and information flow control.
Underlay
Overlay
Controller
NMS
Core/Agg
Access
Overlay is typically provisioned via a Network Management System or controller, hence all on-site equipment needs to be managed remotely.
Deployment efficiency depends on how easy such equipment management can be provided remotely
The challenge: how to simplify underlay on-site configuration and management.

## Slide 5: Current Underlay Configuration Process
Current process
Prerequisites: Prepare and store the underlay configuration files and image at the remote servers.
  Devices power on.
  Devices discover each other via LLDP.
  Paths establish (active topology) based on Spanning Tree (STP is enabled by default).
  Devices get management IP address via DHCP.
  Devices download the images and prepared configuration files from the remote server.
LLDP
LLDP
Controller/NMS
DHCP server
File server (image, config file..)
LLDP
DHCP Discover(broadcast)
LLDP

## Slide 6: Current Gap and Expectations
Issues
  Heavy broadcast traffic (during DHCP process)
  Prone to human error, may cause network failure(i.e. L2 loop) and lose the management of devices
  Need to do the network planning of VLAN, IP…
  Slow process, low efficiency
  When the LAN become large-scale (i.e. thousands of switches and APs), the above issues will become really serious.
Expectations
  Enhanced L2 protocol for topology discovery and data path establishment to achieve underlay configuration automation efficiently.

## Slide 7: Use Case 2- LAN SLA Assurance
Research network
Video surveillance
Energy efficiency IoT
…
Enterprise IT (UC, Internet…)
Multi-service convergence LAN
  Enterprise IT (Email, UC, Internet…)
  Research and/or test network
  Video surveillance
  Energy efficiency IoT, i.e. the auto control of temperature, light, humidity…
Mission-critical applications requires SLA guarantee such as bandwidth /delay/ packet delay variation /packet loss ratio, etc.
Not enough LAN SLA assurance currently
  Current the MSP typically only promises LAN SLA for the network availability, time to response and repair etc. in the contract.
  Didn’t see any LAN SLA guarantee offered by MSP regarding to the bandwidth, delay, packet delay variation , packet loss ratio …
Single physical network
Multiple services

## Slide 8: Current Gap and Expectations
Issues
  Traditional Ethernet technology doesn’t provide latency determinism, specifically, strict upper bound to latency, packet delay variation and packet loss ratio.
  TSN technologies can provide deterministic behavior (premium SLA guaranteed) , but it is more suitable for the pre-planned and well-engineered network with size limit.
Expectations
  A sets of new technologies to guarantee SLA for per user or per application at large-scale LAN.

## Slide 9: Summary
The presentation outlines two use cases and related technology requirement for Managed-LAN service.
Other use cases and requirements could be discussed and added on later.
Call for interest to join the discussion and study.