## Slide 1: LAN Technology Directions and Opportunities for Managed Services
Paul Congdon
September 2019

## Slide 2: The Forces Driving Change in the Campus LAN
Digital Transformation
The Interactive Cloud
Mobility
IoT
Security
Notes: Digital transformation:
  DT is about increasing organizational efficiency and agility for business processes. Enterprises are digitizing workflows for higher productivity, lower operating costs and competitive advantage. As more business processes become digital, networks, including campus LANs, have to support the shift in scale and complexity. Digital transformation is the adoption of digital processes and tools to achieve strategic business goals. This is really the umbrella force that is enabled by cloud, mobility, IoT and security below – the other forces are really all about digital transformation.
Interactive Cloud:
  The need to interact with the cloud in real-time is more important - augmented reality, voice recognition, all the work in the DC can’t be dropped in the LAN
  Enterprises are augmenting internal, on-premise IT with cloud, including on-premise private cloud, colocated private cloud or public cloud services. Campus networks have to meet user expectations of application performance and administrator needs around security and policy in a consistent way.
Mobility:
  Wireless and mobility are shaping enterprise network infrastructure. Users accessing corporate data from smartphones create challenges for back-end IT infrastructure and greater demand for enterprise mobility. But it is a demand that has to be met: mobile devices are already the predominant means of network access for all users. Improvements in wireless communications are impacting the wired network and convergence between LTE/5G and WiFi in unlicensed bands will likely require additional innovations to support fair coexistence.
IoT:
  The internet of things (IoT) journey is well underway, but billions of machine-to-machine connections will emerge in the next few years that require machine learning intelligence based on analytics and business policy. Enterprise campus networks need the bandwidth and flexibility to support this influx of machine connectivity. Most enterprises will undertake IoT data aggregation, filtering and analysis at the network edge, usually for the purposes of security and speed data analysis. Headless on-boarding and isolation of IoT from other campus LAN use cases may be beneficial for many reasons.
Security:
  All these developments – digitisation, cloud, mobility and IoT – have security implications. Each new connection is a potential attack vector, and attacks are becoming increasingly sophisticated and obscured via encryption and various deceptions. Campus networks have to secure these new connections by detecting anomalies – even encrypted ones – and recognising potentially malicious behaviours and patterns in real time and at scale.

## Slide 3: Change Brings New Requirements the need for more…
More Scale
More Coordination
More Performance
More Reliability
More Synchronization
More Security
More Please
Notes: More Scale – more stuff on network
  IoT, Mobile – Not just bandwidth, but number of devices on the network stresses tools, reports, etc…
More north/south communication
  Everything to/from cloud – coordinated SD-LAN, SD-WAN becomes an interesting use-case and requirement. Means management tools can’t focus on silos of the solution – Wired, Wireless and WAN gateway in a single view
More bandwidth, faster links
  Faster WiFi, digital transformation – use of video – just the insatiable consumption of bandwidth.
More reliability
  The interactive cloud needs low latency and nothing impacts latency more than packet loss, so need more reliability and congestion management
More timing and synchronization
  LAN technologies and Etherrnet are finding their way into more verticals – this can be an interesting service diversification. Automotive and industrial markets, wireless coordination is an interesting future
More security
  The new requirements brings need for additional security. more things on network, public comms to the cloud, regulation - compliance, privacy

## Slide 4: Technical Trends and Innovation in the LAN
LAN Management Architectures
Virtualization in the LAN
Multi-Gigabit PoE
WiFi6 and Beyond
Timing and Synchronization
Underlay
Overlay
Virtual Networking
Network Management
Notes: Each will be discussed in detail, but these are some recent technical innovations and especially an industry focus on standards

## Slide 5: LAN Management Architectures
Control
Forwarding
Data
Control
Forwarding
Data
Control
Forwarding
Data
Control
Forwarding
Data
Control
Forwarding
Data
NMS
Forwarding
Data
Forwarding
Data
Forwarding
Data
Forwarding
Data
Forwarding
Data
Control (ler)
NMS
App
App
…
Early SDN
Control
Forwarding
Control
Forwarding
Data
Data
Data
Control (ler)
NMS
App
App
…
Forwarding
Data
NFV
Forwarding
Data
NFV
Forwarding
Data
NFV
Centralized Forwarding
Control
Forwarding
Data
Control
Forwarding
Data
Control
Forwarding
Data
Control
Forwarding
Data
Control
Forwarding
Data
NMS
Cloud-Based
SDN + Cloud-Based
Control (ler)
NMS
App
App
…
Control
Forwarding
Data
Control
Forwarding
Data
Control
Forwarding
Data
Control
Forwarding
Data
Control
Forwarding
Data
Forwarding
Data
NFV
Forwarding
Data
NFV
Forwarding
Data
NFV
Trends
Programmable
Outsourceable
Service Oriented
Simplified Scaling
Adapting to the business pressures on traditional IT

## Slide 6: Virtualization in the LAN
Founded on standards-based technologies – but, no interoperability, so no standards!
  VxLAN encapsulation, LISP auto-provisioning, 802.1X authentication
Benefits for a Managed LAN
  Link the SD-LAN -> SD-WAN -> Cloud Services
  Multi-tenant infrastructure
  Secure isolation of slices
  Service Level Agreements
Implications
  Encapsulation HW likely requires upgrades
  Orchestration SW needs to be vendor agnostic
Underlay
Overlay
Orchestration
Quality of Service VoIP
Secure video surveillance
Energy efficient IoT
…
Policy assured Corporate LAN
Common physical underlay
Purpose built network slices

## Slide 7: Multi-Gigabit PoE Driven by WiFi innovation
1G-PoE has had a long run…
  First introduced in 802.1af-2003
  Billions of ports and existing cables
WiFi keeps getting…
  Faster
  More power hungry
  More sophisticated (see next slide)
What does this mean?
  Upgrade Cycle!
  Faster access => Faster fiber uplinks
  Door opener for Managed Services
2.5G
5G
10G
IEEE Std 802.3bz-2016
IEEE Std 802.3bt-2018

## Slide 8: WiFi 6 and beyond
More capacity, more density, more coordination
IEEE Std 802.11ax-2019
9.6 Gbps via 8 streams
Mu-MIMO and OFDMA
Higher density and higher throughput
IEEE Std 802.11be-2024(?)
320MHz bands, 16 streams
Lower latency and higher throughput
Multi-Ap Coordination
Is it time for time synchronization in the backhaul?

## Slide 9: Timing and Synchronization on the LAN
Trending from niche to mainstream
Synchronization
Reliability
Latency Control
Manageability
IEEE 802.1
Time Sensitive Networking (TSN)
Reliability
Redundant Transmissions (802.1CB)
Path Control (802.1Qca)
Reservations (802.1Qat)
Stream Filtering (802.1Qci)
Resource Allocation (802.1Qdd)
Manageability
YANG (802.1Qcp, etc)
QoS Provisioning (802.1DC)
Registration (802.1CS)
Profile for SPs (802.1DF)
Profile for Automotive (802.1DG)
Stream Filtering (802.1Qci)
Time Sync
Timing and Sync (802.1AS)
IEEE 1588 Profile
Bounded Latency
Credit Based Shaper (802.1Qav)
Frame Preemption (802.3br & 802.1Qbu)
Scheduled Traffic (802.1Qbv)
Cyclical Queuing (802.1Qch)
Asynchronous Traffic Shaping (802.1Qcr)
Pro Audio
Industrial
Automotive
Mobile Fronthaul
WiFi Backhaul?
2005
2021

## Slide 10: Never Forget About Security
Scaling up with IoT and Mobile means… a great attack surface
Everything in the cloud means… more exposure to threats
World markets and increased regulation mean… more compliance requirements
Implications
Top consultative engagement with the customer
Use case for LAN virtualization
Use case for Service Provider analytics

## Slide 11: Why Now is the time for Service Providers
The upgrade cycle is now!
  WiFi impacts the wired LAN
  Embedded virtualization in the access layer
  Timing and synchronization enablement
Management architectures trends enable managed services
  SDN standardized and abstracted the network
  Cloud-based management enables outsourcing and multitenancy
New LAN technologies are complex
  Unlicensed interplay with 5G and WiFi
  Aligning SD-LAN with SD-WAN
  End-to-end SLA assurance
Security demands continue to grow
  A bigger attack surface brings the need for policy enforced isolation
  Increased compliance and vulnerability for business

## Slide 12: Success Factors for Managed LAN Service
Managed LAN Service is about replacing or augmenting existing IT
You must have a customer relationship
You must take advantage of upgrade cycles
You must have an aligned business focus (small, medium, large Enterprise)
You must have the correct tools
Tools
Cloud driven remote management – scalable and cost effective
Standards based virtualized LAN infrastructure
Deployable next generation WiFI
Multi-tenant analytics platforms to curate data
Security and compliance solutions for the LAN
Means for defining and delivering SLAs on the LAN