IEEE P802-REVc Working Group Ballot #1
Comment Discussion, July

---
Items for 7/9/23

---
Current Status
Resolution status		Editing status
Accepted	95	Open	4
Revised	81	In work	0
Rejected	15	Ready	55
Suggest Accepted	0	Applied	137
Suggest Revised	1	Total	195
Suggest Rejected	2	% applied	70%
# left to resolve	3
% left to resolve	2%

---
CID 98: Define IEEE 802 network/family
- Current definition:
  - IEEE 802® network: A network consisting of one or more interconnected networks each using a medium access control (MAC) protocol specified in an IEEE 802 standard.
- One suggestion: An IEEE 802 Network should be all networks that can be bridged together, including those that do not use and IEEE 802 MAC/PHY standard.
  - IEEE 802® network: One or more interconnected networks that use IEEE 802.1Q bridging
- Now in 4.1:
  - “The family of IEEE 802 standards is the collection of standards that have been developed under the IEEE 802 LMSC, see 4.4 for a list of the IEEE 802 standards current as of the publication of this standard.”

---
CID 109: EPD and LPD
- Comment: EPD and LPD as described in the draft appear to be inconsistent with the usage of those terms in other standards within the IEEE 802 "family", such as 802.11 and 802.1AC.
- Proposed Change: Revise definitions of EPD and LPD to maintain peace within the family.
- Action: Marks has proposed specific changes. Under discussion with the group.

---
CID 81
- Comment: The 802.1Q standard capitalizes Bridge whenever it is used to refer to a compliant Q Bridge, however 802 seems to ignore this convention.
- Proposed Change: Change to: IEEE Std 802.1Q adds additional capabilities to the MAC bridge functionality including virtual local area networks (VLANs), riorities, and provider bridging, as described in 5.3.2.5.
- Proposed Resolution: Suggested Rejected: The commenter did not provide sufficient detail to implement the suggested change in the standard.