## Slide 1: Resolving EPD/LPD inconsistency
Date: 2023-12-19
Authors:

## Slide 2: Abstract
High-level discussion of the concepts behind the terms EPD and LPD in P802-REVc and other IEEE 802 standards, along with suggested directions toward consistency.

## Slide 3: Background
Prior contributions highlighted EPD/LPD inconsistency; e.g.:
  maint-Marks-epd-lpd-0719-v02 (“What are EPD and LPD?”)
  maint-finn-epd-lpd-errors-0919-v02 (“Why the EPD/LPD information in IEEE 802, IEEE 802.1AC, and 802.1Q must be fixed”)
  maint-Marks-Finn-epd-lpd-1119-copyright (“Clarifying EPD and LPD”)
  802.11-20-0174-01-0arc (“EPD and LPD Terminology Misalignment in IEEE Std 802.1 and 802.11”)
  802.11-20-0245-02-000m (“Corrections to EPD and LPD Terminology”)
  802.11-21-0092-01-0arc (“LLC Theory and Protocol Discrimination”)
Since then:
  EPD and LPD have been stricken from 802.1Q (in 802.1Q-2022)
  EPD/LPD have been discussed in ballot of IEEE Std 802 revision (P802-REVc)
    Changes in IEEE P802-REVc/D1.2 are now in recirc
EPD and LPD are also used extensively in 802.11 and in 802.1AC
  802.1AC: mainly in Clauses 12. (Protocol discrimination and media), 13.2 (Wireless LAN convergence function), and B.1.5 (IEEE 802.11 parameter mapping)

## Slide 4: Status
Currently, P802-REVc describes (5.2.2) two methods “used by the LLC sublayer to determine the protocol identifier designating the higher layer protocol to which to deliver an LLC sublayer protocol data unit”:
  EPD: EtherType protocol discrimination (EPD), which uses, as the protocol identifier, the EtherType value made available to the LLC sublayer through the MSAP
  LPD: LLC protocol discrimination (LPD), which uses, as the protocol identifier the LLC address as specified in ISO/IEC 8802-2 or, using a particular form (described in 9.4) of the Subnetwork Access Protocol (SNAP) format, an EtherType
These definitions are confusing. One major point of confusion:
Since the draft distinguishes two “methods,” many readers understand them to be non-overlapping alternative methods. However, they are not:
  e.g., a protocol carrying an EtherType identifier within SNAP is both EPD [per (a)] and LPD [per (b)].

## Slide 5: Example of Inconsistency with 802.11
P802-REVc-d1.2 says 802.3 “uses the value of a Length/Type field to distinguish between EPD and LPD.”
  802-2014 says “the value of the Type/Length field in the IEEE 802.3 MAC frame format directs the protocol parser into the LPD HLPDE if the value is less than 1536.”
  Both cases indicate that Ethernet supports both EPD and LPD
    EPD when the Length/Type field is a Type
    LPD when the Length/Type field is a Length [but may be EPD as well as LPD?]
IEEE Std 802.11-REVme/d4.1 says “As specified in IEEE Std 802, EPD encoding always starts with a Length/Type field that is either a 2-octet length or a 2-octet EtherType”
  In other words, Ethernet uses only EPD, for any value of the Length/Type field

## Slide 6: Two key concepts
Two concepts are essential to the problem:
What is the protocol identifier? (EtherType; an LSAP address; …)
  Each has an IEEE RA registry globally-unique assignment (links above)
  Each is used to distinguish the “higher-layer” protocol that is being carried in the data, and are intended to (in the LLC) demultiplex the data payload to the appropriate higher-layer entity for further processing per its protocol definition
  Note: IEEE Std 802 also specifies a third type of protocol identifier: a private protocol identifier based on an OUI
How is the protocol identifier encoded?
  “802.3 style”, using a “Length/Type” field [called “Length/Type encoding” in P802-REVc-d1.2]
  “802.2 style”, with no “Length/Type” field [called “LSAP encoding” in P802-REVc-d1.2]
Concepts (1) and (2) are orthogonal. Either encoding is enabled to carry any type of protocol identifier.
The definitions of EPD and LPD currently in P802-REVc do not make a distinction based on either (1) or (2).

## Slide 7: Proposed Direction
P802-REVc should clearly identify the two key concepts and state that they are orthogonal.
  Most of the needed material was added in P802-REVc-d1.2
The concepts of EPD and LPD are unnecessary
  should be deleted
  or could be retained without being used for differentiation
802.11 is already written based on the understanding that EPD and LPD are encoding types.
  fairly easy to revise 802.11 so that EPD and LPD are replaced by encoding types
802.1AC should be aligned
  alignment would be imperative if EPD and LPD are deleted from IEEE Std 802