IEEE P802-REVc Working Group Ballot Recirculation #2
Comment Resolution

---
Items for 24 January, 2024

---
Agenda
- Close editorial comments (CIDs 1, 8, 9, 11, 15, 16,18, 19)
- CID 38: IP in a RM
- Description of switch, CID 12
- New text for TSN, CID 17
- Bridges, bridgeable, CID 3, CID 4
- Do bridges have to support EtherTypes, CID 6
- EPD vs. LPD discussion

---
CID 38
- Comment: Perhaps adding an RM with IP, or a reference to IP layering, might further clarify the context.
- Suggest Revised: In 5.3.3, change
  - “These process network layer protocols that operate directly above the LLC sublayer, with forwarding decisions based on network layer addresses.”
- With
  - “These process network layer protocols that operate directly above the LLC sublayer, as shown in Figure 3, with forwarding decisions based on network layer addresses.”

---
CID 12: Switch
- Comment: The sentence is misleading. Though it does not actually say that people use the term "switch" to indicate compliance with IEEE Std 802.1Q, people may get that impression.
- Proposed change: Change note to "The term "switch" is sometimes used in the industry to refer to products that include bridging capability, often with other interconnection functions as well."
- Suggest Revised: Change note to “NOTE—The term switch is sometimes used in the industry to refer to products that include a bridging capability, such as an IEEE 802.1Q bridge, often with other interconnection functions. However, while a switch can contain an IEEE 802.1Q bridge, it is not equivalent to an IEEE 802.1Q bridge.”

---
CID 17: TSN update - changes
- Change
  - "Some IEEE 802 standards specify TSN capabilities to provide network protocols and mechanisms for use by applications that need data transport with low and bounded latency, low and bounded delay variation, and low packet loss. The TSN capabilities augment networking protocols and mechanisms to support both TSN traffic streams as well as other traffic. Some TSN capabilities are described in the following standards:"
- to one of the following options A or B (for discussion):
  - A: "Some IEEE 802 standards specify network protocols and mechanisms for applications that need TSN capabilities such data transport with low and bounded latency, low and bounded latency variation, and low packet loss.
  - Some of these network protocols and mechanisms are the following ones:"
  - B: "Some IEEE 802 standards specify network protocols and mechanisms for applications that need TSN capabilities such as data transport from one end station to one or more other end stations with low and bounded latency, low and bounded latency variation, and low packet loss. Some of these network protocols and mechanisms are the following ones:"
- Remarks:
  - My choices on items 5) and 6) was more or less randomly.
  - Term "end station" in option B should imply 802 network.

---
CID 3: Definition of bridgeable
- Comment: The definition of bridge adds the term "bridgeable" as a qualifier on IEEE 802 networks. But, this is not a defined term. It seems that subclause 6.1 is trying to define it, to be, effectively, any network that supports the MAC service (and ISS?) specified in 802.1AC. If that's the intent/meaning, then let's define it as such.
- Proposed Change: Add a definition: "bridgeable: A network that that provides sufficient capabilities to support the MAC Service and Internal Sublayer Service specified in IEEE Std 802.1AC."
- Suggest Revised:	Add a definition “bridgeable network: A network that that provides sufficient capabilities to support the MAC Service and Internal Sublayer Service specified in IEEE Std 802.1AC.”

---
CID 4: IEEE 802 bridgeable vs bridgable
- Comment: Why does a bridge have to connect specifically/only IEEE 802 networks (in fact we note later that some non-802 networks are also bridgeable)? "Bridge" is a generic term, and is further specified as IEEE Std 802.1Q Bridge when it is specifically following IEEE 802 protocols and uses.
- Proposed change: P21.8, delete "IEEE 802". Same thing at P26.25. P35.4, replace "bridged IEEE 802 network" with "bridged network". Same thing at P35.6. P35.19, delete "IEEE 802.1Q". P39.3, delete "IEEE 802". Same thing at P39.7 and P39.10.
- Suggest Accepted: (lets walk through these in the draft)

---
CID 6: Do bridges support EtherTypes
- Comment (6.1, p39, l8): Why does a bridge have to support EtherTypes?
- Proposed change: Delete "and support the use of EtherTypes for protocol identification at the LLC sublayer". Add a new sentence, "An IEEE Std 802.1Q Bridge will further support the use of EtherTypes for protocol identification, and conform to other requirements of IEEE Std 802.1Q."
- Suggest Accepted

---
EPD/LPD
- What is the service interface for 802?
  - Do all 802.1 protocols operate below this interface?
- Where does 802.1X, 802.1AX and 802.1AE fit in the architecture?
  - For example, if enabled, is 802.1X decryption/authentication called first for a packet arriving from a MAC?
  - Is 802.1X encryption/authentication the last process applied to the packet prior to being delivered to the MAC.

---
Items for 23 January, 2024

---
Agenda
- Editorial comments (CIDs 1, 8, 9, 11, 15, 16,18, 19)
- EPD vs. LPD discussion
- Technical and General

---
Ballot result summary
	LB1 TOTAL	LB1 %	RC1 TOTAL	RC1 %	RC2 TOTAL	RC1 %
Yes	37	84%	42	87%	44	88%
No 7 16%	7	16%	6	13%	6	12%
Voting Yes or No	44	100%	48	100%	48	100%
Abstain, lack of time	2	3 %	1	2 %	1	2 %
Abstain, lack of expertise	12	21%	12	20 %	10	17 %
Abstain, other	0	0%	0	0%	0	0%
Repondents	58		37		26
Voting members	56		30		25
Non-voting members	2		7		1
Number of commenters	15		6		7
Number of comments	195		76		19

---
Status 23 January 2024
Resolution status		Editing status
Accepted	0	Open	19
Revised	0	Committee	0
Rejected	0	In work	0
Suggest Accepted	7	Ready	0
Suggest Revised	0	Applied	0
Suggest Rejected	1	Total	19
# left to resolve	19	% applied	0%
% left to resolve	100%

---
Results and Comments
- Ballot results on mentor at:
  - https://mentor.ieee.org/802.1/dcn/24/1-24-0003-01-Mntg-p802-revc-d1-2-wg-ballot-results.ods
- Comment are located on mentor at:
  - https://mentor.ieee.org/802.1/dcn/24/1-24-0002-01-Mntg-p802-revc-d1-2-comments-pdis.ods
- Comments marked with Suggested Accepted, Suggested Revised (with suggestion) and Suggested Rejected (with rejection reason)
  - Based solely on Technical Editors humble opinion (as a starting point).
  - Sorted by page number (you are welcome to sort them as you wish)

---
Process
- Editorials (CID 1, 8, 9, 11, 15, 16, 18, 19)
  - Pretty simple, review my suggested resolutions
  - Approve as a batch on 1/24
- LPD/EPD – Initial presentations and discussions
- Others in page order

---
EPD/LPD (CID 5, 10, 14) discussion
Review other documents and come back tomorrow

---
Others
- Bridges, bridgeable, CID 3, CID 4
- “New IEEE 802 standards”, CID 7
- Description of switch, CID 12
- List of bridge characteristics, CID 13
- New text for TSN, CID 17 (see slides later)
- Add RM with IP or reference to IP, CID 2
- Do bridges have to support EtherTypes, CID 6

---
TSN changes – rationale (CID 17, 1 of 5)
The introductory three sentences are enhanced over the previous draft, but can be improved. I tried to develop my suggested remedy carefully, because the final formulation may need to survive for a longer time unaltered once 802 REVc is published.
Issues I see with the current three sentences:
1) The lettered list (line 38ff.) shows IEEE 802 standards with protocols and procedures. In contrast, the second introductory sentence these standards describing TSN capabilities. Both terms are mixed.
2) I do not think there is a common understanding of what "TSN capabilities" are. For example:
- The referred 802 standards have no definition of what a TSN capability is and what not.
- Different equipment vendors may have "TSN..." products that differ significantly in the supported 802 protocols and mechanisms, which may sometimes be a result of different target markets, link speeds, or a variety of other reasons.
- Different individuals in WG 802.1 may likewise different views on what the "relevant"/"important" protocols and procedures are.

---
TSN changes – rationale (CID 17, 2 of 5)
- The set of relevant protocols and procedures may also vary between profile projects and standards (Std 802.1BA, Std 802.1CP, P802.1DG, P802.1DP, IEC/IEEE P60802) for different markets. In addition, listing many transmission selection algorithms here may be misinterpreted. For example, classic strict priority transmission selection is sufficient for bridges in Std 802.1CM ("TSN for Fronthaul"). None of the other transmission selection algorithms are listed as mandatory, and the strict priority algorithm was there before "TSN" and is also there in pure best-effort networks. In a weaker form, something similar applies for the upcoming Std 802.1DP for the mandatory transmission slection algorithms in bridges - strict priority and credit-based shaper are sufficient for some bridges in the current draft of P802.1DP. Credit-based shaper was also there before "TSN", although it is at least listed in the current 802 REVc draft.
3) Along the lines of item 2), I do not think there is a common understanding of "TSN traffic streams".
4) The entire second sentence (the one with the "TSN traffic streams") appears not very helpful for readers of Std 802 at all.
5) "latency" and "delay" are used as synonyms. One is enough.
6) "networking protocols and mechanisms" and "network protocols and mechanisms" are used as synonyms. One is enough.

---
TSN changes – rationale (CID 17, 3 of 5)
Background on my suggested remedy:
On item 1): IMHO it is a good idea to separate "TSN capabilities" from "protocols and mechanisms"/not use both interchangably.
On item 2): In fact, Std 802 can leave it entirely open what protocols and mechanisms are "TSN" by avoiding indications or implications to the furthest extent. This would reduce the chance for misinterpretation. There may be a unified view in a far future of what TSN is (beyond the name of an IEEE 802.1 Task Group), but I do not think that this view is available now. TSN capabilities, on the other hand, can be used as a generic term for capabilities in 802 networks like data transport with low and bounded latency, low and bounded delay variation, and low packet loss. But the term can reside as a definition left to the profiles, vendors, users, individuals, whomever by letting "TSN capabilities" being an application-specific definition.

---
TSN changes – rationale (CID 17, 4 of 5)
On item 3): I had a look into IEEE Std 802.1Q-2022 and 802.1CB-2017 on terms close to "TSN traffic stream".
- In 802.1Q: "time-sensitive streams", "guaranteed streams", "traffic streams", just "streams" (also with different capitalization), and "TSN Streams" (note that there is no match for "TSN traffic streams"). At least just "Stream" and "time-sensitve stream" have definitions in 3.259 and 3.270, respectively. The others have no definition.
- In 802.1CB: "Stream" and other more specific ones. "Stream" has a definition in clause 3.
The definitions of "Stream" in 802.1Q and 802.1CB are fortunately very similar:
- In 802.1Q: "A unidirectional flow of data (e.g., audio and/or video) from a Talker to one or more Listeners."
- In 802.1CB: "A unidirectional flow of time-sensitive data from one source to one or more destinations, and at the highest level, one Talker end system to one or more Listener end systems."
Covering both and applying some Std 802 wording ("End Station"), just "Stream" could be described as "Unidirectional flow of data from one to one or more other end stations". This could be used as an approach to translate "TSN traffic streams" to something an Std 802 reader may understand easily. I don't see a need to introduce the term "TSN traffic streams", especially because I could not find a definition in 802.1Q or 802.1CB or any other mentioning in the current 802 REVc draft.

---
TSN changes – rationale (CID 17, 4 of 4)
On item 4) [and in continuation to item 3)]: The entire sentence in the current draft basically says "protocols and mechanisms added to support one particular sort of traffic [TSN traffic streams] and other sorts of traffic". This can be collapsed to "any sort of traffic"/"different sorts of traffic". Such a statement does not appear very helpful at all. I think the original intent (and with Std 802 terms) can simply be covered by replacing the entire sentence with something simpler, deleting it (A in the suggested remedy) or incorporating it into the first sentence without diving (B in the suggested remedy).
On items 5) and 6): Trivially solved by deciding for one of both (but not both).

---
TSN update - changes
- Change
  - "Some IEEE 802 standards specify TSN capabilities to provide network protocols and mechanisms for use by applications that need data transport with low and bounded latency, low and bounded delay variation, and low packet loss. The TSN capabilities augment networking protocols and mechanisms to support both TSN traffic streams as well as other traffic. Some TSN capabilities are described in the following standards:"
- to one of the following options A or B (for discussion):
  - A: "Some IEEE 802 standards specify network protocols and mechanisms for applications that need TSN capabilities such data transport with low and bounded latency, low and bounded latency variation, and low packet loss.
  - Some of these network protocols and mechanisms are the following ones:"
  - B: "Some IEEE 802 standards specify network protocols and mechanisms for applications that need TSN capabilities such as data transport from one end station to one or more other end stations with low and bounded latency, low and bounded latency variation, and low packet loss. Some of these network protocols and mechanisms are the following ones:"
- Remarks:
  - My choices on items 5) and 6) was more or less randomly.
  - Term "end station" in option B should imply 802 network.